## Slide 1: Contouring

## Slide 2: Contour An imaginary line on the ground surface joining the points of equal elevation is known as contour.
In other words, contour is a line in which the ground surface is intersected by a level surface obtained by joining points of equal elevation. This line on the map represents a contour and is called contour line.
2
CONTOURING
2

## Slide 3
Contour Map
A map showing contour lines is known as Contour map.
A contour map gives an idea of the altitudes of the surface features as well as their relative positions in plan serves the purpose of both, a plan and a section.
3
CONTOURING
3

## Slide 4
Contouring
The process of tracing contour lines on the surface of the earth is called Contouring.
3
CONTOURING
4

## Slide 5
PURPOSE OF CONTOURING
Contour survey is carried out at the starting of any engineering project such as a road, a railway, a canal, a dam, a building etc.
For preparing contour maps in order to select the most economical or suitable site.
To locate the alignment of a canal so that it should follow a ridge line.
To mark the alignment of roads and railways so that the quantity of earthwork both in cutting and filling should be minimum.
3
CONTOURING
5

## Slide 6
PURPOSE OF CONTOURING (contd.)
For getting information about the ground whether it is flat, undulating or mountainous.
To find the capacity of a reservoir and volume of earthwork especially in a mountainous region.
To trace out the given grade of a particular route.
To locate the physical features of the ground such as a pond depression, hill, steep or small slopes.
CONTOURING
6

## Slide 7
CONTOUR INTERVAL
The constant vertical distance between two consecutive contours is called the contour interval.
HORIZONTAL EQUIVALENT
The horizontal distance between any two adjacent contours is called as horizontal equivalent.
The contour interval is constant between the consecutive contours while the horizontal equivalent is variable and depends upon the slope of the ground.
CONTOURING
7

## Slide 8
FACTORS ON WHICH CONTOUR - INTERVAL DEPENDS
The contour interval depends upon the following factors:-
i) The Nature of the
Ground country,
In flat and the
contour
uniformly sloping interval is small ,
but in broken and
mountainous region the contour interval should be large otherwise the contours will come too close to each other.
CONTOURING
8

## Slide 9: FACTORS ON WHICH CONTOUR - INTERVAL DEPENDS
ii) The Purpose and extent of the survey. Contour interval is small if the area to be surveyed is small and the maps are required to be used for the design work or for determining the quantities of earth work etc. while wider interval shall have to be kept for large areas and comparatively less important works.
CONTOURING
9

## Slide 10
COMMON VALUES OF THE CONTOUR - INTERVAL
The following are the common values of the contour interval adopted for various purposes:-
i) For large scale maps of flat country, for building sites, for detailed design work and for calculation of quantities of earth work;
0.2 to 0.5 m.
CONTOURING
10

## Slide 11
COMMON VALUES OF THE CONTOUR - INTERVAL
ii) For reservoirs and town planning schemes;
0.5 to 2m.
For location surveys. 2 to 3m.
For small scale maps of broken country and general topographic work; 3m,5m,10m,or 25m.
CONTOURING
11

## Slide 12
CHARACTERISTICS OF CONTOURS
All points in a contour line have the same elevation.
Flat ground is indicated where the contours are widely separated and steep- slope where they run close together.
A uniform slope is indicated when the contour lines are uniformly spaced and
A plane surface when they are straight, parallel and equally spaced.
CONTOURING
12