## Slide 1: LECTURE#11 PEDESTRIAN SURVEY

## Slide 2: PEDESTRIAN SURVEY
Pedestrian surveys are often conducted simultaneously with manual vehicle counts.
This particularly the case at road junctions, where the volume of pedestrians and the routes they take while crossing are important in design and construction terms.
These surveys are now increasingly carried out as planners seek to make safer environments and manage traffic flows in a proactive way

## Slide 3: Cont..
A comprehensive pedestrian count, to determine the over-all pedestrian traffic patterns for a multiplicity of purposes, should include all midblock points and intersections.
Where more restricted pedestrian counts should be undertaken as follows
  At intersections where pedestrian accidents exceed four a year
  Where pedestrian movement creates other traffic problems
  At mid-block locations
  Where heavy pedestrian volumes occur
  At areas or locations prescribed by the count's purpose.

## Slide 4: DATA COLLECTION
Before deciding on the appropriate extent and standard of pedestrian facilities, it is important to assess the potential demand.
The possible methods of obtaining such estimates are
  Manual Count
  Video Survey
  Attitude Survey .

## Slide 5: MANUAL COUNTS
Count the flow of pedestrian through a junction, across a road, or along a road section/footway manually using manual clicker and tally marking sheet.
Manual counts need to satisfy the following conditions
  The time period(s) in the day over which the counts are undertaken must coincide with the peak times of the activity of study.

## Slide 6: Cont..
  The days of the week and months of the year when observations are made must be representative of the demand. School holidays, early closing, and special events should be avoided since they can result in non-typical conditions.
  The survey locations need to be carefully selected in order to ensure that the total existing demand is observed.

## Slide 7: VIDEO SURVEY
Cameras are setup at the selected sites and video recording taken of the pedestrians during the selected observation periods.
A suitable vantage point for the camera is important. Such survey produces a permanent record of pedestrian movement and their interaction with vehicles.
In it the record of behavior pattern is also obtained which helps in analyzing the crossing difficulties.

## Slide 8: ATTITUDE SURVEY
Detailed questionnaire requires enabling complete information about pedestrian’s origins and destination points, also can gather information on what new facilities, or improvements to existing facilities, need to be provided to divert trips to walking, or increase the current pedestrian activities.

## Slide 9: COMPUTE THE PEDESTRIAN NEED
The need for pedestrian crossing facilities is calculated by PV2 where
  P= the number of pedestrians crossing in an hour
  V= the flow of vehicles in both directions in an hour

## Slide 10: Cont..
To provide an accurate picture of pedestrian traffic, the distorting effects of abnormal seasonal and temporal conditions should be avoided.
The count should not be conducted when unusually hot or cold weather keeps people off the streets.