## Slide 1: LECTURE # 08 ORIGIN AND DESTINATION SURVEY

## Slide 2: ORIGIN AND DESTINATION SURVEY
Origin is defined as place where the trip begins and destination is defined as the place where trip ends.
Transportation planner are required to predict when and where people will travel in the future so that development of the transportation network can best accommodate the public’s needs.
An essential component of the transportation planning study is the origin-destination survey.

## Slide 3: Cont..
It provides the planner with the existing travel patterns and characteristics of the population, so that future needs and desires can be realized.
Decision including development of transit routes, widening of highways, and extension of rail lines utilize results of origin-destination studies as a major criterion for action.
The purpose of study must be properly predefined for an origin destination survey to be useful.
Data needed to decide when and where to extend a rail transit line is very different from needed to decide the location of a bus terminal.

## Slide 4: Cont..
Gathering the travel characteristics of the population is complicated and labor-intensive task that demands pre-planning of all activities.
Testing of data gathering methods prior to their implementation in the field is a necessary step to, avoid wasted efforts.

## Slide 5: USES OF ORIGIN DESTINATION SURVEY
The specific uses to which O-D survey data can be put are
  To determine the volume or by passable traffic that enters a town, and thus establishes the need for a bypass
  To develop trip generation and trip distribution models in transport planning process.
  To determine the extent to which the present highway system is adequate and to plan for new facilities.
  To assess the adequacy of parking facilities and to plan for future.

## Slide 6: SURVEY METHODS
The following are the methods available for conducting an O-D survey
  Home Interview Survey
  Road-side Interview Survey
  Post-card questionnaire Survey
  Registration number plate survey

## Slide 7: Cont..
In addition to the method employed, the complexity of the origin-destination study will vary in direct proportion to the size of the area to be studied.
A study of the travel pattern for proposing a bus terminal may involve merely interviewing arriving drivers and recording data about their trips.
Useful data in this case should be easy to obtain and verify.

## Slide 8: Cont..
On the other hand, a study aimed at an update of the land use plan for a metropolitan city means dealing with a very large proportion of the travelling public.
All travel patterns into and out of the city, as well as pattern within a city, needs identification and documentation.

## Slide 9: EQUIPMENTS REQUIRED FOR SURVEY
Equipment needed includes writing instruments and clipboards, printed questionnaire, and note taking materials.
Alternately, video equipments may be used and the interviewee’s responses recorded for summary at the later date.

## Slide 10: DATA COLLECTION
Define the Scope of the Study and Identify the Target Group
  This Origin Destination study seeks to identify the travel patterns of a population.
  The investigator should first choose a target population such as those arriving at the building or business during a specific time.
  For this exercise, the target population may be all students arriving at a specific building or people approaching a restaurant during the peak hour.
  Before any work is accomplished, the investigator needs approval from the appropriate authority to interview the subjects.

## Slide 11: Cont..
Refine the Method by Which Data will be Obtained
  Although there are many different methods to obtain O-D data, it is essential to refine the selected method to suit the application at hand.
  The interviewer might verbally interview each person, but this may develop an impatient queue of people, jeopardizing data reliability.
  The exercise can be carried out in classroom buildings where people stay longer.
  The investigator can visit each classroom while classes are in session or visit each department during a specified hour and interview people or distribute the questionnaires. This method is recommended for this exercise.

## Slide 12: Cont..
Develop the Questionnaire
  Nearly all origin-destination studies try to answer the following questions regarding the travel characteristics of the sampled populations.
  The questions are as follow and may be concerned with a single trip or many trips throughout the day or week.
    When did they travel? Specify, what time of day did they travel both to and from their origins and destinations?
    Where did they travel? Where did they began and end each trip?

## Slide 13: Cont..
    How did they travel? Which mode or modes of travel were used when making each of the trips?
    Why did they travel? What was the purpose of each trip? Was the trip purpose to reach a specified destination or was there a stop on the way to another destination?
    Who was travelling? What were the characteristics of the people being studied?

## Slide 14: Cont..
Collect the data
  The data collection methods used depends on the chosen location.
  Assuming that classroom building is the location, then, the interviewer visits all classrooms during one class period and have each occupant complete the questionnaire.
  The time of day when data is collected should be considered so that a sufficient sample may be obtained.

## Slide 15: Cont..
Check the data on each questionnaire
  The completeness of each questionnaire should be checked before termination of collection efforts.
  The investigator should quickly check all parts of the questionnaire when received and make sure responses to all questions have been entered.

## Slide 16: DATA ANALYSIS
The travel information form provides for the reduction of the data.
To aid in the interpretation of the results, the investigator should consider graphical representation of the summary.
Graphical summaries similar to the pie charts and bar graphs are very effective at presenting the findings of a survey.
Origin and destination study findings are presented to decision makers to aid them in their effort to develop transportation strategies.

## Slide 17: Cont..
The final report should seek to draw as much information as possible from the data and present it in such a manner that its conclusions are easily understood.