## Slide 1: LECTURE # 09 TRIP GENERATION SURVEY

## Slide 2: TRIP GENERATION SURVEY
This survey predicts the number of trips originating or destined for a particular traffic analysis zone.
As land use changes throughout a community, the need to assess the impact of development on traffic becomes more and more important.
Traffic impact studies address the pre and post development traffic conditions.

## Slide 3: Cont..
These studies are produced to identify deficiencies in the transportation network and to develop a range of solutions to these potential problems.
The key to producing successful estimates of future traffic volumes rests with the ability to identify a reliable trip generation model.

## Slide 4: DATA COLLECTION
The essence of the data collection part of this study is the measurement of traffic volumes entering and exiting a facility during a specific time frame.
Because of this, the investigator needs minimal equipment.
Although video monitoring may be used, the study requires basic note taking material.

## Slide 5: CHOOSE A LOCATION
This study requires the investigator to look at the trip- making of a sub division, a small apartment complex, or a fast food restaurant.
The location choice to conduct the survey should be based on the number of entrance/exit points to the land use and the number of observers or the equipment available.
The number of observers needed varies in direct relationship to the number of access points

## Slide 6: RECORD TRAFFIC DATA
Vehicles entering and exiting the facility are recorded during the chosen hour.
It is imperative the counts be taken at all driveways and access point simultaneously.
The type of vehicle should be counted as it gives insight to the vehicle mix using the facility.
Observer should record entering and exiting vehicles separately.

## Slide 7: CHECK THE DATA BEFORE LEAVING THE FIELD
Standard practice dictates that all data recorded in the field is to be checked before leaving the field.
Investigators should check to see that the start and finish times are the same for all observers and that the data recorded will satisfy the analysis needs of the study.

## Slide 8: DATA ANALYSIS
Calculate the Generation Rate of the Studied Land Use
  The trip generation rate is calculated by summing the total number of vehicles entering and exiting the facility during the study hour and dividing it by the magnitude of that facility.
  For example a 200-house subdivision is examined and found to generate 221 vehicles per hour during the evening peak hour. Dividing 221 by 200, the magnitude of the facility, the trip generation rate measured was 1.05 vehicles per hour per unit.

## Slide 9: Cont..
Summarizing Findings in Report Form
  At this point, the findings should be summarized and presented in report form.