## Slide 1: lecture 5 subject plans
Master planning-II

## Slide 2: Contents of Lecture
General
Functions
Area covered by subject plans
Form and content
  Proposal maps
  Other illustrations
  Written Statement

## Slide 3: 1) General
Most local planning matters will be dealt with by district or action area plans.
These are comprehensive plans. That is, they deal with the full range of planning matters for the areas in question, and enable the authority to treat problems in relation to other planning topics.
This comprehensive approach to planning issues is clearly preferable to treating them in isolation because the various aspects of a plan are interdependent; for instance policies for shopping provision in a town cannot readily be separated from, say, those for transportation or housing densities.
Consequently, whilst it may be expedient in certain circumstances to deal with individual planning subjects, it is intended that most local planning matters should be dealt with as part of district or action area plans.

## Slide 4: 2) Functions
However, there will be some matters requiring the development of detailed local policies and proposals which cannot be conveniently fitted into the time-table of preparing district plans. This will be the case where there is an urgent need to develop a particular structure policy in advance of a comprehensive district plan or where other issues in a particular area are insufficient to justify comprehensive treatment. Circumstances such as these call for subject plans whose range of functions is that already explained all local plans.

## Slide 5: 3) Area covered by subject plans
Plans of this kind may be concerned with issues that cover parts of a wide area, such as the reclamation of a number of sites left derelict- by mineral workings, or the conservation of several areas of architectural interest; alternatively they may be concerned with some form of linear development, such as the visual or environmental treatment of a motorway corridor in the countryside or the recreational use of a river valley or a strip of coast.
The coverage of such plans may sometimes be similar to that of a district plan but their content may differ from it in being confined to a single aspect of planning, e.g. special proposals for dealing with the working of a mineral that only occurs in one part of a county.

## Slide 6: 3) Area covered by subject plans Conti….
In some circumstances, subject plans may be needed to give immediate effect to certain administrative procedures associated with the development plan. Plans of this type may be concerned with the definition of areas within which certain policies, powers or grant aid may apply.
Examples are for a green belt, for an area of outstanding natural beauty, for an area designated for town development.
Normally such proposals, together with their associated policy statements, should be included as part of a district or an action area plan.

## Slide 7: 4) Form and content
All subject plans should contain maps and diagrams accompanied by statements of policies and proposals.

## Slide 8: Proposals map
It is a requirement that each local plan should contain proposal map, indicating precise intentions to the public, property owners and developers.
This principle will apply to subject plans; thus a plan for recreation in a river valley will contain a map, or a series of inset maps, drawn on an ordnance survey base showing the policies and proposals for, e.g. camping and caravan sites, car parks, new roads, footpaths and boating facilities.
A similar form would be required for proposals to restore derelict land or to co-ordinate the landscaping of a motorway corridor. Insets to a larger scale, prepared and adopted simultaneously, should be used wherever the authority feel that the basic scale does not enable them to show their intentions in sufficient detail.

## Slide 9: Other illustrations
Subject plans can include such additional illustrative matter as may be necessary to explain them. For example, in a plan for the recreational development of a river or a canal, the authority may find it useful to produce a diagram with symbols to demonstrate how detailed proposals interrelate.
This will show how intensive public use of the water and waterside areas is to be concentrated at points accessible by road, by the establishment of, car parks, picnic sites and so on.
It will at the same time show how the greater length of the waterways is thus preserved for activities like boating, walking or riding, and the quieter pursuits, such as angling or bird watching. Again, sketches and photo-montages will help to demonstrate the authority's landscaping proposals for a. motorway corridor. Tables or graphs may be used to show, for example, the acreage of derelict land of various kinds which the plan proposes to restore.

## Slide 10: Written statement
The statement should describe the characteristics of the area. It should explain the plan's relationship to the approved structure plan and to other local plans, the policies and proposals which it embodies, and the reasoning underlying them. It should also explain why it has been necessary to produce a separate plan for a particular subject. The general considerations that should guide the presentation of a local plan's written statement have already been described they apply here too. In particular, care should be taken to quote any passages from the structure plan which bear on the subject plan's relationship with it.
For a plan of that prepared for administrative purposes, there will be a proposals map, showing the precise boundaries of the area in question. The accompanying statement should set out the policy for the area, show how it fits within the framework of the structure plan (this may not necessarily be appropriate to street authorization) and explain the relation between the subject plan and any other relevant local plans.