## Slide 1: COLOR MODELS

## Slide 2
Light and EM waves
Light is an electromagnetic wave
If its wavelength is comprised between 400 and 700 nm (visible spectrum), the wave can be detected by the human eye and is
called monochromatic light

## Slide 3
Light
Light is fundamental for color vision
Unless there is a source of light, there is nothing to see!
What do we see?
We do not see objects, but the light that has been
reflected by or transmitted through the objects

## Slide 5: Cont.
Pupil - The opening through which light enters the eye - size from 2 to 8 mm in diameter
Iris - The colored area around the pupil that controls the amount of light entering the eye.
Lens - Focuses light rays on the retina.
Retina - The lining of the back of the eye containing nerves that transfer the image to the brain.
Rods - Nerve cells that are sensitive to light and called scotopic (ldim light vision).
Cones - Nerve cells that are sensitive to a particular primary color and also called photopic (bright light vision).

## Slide 6: Figure 46-9
Cornea
Lens
Retina (photoreceptors are on the inside surface)
Sensory nerves to brain
The Cephalopod Eye
This “design” is “more intelligent” than that of mammals (humans) because it lacks the blind spot and maximizes light exposure to receptors
Notes: 6

## Slide 7: Color Fundamentals
The experiment of Sir Isaac Newton, in 1666.

## Slide 8: Preview
Motive
- Color is a powerful descriptor that often simplifies object identification and extraction from a scene.
- Human can discern thousands of color shades and intensities, compared to about only two dozen shades of gray.

## Slide 9
Due to the different absorption curves of the cones, colors are seen as variable combinations of the so-called primary colors: red, green, and blue
Their wavelengths were standardized by the CIE in 1931: red=700 nm, green=546.1 nm, and blue=435.8 nm
The primary colors can be added to produce the secondary colors of light, magenta (R+B), cyan (G+B), and yellow (R+G)
Primary and Secondary Colors

## Slide 10
Basic quantities to describe the quality of light source:
  Radiance: Total amount of energy that flows from the light source (in W).
  Luminance: A measure of the amount of energy an observer perceives from the light source (in lm)
  Brightness: A subjective descriptor that embodies the achromatic notion of intensity and is practical impossible to measure.
Color Fundamentals (con’t)c

## Slide 11: Color Fundamentals (con’t)
The characteristics generally used to distinguish one color from another are Brightness, Hue, and Saturation.
  Hue: Represents dominant color as perceive by an observer.
  Saturation: Relative purity or the amount of white light mixed with a hue
Hue and saturation taken together are called Chromaticity, and therefore, a color may be characterized by its Brightness and Chromaticity.

## Slide 12: Color Models
The purpose of a color model (also called color space or color system) is to facilitate the specification of colors in some standard, generally accept way.
RGB (red,green,blue) : monitor, video camera.
CMY(cyan,magenta,yellow),CMYK (CMY, black) model for color printing.
and HSI model,which corresponds closely with the way humans describe and interpret color.

## Slide 13: Color Fundamentals (con’t)
Tri-stimulus values: The amount of Red, Green and Blue needed to form any particular color
Denoted by: X, Y and Z
Tri-chromatic coefficient:

## Slide 14: Color Fundamentals (con’t)
Standard wavelength values for the primary colors

## Slide 15
Red-Green-Blue
• Most commonly known color space
– used (internally) in every monitor
– additive

## Slide 16: Color Fundamentals (con’t)

## Slide 17
Cyan-Magenta-Yellow
• Used internally in color printers
• Substractive
• Complementary to RGB:
•C=1-R
•M=1-G
•Y=1-B
• Also CMYK (blacK)
– mostly for printer use

## Slide 18: The RGB Color Models (con’t)

## Slide 19: The RGB Color Models (con’t)

## Slide 20: The CMY and CMYK Color Models
Cyan, Magenta and Yellow are the secondary colors of light
Most devices that deposit colored pigments on paper, such as color printers and copiers, require CMY data input.

## Slide 21
CMYK
• K is for blacK
• Save on color inks, by using black ink preferably
• K = min(C,M,Y)
• C = C-K
• M = M-K
• Y = Y-K

## Slide 22: 4.6 Color Image Processing
RGB Model

## Slide 23: The RGB Color Models

## Slide 24
The RGB Color Model
If R,G, and B are represented with 8 bits (24-bit RGB
image), the total number of colors is (28 )3=16,777,216

## Slide 25
The HSI Color Model
RGB, CMY, and the like are hardware-oriented color spaces (suited for image acquisition and display)
The HSI (Hue, Saturation, Intensity) is a perceptive color space (suited for image description and interpretation)
It allows the decoupling of chromatic signals (H+S) from the intensity signal (I)

## Slide 26: The HSI Color Models

## Slide 27
The HSI Color Models

## Slide 28
Two HSI Color Models

## Slide 29
Example
Comparison:
CMYK,
RGB,
and HSI