## Slide 1: Melt Spinning
Dr Shama Sadaf
Home Economics Department
Lahore College for Women University Lahore

## Slide 2: Spinning

## Slide 3: Spinning
Spinning is manufacturing process for creating polymer fibers. It is a specialized form of extrusion that uses a spinneret to form multiple continuous filaments.
There are three types of spinning
Wet
Dry
Melt spinning

## Slide 5: Melt spinning
Melt spinning is the most convenient and economic method for polymer fiber manufacturing at industrial scales.
Melt spun fibers can be extruded from the spinneret in different cross-sectional shapes (round, trilobal, pentagonal, octagonal, and others). Trilobal-shaped fibers reflect more light and give an attractive sparkle to textiles. Pentagonal-shaped and hollow fibers, when used in carpet, show less soil and dirt. Octagonal-shaped fibers offer glitter-free effects. Hollow fibers trap air, creating insulation and provide loft characteristics equal to, or better than, down.

## Slide 7: Process
. In melt spinning, the fiber-forming substance is melted for extrusion through the spinneret and then directly solidified by cooling
Finally, spin finish is applied before the filament bundles are wound on tube rolls.

## Slide 9: Advantages
Can be used for both staple and continuous filament
No environment pollution
High production speed (2500-3000) ft/min
Low investment cost

## Slide 10: Disadvantages
Separate drawing step (unless spin draw)
Necessary high temperature may damage some polymers