## Slide 1: Metal biotechnology
By
Dr. Zaryab Khalid
Class: Ms Botany
Semester: II
Subject: Environmental Biotechnology

## Slide 2
Mineralisation: The release of elemental carbon, nitrogen, sulphur, phosphorus and other trace elements by soil microorganisms from organic materials, is one of the important biochemical properties of microbes.
Microbes are now recognized as important geologic agents, playing a role in processes such as mineral formation, mineral degradation, sedimentation, weathering and geochemical cycling.

## Slide 3: MINERAL CYCLING
The most important vital cycles of nature include carbon, sulphur and nitrogen cycles.
Carbon and nitrogen undergo normal degradation and assimilation cycles.
Metals like Sulphur, Iron, Phosphorus, etc. undergo various extraction processes. These processes can be aided by microorganisms.

## Slide 4: Microbial Transformation
Almost all microorganisms interact with metals.
Two most important sections that are of potential economic and industrial interest are leaching metals from their ores and concentrating metals from wastes or dilute mixtures.
Firstly, metal is extracted from large quantities of low-grade ores and the second reaction would provide methods for recycling precious metals and controlling pollution caused by toxic metals.

## Slide 5
The most important microorganism important in leaching of metals is Thiobacillus ferrooxidans, a rod shaped bacterium discovered in acidic water draining coal mines.
Leaching begins with the circulation of water through large quantities of ore.
The bacteria which are naturally associated with the rocks, then cause the metals to be leached by one of the methods:
Either the bacteria directly act on the ore to extract the metal
The bacteria produces substances such as ferric iron and sulphuric acid which then extract the metal

## Slide 6
Thiobacillus ferrooxidans gets energy for growth from the oxidation of either iron or sulphur. The iron must be in the ferrous or bivalent form and is then converted by the bacterium into ferric.
The combination of Leptospirillum ferrooxidans and T. organoparpus can degrade the pyrite and chalcopyrite neither of which can be extracted by the bacterium alone.
Sulfolobus acidocaldarius and S. brierlevi oxidizes sulphur and iron for energy relying on either carbon dioxide or simple organic compounds for carbon.

## Slide 7: Leaching And Extraction
Bioleaching is the part of microbial mining.
In microbial leaching or bioleaching metals can be extracted from large quantities of low grade ores.
Bioleaching uses microorganism to alter the physical conditions in an ore so that the desired metal ions are released from compounds in form that can be easily extracted and purified.
The process is proven commercial technology for copper extraction from low grade ones and is now being applied to the extraction of other metals such as gold, cobalt and nickel.

## Slide 8: Mechanism involved in Bioleaching
Direct bioleaching: minerals which are susceptible to oxidation undergoes direct enzymatic attack by the microorganism. Certain bacteria such as Thiobacillus ferrooxidans oxidize ferrous ions to ferric ions and this process transfer the electron from iron to oxygen. Iron is extracted from the iron ore pyrite in the most soluble form. Thibacillus thiooxidans extract sulphur from the iron ore pyrite in the form of sulphates which is more soluble form.
Indirect bioleaching: bioleaching of minerals bacteria produces strong oxidizing agents which react with metals and extract them from ores. Bacteria produce oxidizing agents such as ferric ions and sulphuric acid on oxidation of soluble iron and sulphur. Acidic environment is necessary to keep ferric ions and other metals in solution.

## Slide 9: Commercial process of Bioleaching
(I) Slope leaching: In slope leaching the ore is finely ground and kept in large pile in a slope which is subjected to continuous sprinkling of aqueous solution of microorganism. The leach liquor is collected at the bottom of the ore is processed further for metal recovery.
(II) In-situ leaching: In in-situ leaching ore is subjected to bioleaching in its natural occurrence . Aqueous solution of microorganism is pumped through drilled passages within the ore. The leach liquor collected at the bottom of the ore used for metal extraction.
(III) Heap leaching: In heap leaching the ore is arranged in heap and goes through the same treatment such as in slope leaching. The aqueous solution containing microorganism works on the heap of the ore and produces leach liquor.

## Slide 10
From the solution, microbes can remove metals in three steps:
The absorption of metal ions into the surface of a microorganism
The intracellular uptake of the metals
Chemical transformation of the metals by biological agents
Microbes possess a negative electric charge owing to the presence of negatively charged groups of atoms on the cell membrane and the cell wall.
The charged group include carboxyl,phosphoryl,sulphhydryl, and hydroxyl.

## Slide 11: Advantages of Bioleaching
Extraction of metals from low grade ores
Very economic process
Employed for collecting metals from wastes and drainages
Environment friendly process
Used to extract refined and expensive metals which is not possible by other chemical processes

## Slide 12: Disadvantages
Very slow process
Dependency on several atmospheric condition decrease the efficiency of the process

## Slide 13: Future Prospects
Microbial genesis of sulphur from sulphate or of methane from organic residues in natural environment.
Immobilization or volatilization of polluting toxic elements such as arsenic and mercury
Microbial desulphurization of coal.
Microbial removal of methane from coal mines..
Use of alliphatic hydrocarbon-utilizing bacteria in detecting petroleum deposits including microbial processes for obtaining petroleum products from oil shale and tar sands.
Microbial processing and removal of pyritio impurities from pottery clay.
Immobilization of manganese and recovery of manganese and radium from tailings through the use of microorganisms using bioaccumulation.

## Slide 14: References
http://www.biotecharticles.com/Applications-Article/Bioleaching-Application-of-Biotechnology-in-Mining-Industry-850.html
http://books.google.co.in/books?id=0DKMsFPa-BgC&pg=PA89&lpg=PA89&dq=metal+biotechnology&source=bl&ots=opCBP-17nA&sig=G62p7UKwKsFfDxdEjpYZas3Fqv0&hl=en&sa=X&ei=x4NtUYbHDsTtrQfXzIC4DQ&ved=0CEQQ6AEwAg#v=onepage&q=metal%20biotechnology&f=false