## Slide 1
LECTURE # 03
BASIC COMPONENTS OF A BUILDING

## Slide 2: WHAT IS A BUILDING?
Any structure for whatsoever materials
whatsoever purpose and of constructed and every part
thereof whether used as human habitation or not and
includes chimneys,
foundation, plinth, walls, floors, plumbing and building services,
roofs, fixed
platforms, verandah, balcony, cornice or projection, part of a building or anything affixed thereto or any wall enclosing or intended to enclose any land or space and signs and outdoor display structures. tents/ shamianahs / pandals, tarpaulin shelters, etc., erected for temporary and ceremonial occasions shall
not be considered as building.

## Slide 3
PURPOSE OF A BUILDING
Buildings serve several needs of society primarily as shelter from weather, security, living space, privacy, to store belongings, and to comfortably live and work. A building as a shelter represents a physical division of the human habitat (a place of comfort and safety).

## Slide 4: TYPE OF BUILDINGS Residential house, school, hospital, or factory etc. Buildings may be load bearing masonry buildings or RCC framed structure building.
Load Bearing Masonry Building
RCC framed Structure Building

## Slide 5: BASIC COMPONENTS OF A BUILDING
There are two basic components of a building:
1. Sub-Structure or Foundation:- The lower portion of the building, which is located below the ground/soil , is called foundation. Foundation, which is in direct contact with ground in depth, transmits the loads of the super-structure to the supporting soil. Floors below ground/soil are called basement, being below ground, wherever constructed are also part of Sub-Structure. However Padstone foundation is always over ground and normally found in hill area.
2. Super Structure: The upper part/portion of the building above ground level with roof and walls including all attached apparatus, equipment, and fixtures.

## Slide 7: LOADS OF SUPER STRUCTURE
Dead loads
They are the permanent or stationary loads which are transferred to structure throughout the life span. Dead load is primarily due to self-weight of structural members like walls, roofs, permanent partition walls and other fixed components of building, fixed permanent equipment, furniture and weight of different materials etc.
2. Live loads
They are either movable or moving loads without any acceleration or impact. Live loads that do, or can, change over time. Live loads include any temporary or transient forces that act on a building or structural element. Typically, they include people, movable partitions and furniture, vehicles, and almost everything else that can be moved throughout a building.

## Slide 8: LOADS OF SUPER STRUCTURE
3. Impact Loads
They are the loads that are caused by vibration or impact or acceleration. Thus, impact load is equal to imposed load incremented by some percentage called impact factor or impact allowance depending upon the intensity of impact.
4. Environmental loads
They are the loads that are created naturally by the environment and include wind, snow, seismic, and lateral soil pressures.

## Slide 9
Foundations are divided into two categories:
Shallow foundations
Shallow foundations can be made in depths of as little as 3ft (1m) and are used for small, light buildings.
2. Deep foundations
Deep foundations can be made at depths of 60 - 200ft (20 - 65m) and are for large, heavy buildings
TYPE OF SUB-STRUCTURE/FOUNDATION

## Slide 10
1. Basic Forms 3. Spatial Forms
Doors Rooms
Windows Washrooms Residential
Lintels Kitchens
2. Structural Forms Shops/Offices
Walls Prayer area Commercial
Roofs Washrooms
Floors Cafeteria
Foundations
ARCHITECTURAL REPRESENTATION OF FORMS

## Slide 11: SUPER STRUCTURE
Generally consist of the following:
Plinth
Floors
Column
Walls
Openings (Doors/Windows/Ventilators)
Sill
Lintel
Arch
Beam
Roof
Parapet
Staircase

## Slide 12
PLINTH
Plinth is a part of the super-structure, defined as the portion of the structure between the surface of the surrounding ground and surface of the floor, immediately above the ground.
The distance between the surface of the surrounding ground and surface of the floor, immediately above the ground is called plinth height, which should be of minimum 450 mm, negotiable by steps or ramp.
The level of the floor is usually known as the plinth level. The built-up covered area measured at the floor level is known as plinth area.

## Slide 13: FLOOR
A floor is the walking surface of a room. The levels of a building are often referred to as floors although a more proper term is story or storey.
A floor is a plane area to support occupants, furniture's, and equipments.
Floors typically consist of a subfloor for support and a floor covering used to give a good walking surface.

## Slide 14: FLOOR

## Slide 15
COLUMN
A column or pillar is a vertical structural element that takes the load of beam slab etc. and transfers the load to the earth independently is called column.
Columns are frequently used to support beams or arches on which the upper parts of walls or ceilings rest.

## Slide 16: WALLS
Walls are the vertical elements and fundamental part of the superstructure of a building which enclose the space within it and which may also divide that space.
A wall is a structure that defines an area, carries a load, provides shelter and security. There are many kinds of walls: External walls, Internal walls, partition walls Defensive walls in fortification, Retaining walls, Boundary walls, Load bearing walls, Non load bearing walls, Curtain walls etc.

## Slide 17: OPENINGS
An opening is a gap, hole, breach, or aperture in the wall of a building for ingress and egress and for admission of light and air.
Types of Openings in Buildings
1. Doors – An openable barrier secured in an opening left in a wall for the purpose of ingress and egress to/ from the structure. It basically consists of two parts, namely, frame and shutter.
2. Windows – An opening especially in the wall of a building for admission of light and air.
3. Ventilators – An opening or aperture smaller than window, in the wall and above lintel level for ventilating a room or other space.

## Slide 18: OPENINGS
Door
Ventilator
Window

## Slide 19
Sill – The bottom of a door or window. This piece of framing that will rest on the bottom of the masonry or rough opening.
Lintel – A structural horizontal block that spans the space or opening between two vertical supports and serves to carry the weight of the wall above it. A horizontal supporting member, installed above an opening such as a window or a door.
Arch – An arch is normally a curved member comprising of wedge shaped building blocks holding each other with mutual pressure.

## Slide 21: BEAM
A beam is a horizontal or inclined structural element/member spanning a distance between one or more supports, and carrying vertical loads across (transverse to) its longitudinal axis that is capable of withstanding load primarily by resisting against bending.
A beam is a laterally loaded member, whose cross- sectional dimensions are small as compared to its length.

## Slide 22: BEAM

## Slide 23: ROOF/TERRACE
A roof is part of a building envelope. It is the covering on the uppermost part of a building or shelter which provides protection from weather, notably rain, snow, heat, wind and sunlight.
The characteristics of a roof are dependent upon the purpose of the building that it covers, the available roofing materials and the local traditions of construction and wider concepts of architectural design and practice and may also be governed by local or national legislation.
A roof may also provide additional usable space for roof/ terrace garden, installation of water tank, solar panel/ heater, etc. Roof can be flat roof or slope roof.

## Slide 24: ROOF/TERRACE

## Slide 25: PARAPET
Parapet is generally 10 cm thick partition wall constructed above slab to enclose the terrace open to sky.
Parapet is a barrier at the edge of a roof, terrace, balcony, walkway or other structure.

## Slide 26: STAIRCASE
A staircase/stairway is a construction designed to bridge a large vertical distance by dividing it into smaller vertical distances, called steps. Stairs may be straight, round, spiral, dog legged or may consist of two or more straight pieces connected at angles.
In buildings, stairs is a term applied to a complete flight of steps between two floors. A stair flight is a run of stairs or steps between landings.
An average flight of stairs has 10 to 12 steps but it may vary according to the building type and size.
No of risers= Total height of floor/ Height of riser
No of tread= Number of riser-1

## Slide 27: STAIRCASE

## Slide 28: THE END