## Slide 1: LECTURE # 02 SITE PLANNING PROCESS, OVERVIEW OF SITE ANALYSIS AND ITS ELEMENTS

## Slide 2: SITE PLANNING PROCESS
Site Planning is defined by Kevin Lynch as “the art of arranging structures on the land and shaping the spaces between; an art linked to architecture, engineering, landscape architecture and city planning.”
There are several notable models from which we can draw to understand the basic components of the site planning and design process.
Kevin Lynch outlines an eight-stage site planning cycle that includes:
Defining the problem
2. Programming and the analysis of site and user

## Slide 3: SITE PLANNING PROCESS
3. Schematic design and the preliminary cost estimate
4. Developed design and detailed costing
5. Contract documents
6. Bidding and contracting
7. Construction
8. Occupation and management

## Slide 4: PURPOSE OF SITE PLANNING PROCESS
To learn and practice a logical method of fitting design programs and sites harmoniously.
To understand interaction of factors including Natural factors (landscape), Socio-economic forces (planning), and technological functions (architecture & engineering) in design process.
To understand the site development process by observing natural and human factors affecting the form and appearance of the environment.
To collect information and data concerning planning or design issue.

## Slide 5: PURPOSE OF SITE PLANNING PROCESS
To classify and analyze the data.
To make recommendations for issues at hand.
To draw up guidelines for planning, architecture and landscape disciplines.

## Slide 6: SITE PLANNING PROCESS
The site design process is divided up into three phases: 1. Research
2. Analysis 3. Synthesis
Research phase The first step is defining the problem and its definition. Usually taken care of by the Architect.
Analysis phase The next step involves integrating site and use functions. Numerous site elements related to site viz. Access, Shape, surroundings etc. are being studied and analyzed.

## Slide 7: SITE PLANNING PROCESS
Synthesis phase
After analysis, a program is developed as a solution to problem at hand. This phase deals with schematic design of a site plan.
i. Chronology of steps after synthesis.
ii. Developed designs and a detailed cost estimate.
iii. Preparation of construction documents for the plan.
iv. Bidding and contracting for the project.
v. Construction
vi. Occupation and management of the site.

## Slide 8: SITE ANALYSIS
Site analysis is an inventory completed as a preparatory step to site planning, a form of urban planning which involves research, analysis, and synthesis.
It primarily deals with basic data as it relates to a specific site. The topic itself branches into the boundaries of architecture, landscape, engineering, real estate development, economics, and urban planning disciplines.
Site analysis is an element in site planning and design. Kevin A. Lynch, an urban planner developed an eight cycle step process of site design, in which the second step is site analysis.

## Slide 9: ELEMENTS OF SITE ANALYSIS
Location
The site should be related to existing roads and landmarks. Time & distances from major nodes should be recorded.
Neighborhood context
Zoning of the neighborhood is important and information could be found with municipal authorities. Numerous issues viz. architectural patterns, street lighting, condition of existing buildings must be observed. This would also include the immediate surroundings of the site. The reaction of the surrounding buildings towards the site and people moving around should be analyzed.

## Slide 10: ELEMENTS OF SITE ANALYSIS
Subsurface Features This includes analysis of the following: Geology: Geological history of the area, bedrock type & depth etc.
Hydrology: Underground water table, aquifers, springs etc.
Soil Genesis: Erosion susceptibility, moisture, bearing capacity etc.
Natural Surface Features
Most of this information will be derived from the topographic features on the site. A contour map of this magnitude can be drawn. Trees, ground cover, ground texture, and soil conditions could be directly observed. Study of vegetation should be done in relation to type, size, location, shade pattern, aesthetics, ecology etc. Slope study must entail gradient, landforms, elevations, drainage patterns etc.

## Slide 11: ELEMENTS OF SITE ANALYSIS
Manmade features
Buildings, walls, fences, patios, plazas, bus stops, shelters etc. shall be carefully recorded on maps.
Size and zoning
Land use of site, adjacent use, zoning restrictions, easement etc. Site boundaries can be located by either verifying the dimensions physically or through map records of land Development controls such as height restrictions, ground coverage, FAR parking requirements could be obtained from development plans. Zoning classifications from a zoning map to be procured from the city planning department.

## Slide 12: ELEMENTS OF SITE ANALYSIS
Circulation
Study of important nodes and linkages. The uses of streets, roads, alleys, sidewalks, and plazas are important.
Utilities
Includes power, sewage network, gas network & water supply. Availability and proximity to sources are to be examined.
Sensory
Aerial photography, sketching, visual surveys and other methods of direct observation to be employed. Sensory elements such as noise, odors, smoke, and pollutant areas must be detected and re corded.

## Slide 13: ELEMENTS OF SITE ANALYSIS
Human and cultural
Census data to be used for social factors such as population, population density, literacy, sex ratio, occupation pattern, ethnicity, cultural typology etc.
Climate
Information on precipitation, annual rain/snow, humidity, wind direction, solar intensity & orientation, average max & min temperature can be obtained through the local weather service. Rainfall, humidity & temperature over months must be recorded. Annual sun path data throughout an entire year to be noted importantly.

## Slide 14: ELEMENTS OF SITE ANALYSIS
Aesthetic Factors Visual analysis
Scenic views, flora and fauna, rock formations, water bodies, green cover valleys, rivers and mountains etc. add to value of site. Any such features if available shall need call for designing preferential locations.