## Slide 1: LECTURE # 03 SITE ANALYSIS FACTORS

## Slide 2: SITE ANALYSIS FACTORS
The analysis of the site and its environs includes various factors and features that affect it.
These factors influence final site selection and provide clues in establishing guidelines for later development.
Broadly these factors are categorized as:
1. Natural Factors
2. Biological Factors
3. Cultural/Aesthetic Factors

## Slide 3
THE NATURAL FACTORS

## Slide 4: SITE INVENTORY NATURAL FACTORS
Categories | Attributes
Soils | Types Bearing capacity Porosity Stability Erosion Fertility Acidity (pH)
Hydrology | Surface drainage Water chemistry (e.g., salinity nitrates or phosphates) Depth to seasonal water table Aquifer recharge areas Seeps and springs

## Slide 5: SITE INVENTORY NATURAL FACTORS
Categories | Attributes
Physiography | Geomorphology Topography Landforms Slope Relief and Elevation
Geology | Seismic hazards Depth to bedrock Surficial rocks
Climate | Winds (i.e., prevailing or winter Fog pockets Solar orientation Precipitation Humidity

## Slide 6
SITEPLANNINGREVIEW
1. SOILS
In site planning, it is important to establish the relationship between soil composition and land uses (other than agriculture).
Soil surveys help guide in site selection for residential, industrial, and other forms of development that involve surface and subsurface structures.
Main features to describe soil for use in site design include:
Soil composition and texture
Erosion/ Erodability

## Slide 7
SOIL SUITABILITY
Soil suitability for land uses should be studied particularly for:
Type and size of a building’s foundation system
Dwellings with basements
Drainage of ground and surface water
Absorption fields for septic tanks
Types of plant material able to grow on a site
Streets and parking
ponds or reservoir areas
Recreational facilities

## Slide 8
SOIL EROSION
Soil erosion – when rocks are broken down (weathered) into small fragments, and carried by wind, water, ice and gravity.
Four factors need to be considered in forecasting erosion rates:
Vegetation
Frequency and intensity of rainfall
Soil type
Slope size and inclination

## Slide 9
SOIL EROSION
1. Vegetation:
  Foliage intercepts raindrops
  Organic litter on the ground reduces impact of raindrops
  Roots bind together aggregate of soil particles
  Cover density, in form of ground cover or tree canopy, decreases soil loss to runoff
  2. Frequency and Intensity of Rainfall
  Intensive rainfalls produced by thunderstorms promote the highest rates of erosion.
  Accordingly, the incidence of storms plus total annual rainfall can be a reliable measure of the effectiveness of rainfall in promoting soil erosion.

## Slide 10
SOIL EROSION
3. Soil Type:
  Intermediate textures like sand will usually yield (erode) first.
  To erode clay, the velocity of the runoff should be high velocity of the runoff should be high enough to overcome cohesive forces that bind the particles together.
  Similarly, high velocities would be needed to move masses of pebbles and particles larger than those of sand.
  4. Slope Size and Inclination:
  The velocity of runoff is closely related to the slope of the ground over which it flows. Slopes that are both steep and long produce the greatest erosion because they generate runoff that is high in velocity and mass.
  Slope also influences the quantity of runoff since long slopes collect more rainfall and thus generate a larger volume of runoff.

## Slide 11: SOIL COMPOSITION & TEXTURE
Composition and texture are generally the most meaningful; from them we can make inferences about bearing capacity, internal drainage, erodibility, and slope stability.
Composition refers to the material that makes up soil including mineral particles, organic matter, water, and air.
Mineral Particles comprise 50% to 80% of the volume of the soil and form the all important skeletal structure of the soil.
Bearing capacity is a soil’s resistance to penetration from a weighted object such as a building foundation.

## Slide 12: SOIL COMPOSITION & TEXTURE
Organic Matter varies radically in soils and usually imposes a limitation to any building structure. Organic matter is important only for soil fertility, moisture absorption and retention and for landscaping.
Water content varies with particle sizes, local drainage, topography and climate. Most water occupies the spaces between particles; only in organic soils do the particles themselves actually absorb measurable amounts of water.
Air is what occupies remaining space that is not occupied by water. In layers where groundwater is formed by gravity water in the subsoil and underlying rock, there is absence of air.

## Slide 13: SOIL COMPOSITION & TEXTURE
Texture is the term used to describe the composite sizes of particles in a soil sample.
There are 12 basic terms for texture, at the center of which is Class loam,which is an intermediate mixture of 40% sand, 40% silt and 20% clay.

## Slide 14: HAZARDOUS SOIL CONDITIONS
Expansive soils usually pose a threat of hazardous soil conditions.
Impact of expansive soils may be:
  Extensive cracking of sidewalks,
  Foundation failures,
  Retaining wall failure, and so on.
The description of expansive soils recognition in the field is given below:
Under Dry Conditions
Soil is hard and almost rocklike; difficult to impossible to crush by hand.
Glazed, almost shiny surface where previously cut by shovel or scraper.
Very difficult to penetrate with pick or shovel.
Surface irregularities such as tire tracks cannot be obliterated by foot pressure.

## Slide 15: HAZARDOUS SOIL CONDITIONS
Ground surface displays cracks occurring in a more or less regular pattern. Crack width and spacing are indicative of relative expansion potential in horizontal plane.
Under Wet Conditions
Soil very sticky. Exposed soil will accumulate on shoe soles to a thickness of 2-4 inches when walked upon for a short distance.
Soil can be molded into a ball by hand. Hand molding will leave a nearly invisible powdery residue on hands after they dry.
A shovel will penetrate soil quite easily, and the cut surfaces will be smooth and tend to be shiny.
Freshly machine scraped or cut areas will tend to be smooth and shiny.
Heavy construction equipment such as bulldozers and compacting rollers will develop a thick soil coating, which may impair their function.

## Slide 16: 2. HYDROLOGY
Hydrology – the natural science that studies the Waters of the Earth, their occurrence, circulation and distribution, their chemical and physical properties, and their reaction to the living environment including their relation to all living things.
Hydrologic cycle – or the planet’s water cycle, described by the movement of water from the oceans to the atmosphere to the continents and back to the sea .
Hydrological features are of primary importance for developing the site drainage patterns.

## Slide 17: SITE DRAINAGE PATTERNS
Both the surface and the sub-surface drainage patterns on a site may greatly influence land use.
All water bodies including rivers, drainage channels, marshes, wetlands, floodplains and aquifers ,must be inventoried and analyzed for their opportunities or constraints.

## Slide 18: MARSHES, FLOODPLAINS & AQUIFERS
Marshes may be a scarce or unique feature requiring protection because of associated wildlife habitat of much value.
Floodplains must also be studied carefully for 100 years storms and some recreational uses may be located in floodplains.
Aquifers are water-bearing strata of rock, gravel, or sand in which groundwater is stored. Being very valuable resource of potable water, they should be protected from septic systems and sewer lines etc. They can both store and transmit groundwater in significant quantities
Watershed is a geographic area of land bounded by topographic features and height of land that captures precipitation, filters and stores water and drains waters to a shared destination.

## Slide 19: 3.PHYSIOGRAPHY
Physiography is the branch of Geography that deals with the description of landforms.
Landforms are irregularities on the earth’s surface which are derived from volcanic, glacial, or erosional processes.
Knowledge of their kinds and characteristics will influence the planning and design if the site is part, of or encompasses, such an irregularity.
The branch of Physiography which deals with the origin and nature of Landforms is known as Geomorphology.

## Slide 20: TOPOGRAPHY
Topography describe the shape and relief of land. It is a measurement of elevation and relief of the land.
It is measured with contours that connect points representing the same elevation.
The topography of a site may dictate the purposes for which the site may be practically used and eventually the layout of the proposed project.
The location of buildings and roads, pedestrian circulations and the arrangement of other features are all commonly affected by topography.

## Slide 21: CONTOUR LINES
Contour lines are imaginary lines in plan view that connect points of equal height above a datum or bench mark.
Contour lines spaced far apart indicate a flat surface.
Contour lines spaced evenly describe a constant slope.
Contour lines spaced closer together designate a steep rise/fall in elevation.

## Slide 22: TOPOGRAPHIC FEATURES
Following topographic features are considered for site analysis:
  Location of the structure on the site
  Location and sizes of storm and sewerage systems
  Outline of wooded areas
  Hydrographic features (river, lake, etc.)
  Location of utility lines/services
  Slope analysis
  Views
  Approach and the means of accessing the site
  Identification of unique habitats
  Neighboring land-uses
  Right of ways, easements and other encroachments
  Road elevations

## Slide 23: SLOPE ANALYSIS
Slope is the measure of steepness or the degree of inclination of a feature relative to the horizontal plane. Gradient, grade, incline and pitch are used interchangeably with slope. Slope is typically expressed as a percentage, an angle, or a ratio.
Slope analysis produces an overall pattern of slopes which helps the site planner in determining the buildable portions of the site.
These grades are calculated by measuring the distance between contours (D) at a given scale and contour interval (CI).

## Slide 24: SLOPE ANALYSIS
How to calculate Grade?
%Grade = CI/D * 100
If D = 40FT, AND CI = 2ft, the Grade will be:
%Grade = 2/40 * 100
= 5%

## Slide 25: DESIRABLE SLOPE
The slopes can be divided into following classes:
0 – 5% Generally flat Highly buildable
5 – 10% Gently rolling Moderately buildable
10 – 15% Gentle to mild slopes Moderately difficult to build
15 – 20% Mild to steep slopes Difficult to build
20% and over Harsh, steep slopes Unbuildable
Flat or gently sloping sites are preferred for industrial and commercial buildings.
Hilly sites are preferred for terraced suburban residences.
Slopes influence the alignment of modern roads according to class
of roads; the higher the class, the lower the maximum grades allowable.

## Slide 26: 4.GEOLOGY
Geology is the natural science that studies the Earth – its composition; the processes that shaped its surface; and its history.
Earth is made up of rocks (including soil, sand, silt and dust); rocks are composed of minerals; minerals are made up of atoms.
To understand the processes that have occurred in the past, it is useful to review the historical evolution of a region, like:
  Which geological processes have affected the site?,
  What is the formation and the type of bedrock below the surface of the soil?, etc.

## Slide 27: TYPES OF ROCKS
  Igneous Rocks
  Sedimentary Rocks
  Metamorphosed Rocks

## Slide 28: IGNEOUS ROCKS
Igneous rock is formed through the cooling and solidification of magma or lava.
Igneous rock may form with crystallization to form granular, crystalline rocks, or without crystallization to form natural glasses.

## Slide 29: SEDIMENTARY ROCKS
Sedimentary Rocks – when igneous rocks are exposed to surface and weathering reduces them to particles, these particles are moved by erosional process and deposited in layers into rivers and oceans .
These are formed by the deposition and subsequent cementation of that material at the Earth’s surface and within bodies of water.

## Slide 30: METAMORPHOSED ROCKS
Metamorphosed Rocks – when sedimentary rocks are pushed to deeper levels of the earth, they transform into metamorphosed rocks due to changes in pressure and temperature .
Metamorphism is a change in the structure or composition of a rock due to natural agencies, as pressure and heat. Especially when the rock becomes harder and more completely crystalline.

## Slide 31: WHAT IS A BEDROCK?
Bedrock is consolidated rock material lying at various depths below all points of the earth’s surface.
The type and depth of bedrock presents many questions of its adequacy as a base for foundations of walls, walls, or roads.
Test boring can be taken at several locations on the site and a Soil Engineer can be consulted to facilitate the interpretation of the boring results.

## Slide 32: SURFICIAL GEOLOGIC MATERIALS
Above Bedrock, surficial geologic materials extend to the surface soil.
These materials may be of porous and serve as aquifers.
Same regions are prone to movement of the earth’s surface by:
  Tactonic Movements (through crustal stress, shock by earthquakes). or
  Movement caused by Surficial Pressures (including rock falls, landslides, mudflows, and soil creep etc.)

## Slide 33: 5.CLIMATE
Climate is one of the very important factors and sites should be analyzed and planned comprehensively keeping in view the overall climate.
Climates can be divided in five general types:
  Tropical
  Dry/ Arid
  Temperature
  Cold
  Polar

## Slide 34: ROLE OF SITE PLANNER
Site planner should investigate all the climatic factors and especially:
  The solar orientation for the buildings,
  The best facing slopes, and
  The part of the slope that makes use of airflow for warmth in cool climates or for breezes in temperature or hot climates.

## Slide 35: MAIN CLIMATIC FEATURES
Important climatic considerations are:
  Humidity,
  Temperature,
  Precipitation and Wind direction,
  Solar orientation, and
  Fog.

## Slide 36: HUMIDITY
Humidity is the amount of water vapor in the air.
Relative humidity is the amount of water vapor the air is holding, expressed as a percentage of the amount the air can hold at a particular temperature.
If at a particular temperature, air is saturated with water vapor, it has 100% relative humidity.
Warmer temperatures are capable of holding more water vapor before saturation is reached.

## Slide 37: TEMPERATURE
Temperature is another very important factor considering the energy consumption during hot and cold weather.
For each 300ft. Rise in height from the earth’s surface, temperature decreases approximately 1° F in the summer.
Oceans and large lakes retain their heat in winter months as land masses cool and they are cool in summer as land masses warm, thus moderate the temperature.
The more perpendicular a slope is to the rays of the sun, the warmer the surface temperature.

## Slide 38: PRECIPITATION AND WIND DIRECTION
The movement of water particles into air is precipitation and it along with temperature are the major factors affecting vegetation.
Wind direction, also plays an essential role in site selection.
In cool and temperate climates, vegetation may be used to block winter winds.
Cool air flows towards low points or valleys at night, but higher side slopes remain warmer.