## Slide 1: LECTURE # 06 LOCATION OF ACTIVITIES RESIDENTIAL ACTIVITY & COMMERCIAL ACTIVITY

## Slide 2: Location of Activities
Once the site and its purpose have been analyzed, site planning begins with a land use diagram.
The site plan includes two things:
    Physical objects, and
    Human activities
Site Plan refers to activity locations, thus it shows the general functional arrangement of activities.
The classes of different uses in any project must be set with care and divided as finely as will not make their organization too complex.

## Slide 3: Location of Activities
Activities might not function well unless they are located in conjunction with other bonded activities.
When the landuse classes have been set, then all the linkages between them must be analyzed for proper functioning.

## Slide 4: 1. Residential Activity
The primary objective in residential activity site planning is to provide a site that is a desirable place to live for the intended users.
Characteristics associated with the end users of the activity will affect the planning and designing of the site, still there are some commonalities found in quality residential development for all user classes.

## Slide 5: Quality Residential Development
Thomas Hylton (1995) listed 10 attributes of quality residential development:
      A sense of place
      Human scale
      Self-contained neighborhoods
      Diversity
      Transit-friendly design
      Trees
      Alleys & parking lots
      Humane architecture
      Outdoor rooms
      Maintenance and safety

## Slide 6: Classes/ Types of Residential Activity
Different classes for residential activity are:
Based on housing type:
    Detached housing,
    Semi-detached housing,
    Row housing, and
    Flats/ apartments
Based on density:
    High density housing,
    Medium density housing, and
    Low density housing

## Slide 7: Potential Residential Locations
The identification of potential residential sites throughout the topography of the whole site is very important.
A good residential location is a combination of its surroundings, access and amenities.
Proximity to open space features also play an important role in locating the residential sites.

## Slide 8: Homeowner Preference for Proximity to Open-Space Features
Open-Space Feature | Mean Score
Adjacent to wet pond | 4.44
Adjacent to natural area | 4.27
On a cul-de-sac | 3.83
Adjacent to golf course | 3.67
Adjacent to public park | 3.10
Adjacent to dry pond | 2.05
Source: Site Planning and Design Handbook, Pg.305

## Slide 9: Building Residential Sites
In the designing of residential activity, the relation of public and private areas is important to the interaction of residents and the degree of privacy desired.
Residential areas can be categorized as:
    Public areas
    Semi-public areas
    Private areas
    Transition areas

## Slide 10: Public Areas
Public areas are used by all residents of a residential development.
They include:
    Parking areas,
    Roads,
    Walkways,
    Parks,
    Playgrounds,
    Waste collection facilities, etc.

## Slide 11: Semi Public Areas
Semi-public areas are the community or other recreational facilities available only to residents or visitors of a particular residential development or apartment complex.
They include:
    Community swimming pools,
    Entry areas,
    Lobbies,
    Corridors, etc.

## Slide 12: Private Areas
Private areas are either enclosed or screened.
Enclosed areas include the inner of residential units.
Screened areas include the outer garden or lawn where people can outdoors, sunbathe, or entertain friends.
They can also be screened balcony areas and porches.

## Slide 13: Transition Areas
These are areas between public and semi-public spaces and between semi-public and private spaces.
The important concern is to analyze whether a clear sequence of transition from public to semi-public to private spaces exists?
These areas, also known as linkages, provide variety and interest in the landscape.

## Slide 14: 2. Commercial Activity
The location of commercial activity depends on market analysis and accessibility.
Important considerations will be:
    The distribution of population,
    Its buying power,
    The location of competing centers,
    The means of access to the site and their capacity,
    Time distances involved, and
    The customary routes of travel for other purposes.

## Slide 15: Location of Commercial Activities
Commercial activity should typically be located along major roads, and it is desirable to have more than one access.
Important consideration is that the position at major intersection or along a road already flowing full or having through traffic, may discourage customers.
Good visibility from the main roads is desirable.
The areas to be developed should be level and fairly compact in shape.
The site should not be surrounded with ugly, competing, or of nuisance character development.

## Slide 16: Classes/ Types of Commercial Activity
Commercial activity can be:
    Neighborhood Centers – may serve 10,000 people.
    Community Centers – may serving capacity is from 10,000 to 100,000 people.
    Regional Centers – may serve more than 100,000 people.

## Slide 17: Other Required Attributes
Other required attributes towards commercial area development are:
    Enough parking spaces with proper screening,
    Short walking distances,
    Pleasant pedestrian environment,
    Sufficient entrance areas,
    Clustering of similar type of activities,
    Advance services,
    Clarity of form,
    Efficient circulation, and
    Proper designed bus stop/ bay for larger centers, etc.