## Slide 1: LECTURE # 07 LOCATION OF ACTIVITIES INDUSTRIAL ACTIVITY & INSTITUTIONAL ACTIVITY

## Slide 2: 1. Industrial Activity
Industrial activity requires substantial areas of moderately flat and inexpensive land.
The land should lie in such a position that the traffic it will generate, will not disturb residential areas.
Site plan of industrial are should facilitate the future growth/development.

## Slide 3: Area Requirement Attributes
Larger industrial estates/districts range from 150 to 500 acres in size, while on expensive lands, size may be reduced within a range from 50 to 150 acres.
Floor area ratio for industrial area development on inexpensive land may be kept from 0.1 to 0.3 with a density of 10 to 30 workers per acre.
FAR may be increased up to 0.5 with a density of 60 workers per acre in situations where there is greater pressure on land i.e. expensive land.

## Slide 4: Accessibility
Good access is the primary objective for industrial areas, particularly for goods and worker’s transportation.
It is desirable for larger industrial estates to be connected not only with highways, but with rail network also.
Public transport routes should also be designed for industrial areas.

## Slide 5: Circulation
Industrial areas are typically laid out with a grid iron of roads for easy circulation of heavy traffic.
It is desirable for heavy industrial activity to be placed at one level, while light industry enables the small bulk of raw materials and products to be placed at upper floors.
Desirable right of ways for railroads is 40 ft while it is 100 ft for other roads.

## Slide 6: Circulation
It is also desirable to separate traffic circulation with the general circulation as much as possible.
The problem of exit congestion at shift time will be serious, and the capacity of intersections and exits must be checked.
A network of secondary roads which permits quick dispersion of the concentrated load is preferable to a single high capacity highway.
Segregation of shift hours may also help.

## Slide 7: Parking
Extensive parking spaces are required.
Normally, work in industries progress in different shifts, so it happens that one shift arrives before another leaves, so double parking spaces are required at one time.
Parking spaces may be dispersed and closely related to the actual point of work.
Maximum desirable distance from vehicle to plant is 1,000 ft.

## Slide 8: Visibility
Clear visual identity for industrial district/estate exits and entrances is important, and can be accomplished through large scale landscape or vertical features.
Although, each building is competently designed, still these units have negative visual impacts.
The view from the bordering roads is important, hence factories should not be allowed to back onto such roads.

## Slide 9: Utility and Other Desirable Facilities
Electricity, gas, water and sewage disposal of high capacity is also required.
To bring liveliness in these areas, places of recreation and other items such as restaurants etc. may also be provided.
Other required facilities are banks, post offices, fire stations, medical clinics, small shopping and service center and bus or transit terminals.

## Slide 10: 2. Institutional Activity
Institutional land uses are extremely diverse in nature e.g. colleges, universities, hospitals, governmental units and cultural centers.
Such activities are normally long-lived with this element of continuity, an environment of great richness and strong character can be achieved.
Institutional structures are highly individual, thus requires particular services and situation, and must be studied by itself.
Larger institutions are much like a city in miniature.
Because of extreme diversity of the users, a few comments as generalized guidelines can be made.

## Slide 11: Some Generalized Guidelines
The most important consideration is the efficient linkages between different set of activities.
Walking time should not exceed certain limits, otherwise, the institution may begin to operate in sectors, rather than as a unit.
Other important considerations are total size, density, circulation, grain and accessibility form the outer world.