## Slide 1
LECTURE # 04
URBAN DESIGN PRINCIPLES/ELEMENTS

## Slide 2: URBAN DESIGN PRINCIPLES/ELEMENTS

## Slide 3
Urban structure | The overall framework of a region, town or precinct, showing relationships between zones of built forms, land forms, natural environments, activities and open spaces. It encompasses broader systems including transport and infrastructure networks.
Urban grain | The balance of open space to built form, and the nature and extent of subdividing an area into smaller parcels or blocks. For example a ‘fine urban grain’ might constitute a network of small or detailed streetscapes. It takes into consideration the hierarchy of street types, the physical linkages and movement between locations, and modes of transport.
Density + mix | The intensity of development and the range of different uses (such as residential, commercial, institutional or recreational uses).
Height + massing | The scale of buildings in relation to height and floor area, and how they relate to surrounding land forms, buildings and streets. It also incorporates the building envelope, site coverage and solar orientation. Height and massing create the sense of openness or enclosure, and affect the amenity of streets, spaces and other buildings.
Streetscape + landscape | The design of public spaces such as streets, open spaces and pathways, and includes landscaping, microclimate, shading and planting.

## Slide 4
Facade + interface | The relationship of buildings to the site, street and neighbouring buildings (alignment, setbacks, boundary treatment) and the architectural expression of their facades (projections, openings, patterns and materials).
Details + materials | The close-up appearance of objects and surfaces and the selection of materials in terms of detail, craftsmanship, texture, colour, durability, sustainability and treatment. It includes public and private structures and space, street furniture, paving, lighting and signage. It contributes to human comfort, safety and enjoyment of the public or private domain.
Public Realm | Much of urban design is concerned with the design and management of publicly used space (also referred to as the public realm or public domain) and the way this is experienced and used. The public realm includes the natural and built environment used by the general public on a day-to-day basis such as streets, plazas, parks, and public infrastructure. Some aspects of privately owned space such as the bulk and scale of buildings, courtyards and entries that are traversed by the public or gardens that are visible from the public realm, can also contribute to the overall result. At times, there is a blurring of public and private realms, particularly where privately owned space is publicly used.

## Slide 5
Topography, landscape | The natural environment includes the topography of landforms, water and environment
Social + economic fabric | The non-physical aspects of the urban form include social factors (culture, participation, health and well-being) as well as the productive capacity and economic productivity of a community. It incorporates aspects such as demographics and life stages, social interaction and support networks.

## Slide 6: ELEMENTS OF URBAN DESIGN
Signage
Lighting
Parking
Service areas
Fencing
Building Materials
Building Articulation

## Slide 7: Signage
When choosing a sign one must consider several aspects such as the desired size, type and placement of a sign. The first question that you should ask is how much space do you have to construct a sign? If you have limited space you should consider constructing a wall, canopy or awning sign. If the site is large enough to construct a monument sign you should do so in addition to wall, canopy or awning signs.
Architecturally integrate all signs with their surroundings in terms of size, shape, color, texture and lighting so that they are complementary to the overall design of the building and are not in visual competition with other signs in the area.

## Slide 8
Environmental graphic communications whose functions include direction, identification, information or orientation, regulation, warning, or restriction.
Symbols or words whose function is to provide direction, identification, information or orientation, regulation, warning, or restriction.
Signage include direction signs, signs of locality, street names and numbering, information signs, etc.
All types of signs should be visible, clear, simple, easy to read and understand, and properly lit at night.
In general, signs should not be placed behind glass because of possible reflection.
Signage placed on the pedestrian path of travel are considered obstructions; thus, they should be detectable.
All directional and informational signage must be uniform to provide a unique character in a particular precinct.
Signs must not block the view of or the view from adjacent buildings and must not be excessive in size and number.
Traffic signs and signals must be carefully placed in a way that they do not cause or contribute to chaos and clutter.

## Slide 10: Lighting
Lighting is an important element in Urban Design. When considering a lighting design, one must take into account the type of light needed for the specific purpose of the site. Is the light designed to enhance security to the property, provide ambiance, aid drivers by increasing visibility on roadways, or used simply to illuminate a sign? It is important to determine the proper lighting for the structure or site.

## Slide 12: Parking
Parking is an essential element in regards to urban design and traffic circulation. A parking plan should be developed for each site prior to development. The type and number of parking spaces should reflect the desired uses of each site.

## Slide 18: Materials Used
Façade treatment and the architectural detail of buildings contribute significantly to the way a building ‘reads’ from the street and to the character and continuity of the streetscape. The composition and detailing of the building façade also has an impact on the apparent bulk and scale of a building. It is important when considering the design of new development that the predominant patterns, compositions and articulation of façades reinforces the character and continuity of the streetscape. This does not mean replicating the appearance of buildings.
Contemporary design solutions based on sound design principles, which reinforce and make reference to the underlying elements that create the character of the area are encouraged Design consideration is to be given to the underlying building materials that contribute to the character of a building. Such things include roof shape, pitch and overhangs; entry porches, verandas, balconies, terraces, fixtures, & furniture.