## Slide 1
Lecture # 06
Urban Design Characteristics

## Slide 2: Urban Design Characteristics
The urban design characteristics of a neighborhood are composed of the various components in the buildings and streets of the area:
    - Building bulk, use, and type.
    - Building arrangement.
    - Block form and street pattern.
    - Streetscape elements.
    - Street hierarchy.
    - Natural features.

## Slide 3: Urban Design Characteristics
Building bulk, use, and type:
Buildings in a neighborhood are usually described by their bulk, use, and type (such as "narrow, high-rise commercial buildings").
The concept of bulk is created by the size of a building and the way it is massed on its site. Height, length, and width define a building's size; volume, shape, setbacks, lot coverage, and density define its mass.
In describing a building, noting its general use (manufacturing vs. residential, for example) conveys a sense of its appearance, and thus adds to the understanding of its visual and urban design character.

## Slide 4: Urban Design Characteristics
Building arrangement:
This term refers to the way that buildings are placed on zoning
lots and blocks. They may be attached to one another, as are row
houses, or detached and separated by driveways or open uses.
Building arrangements can be quite varied or organized in a
site plan (such as an institutional campus or a large residential
development).

## Slide 5: Urban Design Characteristics
Block form and street pattern:
The shape and arrangement of blocks and surrounding streets may be regular composed of rectangular blocks, formed by streets intersecting at right angles.
The pattern may be defined by irregularly shaped blocks, curving streets, or cul-de-sacs. The block form and street pattern contribute to urban design because they define the flow of activity in an area, set street views, and create the basic format on which building arrangements can be organized.

## Slide 6: Urban Design Characteristics
Streetscape Elements:
Most areas include distinctive physical features that make up a streetscape, such as front yards, street trees, curb cuts, street walls (i.e., the "wall" created by the continuous front facade of buildings along the street), street furniture (i.e., items permanently installed on the street, such as street lights, fire hydrants, or newsstands), building entrances, curb cuts, parking lots, fences, stoops, parking ribbons (i.e., the row of parked cars along a street), service entrances visible from the street, etc.

## Slide 7: Urban Design Characteristics
Street Hierarchy:
Another descriptor for an area's streets is their classification, which convey a sense of width, circulation, and activity. These include expressways, which have limited vehicle access and no at-grade pedestrian crossings, arterials, which have limited, at grade crossings, collector/distributor streets and local streets (which include cul-de-sacs).

## Slide 8: Urban Design Characteristics
Natural Features:
Natural features include vegetation and geologic, topographic, and aquatic features. Rock outcroppings, steep slopes or varied ground elevation, beaches, or wetlands can help define the overall visual character of an area.