## Slide 1: Miscellaneous Building Materials

## Slide 2: Mud
Mud is a mixture of water and any combination of soil, silt, and clay, and usually forms after rainfall or near water sources.
Ancient mud deposits harden over geological time to form sedimentary rock such as shale or mudstone.

## Slide 3: Mud
Adhesive
In the construction industry, mud is a semi-fluid material that can be used to coat, seal, or adhere materials. Depending on the composition of the mud, it can be referred by many different names, including slurry, mortar and concrete.
Material
Mud, cob, adobe, clay, and many other names are historically used synonymously to mean a mixture of subsoil and water possibly with the addition of stones, gravel, straw, lime, and/or bitumen. This material was used a variety of ways to build walls, roofs and floors.

## Slide 4: Cement concrete
Cement concrete is a mixture of cement, sand, pebbles or crushed rock and water. When placed in the skeleton of forms and allowed to cure, becomes hard like a stone. Cement concrete is important building material because of the following reasons.
It can be moulded into any size and shape of durable structural member.
It is possible to control the properties of cement concrete.
It is possible to mechanise completely its preparation and placing processes.
It possesses adequate plasticity for mechanical working.

## Slide 5: Cement concrete
The cement concrete has the following properties
It has high compressive strength
It is free from corrosion
It hardens with age and continues for a long time after concrete has attained sufficient strength
It is proved to be economical than steel
It binds rapidly with steel and it is weak in tension, steel reinforcement is placed in cement concrete at suitable places to take up tensile concrete or simply R.C.C.
It forms a hard surface, capable of resisting abrasion stresses. This is called reinforced cement.

## Slide 6: Metals
 Metals are
employed for various engineering
purposes such as structural members, roofing materials, damp proof courses, pipes, tanks, doors, windows etc out of all the metals, iron is the most popular metal and it has been used in construction activity since pre-historic times.
 For the purpose of study metals are grouped in the following two categories

## Slide 7: Metals
Ferrous metals: Ferrous metals contain iron as their main constituent
Ex: Cast iron, wrought iron, steel
Non-ferrous metal: Non ferrous metal does not contain iron as their main constituent
Ex: Aluminium, copper etc

## Slide 8: Pig Iron
The crude impure iron, which is extracted from iron ores, is known as pig-iron and it forms the basic material for the manufacture of cast-iron, wrought iron and steel.

## Slide 9: Cast iron
Cast iron is manufactured by re-melting pig iron with coke and limestone. This re-melting is done in a furnace known as cupola furnace, which is more or less same as blast furnace. Its shape is cylindrical.

## Slide 10: RCC
RCC (Reinforced Cement Concrete) is the combination of using steel and concrete instead of using only concrete to offset some limitations.
Concrete is weak in tensile stress with compared to its compressive stress. To offset this limitation, steel reinforcement is used in the concrete at the place where the section is subjected to tensile stress.
Steel is very strong in tensile stress. The reinforcement is usually round in shape with approximate surface deformation is placed in the form in advance of the concrete.

## Slide 11
 When the reinforcement is surrounded by the hardened concrete mass, it form an integral part of the member. The resultant combination of two materials are known as reinforced concrete. In this case the cross-sectional area of the beam or other flexural member is greatly reduced.

## Slide 12
Concrete consists of a cement and stone aggregate mixture that forms a rigid structure with the addition of water. When steel that has a high tensile strength is embedded in concrete, the composite material withstands compression, bending, and tensile stresses. Such a material can be used for making any size and shape, for utilization in the construction.
The main quality of reinforced concrete is similarity of its coefficient of thermal expansion with that of steel, due to which the internal stresses initiated due to variation in thermal expansion or contraction are eliminated.
Secondly, on the hardening of the cement paste inside the concrete, it corresponds to the surface features of the steel, allowing the stresses to be efficiently transmitted between the two materials. The cohesive characteristics between the steel and concrete are enhanced by the roughening of steel bars.

## Slide 13: DANGEROUS BUILDINGS

## Slide 14: Building/structure
'Any permanent or temporary building and any other permanent or temporary structure, or erection, of whatever kind or nature.'

## Slide 15: Dangerous Building
The term 'dangerous structure' covers buildings or parts of buildings. It also includes garden walls, fences or hoardings, in fact any built structure that because of its condition could endanger the public.
Buildings, like people, suffer from an ageing process, which can result in the structure becoming weaker. Buildings or structures can become dangerous as a result of poor maintenance, fire, storm, vehicle impact or explosion.
Structure causing danger; likely to harm or hurt; a perilous building

## Slide 16: Causes of Decay in Building
The inappropriate use of a component or material
External causes of decay in buildings
Gravity causes buildings to collapse
Climatic conditions has severe effects on buildings
Fire burns effects the buildings
Vibration of the transportation vehicles effects the buildings
Man-made causes like alteration in the buildings etc. paly significant role in the becoming the buildings dangerous

## Slide 17: Causes of Decay in Building
Effects of water proofing and seepage can’t be neglected
The use of material adjacent to or in combination with another that adversely affects it
A lack of knowledge by the designer regarding the potential deterioration of a material
The building being subject to forces or agents not considered in the design
Inaccurate information from manufacturers
Poor manufacturing quality
Poor workmanship
The failure to carry out necessary routine maintenance at the appropriate time

## Slide 18: Issues related to Dangerous Buildings in Pakistan
Social Attitude
High Construction Cost
High ratio of poor/low income group
Lack of information
Lack of documentation
Incompetent staff
Lack of responsibility by public
Lack of responsibility by regulatory body
Lack of Projects/programs issued by govt. regarding public buildings
Lack of Public Participation
Flood prone areas in Punjab especially on agriculture lands
Lack of Provision in Developmental Plans

## Slide 19: Phase 1
-Proper formation of
association/authority
for
dangerous buildings
Phase 2
controlling
-Formation of proper
legislation
-Preparation
Phase 3
of -Proper
Building Code for documentation of
Dangerous Buildings dangerous
with attributes
-(Area, Condition, Ownership)
-Digital formation
Phase 4
buildings -Zoning of areas with
respect to intensity of
Location, (env.
residential/other)
database -Public
awareness dangerous
regarding buildings
-Special scheme from banks
loans’ public
for
restructuring
of
dangerous buildings
Phase 5
Height, dangerous buildings Project
Initiation by
sensitive/ Government
through
techniques like:
Land Rehabilitation
Land Readjustment
Land Renewal(
Conservation /
Preservation)

## Slide 20: Energy Efficiency and Retrofitting

## Slide 21: Energy efficiency
“Energy efficiency is "using less energy to provide the same service".
For example, insulating a home allows a building to use less heating and cooling energy to achieve and maintain a comfortable temperature.
Installing fluorescent lights or natural skylights reduces the amount of energy required to attain the same level of illumination compared to using traditional incandescent light bulbs.

## Slide 22: Energy efficiency
Compact fluorescent lights use two-thirds less energy and may last 6 to 10 times longer than incandescent lights.
Improvements in energy efficiency are most often achieved by adopting a more efficient technology or production process.

## Slide 23: Energy efficiency is not energy conservation
Energy conservation is reducing or going without a service to save energy.
 For example: Turning off a light is energy conservation. Replacing an incandescent lamp with a compact fluorescent lamp (which uses much less energy to produce the same amount of light) is energy efficiency.

## Slide 24
The concept of sustainable development can be traced to the energy (especially fossil oil) crisis and the environment pollution concern in the 1970s.
It often emphasizes taking advantage of renewable resources, e.g., using sunlight through passive solar, active solar, and photovoltaic techniques and using plants and trees through green roofs, rain gardens, and for reduction of rainwater run-off.
Many other techniques, such as using packed gravel or permeable concrete instead of conventional concrete or asphalt to enhance replenishment of ground water, are used as well.

## Slide 25: What are energy efficient buildings?
“Energy
efficient buildings
(also known as green
buildings or sustainable
buildings) refers to a
structure and using process that is environmentally
responsible and resource-efficient
throughout a
building's life-cycle: from siting to design, construction, operation, maintenance, renovation, and demolition”.

## Slide 26: Energy efficient buildings
The common objective is that green buildings are designed to reduce the overall impact of the built environment on human health and the natural environment by:
Efficiently using energy, water, and other resources
Protecting occupant health and improving employee productivity
Reducing waste, pollution and environmental
degradation

## Slide 27: NEED OF ENERGY EFFICIENT BUILDINGS
There are several reasons which stimulate the desire and need to have energy efficient buildings:
To achieve a sustainable economy in terms of GDP growth
Green building result in reduction of operating costs by 25- 30%
Energy efficient commercial buildings are a great Investment
Energy efficient buildings lower the stress on utility services
Improvement in employees attendance and productivity

## Slide 28: NEED OF ENERGY EFFICIENT BUILDINGS
For the development of local talent pool designers and builders experienced with green projects able to accommodate the growing market demand for sustainable development.
Improvement of people’s living standards
Protection of environment for future generations
To develop a trend of sustainable energy use in commercial and residential buildings

## Slide 29: Retrofitting
Retrofitting refers to the addition of new technology or features to older systems.
Home energy retrofit, the improving of existing buildings with energy efficiency equipment
Seismic retrofit, the process of strengthening older buildings in order to make them earthquake resistant

## Slide 30: RETRO-FITTING TECHNIQUES FOR EXISTING BUILDINGS
Reduce electricity consumption
Simple means can help you to reduce the impact of electricity consumption, like making sure lights are turned off at night, lowering temperature in heated rooms and raising it slightly where it's cool.
Proper organization of functional space
Make sure you are using your premises to its full potential.
Efficient lighting
Use energy efficiency bulbs and daylight controllers which will switch on only when natural light is insufficient. Reduce lighting level by replacing tubes with energy saving light bulbs.

## Slide 31: RETRO-FITTING TECHNIQUES FOR EXISTING BUILDINGS
Get IT (information technology) right
Considering that IT equipment consumes a lot of energy, putting computers in their most efficient setting and switching them off when not in use will allow you to save money.
Consider generating your own energy
Improve glazing and insulation
Control water use

## Slide 32: BENEFITS OF ENERGY EFFICIENT RETROFITTING
Increase in rents on account of better quality facilities and services being offered to occupiers.
Increase in energy efficiency with reduction in the carbon footprint.
Reduction in operational costs as energy efficient practices are implemented
Expected profitable fiscal returns
Provide a competitive edge over other buildings in the same micro-market
Improving the energy efficiency of a building can result in gains in workers’ productivity

## Slide 33: Seismic Retrofitting
It is the modification of existing structures to make them more resistant to seismic activity, ground motion, or soil failure due to earthquakes.
The retrofit techniques are also applicable for other natural hazards such as tropical cyclones, tornadoes, and severe winds from thunderstorms

## Slide 34: When is Seismic Retrofitting Needed ?
The two circumstances are:-
Earthquake damaged buildings, and
Earthquake-vulnerable buildings(with no exposure to severe earthquakes)

## Slide 35
 Public safety only
The goal is to protect human life, ensuring that the structure will not collapse upon its occupants or passersby, and that the structure can be safely exited.
Structure survivability: The goal is that the structure, while remaining safe for exit, may require extensive repair (but not replacement) before it is generally useful or considered safe for occupation.

## Slide 36
 Structure functionality: Primary structure undamaged and the structure is undiminished in utility for its primary application.
of retrofit is high cultural
 Structure unaffected: This level preferred for historic structures of significance.

## Slide 37: Retrofitting Techniques