## REP Prefix

REP repeats the following string instruction CX times. The use of CX is implied with the REP prefix. The decrement in CX doesn’t affect any flags and the jump is also independent of the flags, just like JCXZ.

## REPE and REPNE Prefixes

REPE or REPZ repeat the following string instruction while the zero flag is set and REPNE or REPNZ repeat the following instruction while the zero flag is not set. REPE or REPNE are used with the SCAS or CMPS instructions. The other string instructions have nothing to do with the condition since they are performing no comparison. Also the initial state of flags before the string instruction does not affect the operation. The most complex operation of the string instruction is with these prefixes.

STOS Example – Clearing the Screen

We take the example of clearing the screen and observe that how simple and fast this operation is with the string instructions. Even if there are three instructions in a loop they have to be fetched and decoded with every iteration and the time of three instructions is multiplied by the number of iterations of the loop. In the case of string instructions, many operations are short circuited. The instruction is fetched and decoded once and only the execution is repeated CX times. That is why string instructions are so efficient in their operation. The program to clear the screen places 0720 on the 2000 words on the screen.

|  | Example 7.1 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 | ; clear screen using string instructions [org 0x0100] jmp start ; subroutine to clear the screen clrscr: push es push ax push cx push di mov ax, 0xb800 mov es, ax ; point es to video base xor di, di ; point di to top left column mov ax, 0x0720 ; space char in normal attribute mov cx, 2000 ; number of screen locations cld ; auto increment mode rep stosw ; clear the whole screen pop di pop cx pop ax pop es ret start: call clrscr ; call clrscr subroutine mov ax, 0x4c00 ; terminate program int 0x21 |
| 013 | A space efficient way to zero a 16bit register is to XOR it with itself. Remember that exclusive or results in a zero whenever the bits at the source and at the destination are same. This instruction takes just two bytes compared to “mov di, 0” which would take three. This is a standard way to zero a 16bit register. |

Inside the debugger the operation of the string instruction can be monitored. The trace into command can be used to monitor every repetition of the string instruction. However screen will not be cleared inside the debugger as the debugger overwrites its display on the screen. CX decrements with every iteration, DI increments by 2. The first access is made at B800:0000 and the second at B800:0002 and so on. A complex and inefficient loop is replaced with a fast and simple instruction that does the same operation many times faster.

LODS Example – String Printing

The use of LODS with the REP prefix is not meaningful as only the last value loaded will remain in the register. It is normally used in a loop paired with a STOS instruction to do some block processing. We use LODS to pick the data, do the processing, and then use STOS to put it back or at some other place. For example in string printing, we will use LODS to read a character of the string, attach the attribute byte to it, and use STOS to write it on the video memory.

The following example will print the string using string instructions.

|  | Example 7.2 |
| --- | --- |
| 001 002 003 004 005 006 007 008-027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 | ; hello world printing using string instructions [org 0x0100] jmp start message: db 'hello world' ; string to be printed length: dw 11 ; length of string ;;;;; COPY LINES 005-024 FROM EXAMPLE 7.1 (clrscr) ;;;;; ; subroutine to print a string ; takes the x position, y position, attribute, address of string and ; its length as parameters printstr: push bp mov bp, sp push es push ax push cx push si push di mov ax, 0xb800 mov es, ax ; point es to video base mov al, 80 ; load al with columns per row mul byte [bp+10] ; multiply with y position add ax, [bp+12] ; add x position shl ax, 1 ; turn into byte offset mov di,ax ; point di to required location mov si, [bp+6] ; point si to string mov cx, [bp+4] ; load length of string in cx mov ah, [bp+8] ; load attribute in ah cld ; auto increment mode nextchar: lodsb ; load next char in al stosw ; print char/attribute pair loop nextchar ; repeat for the whole string pop di pop si pop cx pop ax pop es pop bp ret 10 start: call clrscr ; call the clrscr subroutine mov ax, 30 push ax ; push x position mov ax, 20 push ax ; push y position mov ax, 1 ; blue on black attribute push ax ; push attribute mov ax, message push ax ; push address of message push word [length] ; push message length call printstr ; call the printstr subroutine mov ax, 0x4c00 ; terminate program int 0x21 |
| 051 | Both operations are in auto increment mode. |
| 052-053 | DS is automatically initialized to our segment. ES points to video memory. SI points to the address of our string. DI points to the screen location. AH holds the attribute. Whenever we read a character from the string in AL, the attribute byte is implicitly attached and the pair is present in AX. The same effect could not be achieved with a REP prefix as the REP will repeat LODS and then start repeating STOS, but we need to alternate them. |
| 054 | CX holds the length of the string. Therefore LOOP repeats for each character of the string. |

Inside the debugger we observe how LODS and STOS alternate and CX is only used by the LOOP instruction. In the original code there were four instructions inside the loop; now there are only two. This is how string instructions help in reducing code size.

SCAS Example – String Length

Many higher level languages do not explicitly store string length; rather they use a null character, a character with an ASCII code of zero, to signal the end of a string. In assembly language programs, it is also easier to store a zero at the end of the string, instead of calculating the length of string, which is very difficult process for longer strings. So we delegate length calculation to the processor and modify our string printing subroutine to take a null terminated string and no length. We use SCASB with REPNE and a zero in AL to find a zero byte in the string. In CX we load the maximum possible size, which is 64K bytes. However actual strings will be much smaller. An important thing regarding SCAS and CMPS is that if they stop due to equality or inequality, the index registers have already incremented. Therefore when SCAS will stop DI would be pointing past the null character.

|  | Example 7.3 |
| --- | --- |
| 001 002 003 004 005 006 007-026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 | ; hello world printing with a null terminated string [org 0x0100] jmp start message: db 'hello world', 0 ; null terminated string ;;;;; COPY LINES 005-024 FROM EXAMPLE 7.1 (clrscr) ;;;;; ; subroutine to print a string ; takes the x position, y position, attribute, and address of a null ; terminated string as parameters printstr: push bp mov bp, sp push es push ax push cx push si push di push ds pop es ; load ds in es mov di, [bp+4] ; point di to string mov cx, 0xffff ; load maximum number in cx xor al, al ; load a zero in al repne scasb ; find zero in the string mov ax, 0xffff ; load maximum number in ax sub ax, cx ; find change in cx dec ax ; exclude null from length jz exit ; no printing if string is empty mov cx, ax ; load string length in cx mov ax, 0xb800 mov es, ax ; point es to video base mov al, 80 ; load al with columns per row mul byte [bp+8] ; multiply with y position add ax, [bp+10] ; add x position shl ax, 1 ; turn into byte offset mov di,ax ; point di to required location mov si, [bp+4] ; point si to string mov ah, [bp+6] ; load attribute in ah cld ; auto increment mode nextchar: lodsb ; load next char in al stosw ; print char/attribute pair loop nextchar ; repeat for the whole string exit: pop di pop si pop cx pop ax pop es pop bp ret 8 start: call clrscr ; call the clrscr subroutine mov ax, 30 push ax ; push x position mov ax, 20 push ax ; push y position mov ax, 1 ; blue on black attribute push ax ; push attribute mov ax, message push ax ; push address of message call printstr ; call the printstr subroutine mov ax, 0x4c00 ; terminate program int 0x21 |
| 039-040 | Another way to load a segment register is to use a combination of push and pop. The processor doesn’t match pushes and pops. ES is equalized to DS in this pair of instructions. |

Inside the debugger observe the working of the code for length calculation after SCASB has completed its operation.