## Lesson No. 20

## LES and LDS Instructions

Since the string instructions need their source and destination in the form of a segment offset pair, there are two special instructions that load a segment register and a general purpose register from two consecutive memory locations. LES loads ES while LDS loads DS. Both these instructions have two parameters, one is the general purpose register to be loaded and the other is the memory location from which to load these registers. The major application of these instructions is when a subroutine receives a segment offset pair as an argument and the pair is to be loaded in a segment and an offset register. According to Intel rules of significance the word at higher address is loaded in the segment register while the word at lower address is loaded in the offset register. As parameters segment should be pushed first so that it ends up at a higher address and the offset should be pushed afterwards. When loading the lower address will be given. For example “lds si, [bp+4]” will load SI from BP+4 and DS from BP+6.

LES and LDS Example

We modify the string length calculation subroutine to take the segment and offset of the string and use the LES instruction to load that segment offset pair in ES and DI.

|  | Example 7.4 |
| --- | --- |
| 001 002 003 004 005 006 007-026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 | ; hello world printing with length calculation subroutine [org 0x0100] jmp start message: db 'hello world', 0 ; null terminated string ;;;;; COPY LINES 005-024 FROM EXAMPLE 7.1 (clrscr) ;;;;; ; subroutine to calculate the length of a string ; takes the segment and offset of a string as parameters strlen: push bp mov bp,sp push es push cx push di les di, [bp+4] ; point es:di to string mov cx, 0xffff ; load maximum number in cx xor al, al ; load a zero in al repne scasb ; find zero in the string mov ax, 0xffff ; load maximum number in ax sub ax, cx ; find change in cx dec ax ; exclude null from length pop di pop cx pop es pop bp ret 4 ; subroutine to print a string ; takes the x position, y position, attribute, and address of a null ; terminated string as parameters printstr: push bp mov bp, sp push es push ax push cx push si push di push ds ; push segment of string mov ax, [bp+4] push ax ; push offset of string call strlen ; calculate string length cmp ax, 0 ; is the string empty jz exit ; no printing if string is empty mov cx, ax ; save length in cx mov ax, 0xb800 mov es, ax ; point es to video base mov al, 80 ; load al with columns per row mul byte [bp+8] ; multiply with y position add ax, [bp+10] ; add x position shl ax, 1 ; turn into byte offset mov di,ax ; point di to required location mov si, [bp+4] ; point si to string mov ah, [bp+6] ; load attribute in ah cld ; auto increment mode nextchar: lodsb ; load next char in al stosw ; print char/attribute pair loop nextchar ; repeat for the whole string exit: pop di pop si pop cx pop ax pop es pop bp ret 8 start: call clrscr ; call the clrscr subroutine mov ax, 30 push ax ; push x position mov ax, 20 push ax ; push y position mov ax, 0x71 ; blue on white attribute push ax ; push attribute mov ax, message push ax ; push address of message call printstr ; call the printstr subroutine mov ax, 0x4c00 ; terminate program int 0x21 |
| 036 | The LES instruction is used to load the DI register from BP+4 and the ES register from BP+6. |
| 065 | The convention to return a value from a subroutine is to use the AX register. That is why AX is not saved and restored in the subroutine. |

Inside the debugger observe that the segment register is pushed followed by the offset. The higher address FFE6 contains the segment and the lower address FFE4 contains the offset. This is because we have a decrementing stack. Then observe the loading of ES and DI from the stack.

MOVS Example – Screen Scrolling

MOVS has the two forms MOVSB and MOVSW. REP allows the instruction to be repeated CX times allowing blocks of memory to be copied. We will perform this copy of the video screen.

Scrolling is the process when all the lines on the screen move one or more lines towards the top of towards the bottom and the new line that appears on the top or the bottom is cleared. Scrolling is a process on which string movement is naturally applicable. REP with MOVS will utilize the full processor power to do the scrolling in minimum time.

In this example we want to scroll a variable number of lines given as argument. Therefore we have to calculate the source address, which is 160 times the number of lines to clear. The destination address is 0, which is the top left of the screen. The lines that scroll up are discarded so the source pointer is placed after them. An equal number of lines at the bottom are cleared. These lines have actually been copied above.

|  | Example 7.5 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 | ; scroll up the screen [org 0x0100] jmp start ; subroutine to scroll up the screen ; take the number of lines to scroll as parameter scrollup: push bp mov bp,sp push ax push cx push si push di push es push ds mov ax, 80 ; load chars per row in ax mul byte [bp+4] ; calculate source position mov si, ax ; load source position in si push si ; save position for later use shl si, 1 ; convert to byte offset mov cx, 2000 ; number of screen locations sub cx, ax ; count of words to move mov ax, 0xb800 mov es, ax ; point es to video base mov ds, ax ; point ds to video base xor di, di ; point di to top left column cld ; set auto increment mode rep movsw ; scroll up mov ax, 0x0720 ; space in normal attribute pop cx ; count of positions to clear rep stosw ; clear the scrolled space pop ds pop es pop di pop si pop cx pop ax pop bp ret 2 start: mov ax,5 push ax ; push number of lines to scroll call scrollup ; call the scroll up subroutine mov ax, 0x4c00 ; terminate program int 0x21 |

The beauty of this example is that the two memory blocks are overlapping. If the source and destination in the above algorithm are swapped in an expectation to scroll down the result is strange. For example if 5 lines were to scroll down, the top five lines of the screen are repeated on the whole screen. This is where the use of the direction flag comes in.

When the source is five lines below the destination, the first five lines are copied on the first five lines of the destination. However the next five lines to be copied from the source have been destroyed in the process; because they were the same as the first five lines of the destination. The same is the problem with every set of five lines as the source is destroyed during the previous copy. In this situation we must go from bottom of the screen towards the top. Now the last five lines are copied to the last five lines of the destination. The next five lines are copied to next five lines of the destination destroying the last five lines of source; but now these lines are no longer needed and have been previously copied. Therefore the copy will be appropriately done in this case.

We give an example of scrolling down with this consideration. Now we have to calculate the end of the block instead of the start.

|  | Example 7.6 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 | ; scroll down the screen [org 0x0100] jmp start ; subroutine to scrolls down the screen ; take the number of lines to scroll as parameter scrolldown: push bp mov bp,sp push ax push cx push si push di push es push ds mov ax, 80 ; load chars per row in ax mul byte [bp+4] ; calculate source position push ax ; save position for later use shl ax, 1 ; convert to byte offset mov si, 3998 ; last location on the screen sub si, ax ; load source position in si mov cx, 2000 ; number of screen locations sub cx, ax ; count of words to move mov ax, 0xb800 mov es, ax ; point es to video base mov ds, ax ; point ds to video base mov di, 3998 ; point di to lower right column std ; set auto decrement mode rep movsw ; scroll up mov ax, 0x0720 ; space in normal attribute pop cx ; count of positions to clear rep stosw ; clear the scrolled space pop ds pop es pop di pop si pop cx pop ax pop bp ret 2 start: mov ax,5 push ax ; push number of lines to scroll call scrolldown ; call scroll down subroutine mov ax, 0x4c00 ; terminate program int 0x21 |

CMPS Example – String Comparison

For the last string instruction, we take string comparison as an example. The subroutine will take two segment offset pairs containing the address of the two null terminated strings. The subroutine will return 0 if the strings are different and 1 if they are same. The AX register will be used to hold the return value.

|  | Example 7.7 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009-031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 | ; comparing null terminated strings [org 0x0100] jmp start msg1: db 'hello world', 0 msg2: db 'hello WORLD', 0 msg3: db 'hello world', 0 ;;;;; COPY LINES 028-050 FROM EXAMPLE 7.4 (strlen) ;;;;; ; subroutine to compare two strings ; takes segment and offset pairs of two strings to compare ; returns 1 in ax if they match and 0 other wise strcmp: push bp mov bp,sp push cx push si push di push es push ds lds si, [bp+4] ; point ds:si to first string les di, [bp+8] ; point es:di to second string push ds ; push segment of first string push si ; push offset of first string call strlen ; calculate string length mov cx, ax ; save length in cx push es ; push segment of second string push di ; push offset of second string call strlen ; calculate string lenth cmp cx, ax ; compare length of both strings jne exitfalse ; return 0 if they are unequal mov ax, 1 ; store 1 in ax to be returned repe cmpsb ; compare both strings jcxz exitsimple ; are they successfully compared exitfalse: mov ax, 0 ; store 0 to mark unequal exitsimple: pop ds pop es pop di pop si pop cx pop bp ret 8 start: push ds ; push segment of first string mov ax, msg1 push ax ; push offset of first string push ds ; push segment of second string mov ax, msg2 push ax ; push offset of second string call strcmp ; call strcmp subroutine push ds ; push segment of first string mov ax, msg1 push ax ; push offset of first string push ds ; push segment of third string mov ax, msg3 push ax ; push offset of third string call strcmp ; call strcmp subroutine mov ax, 0x4c00 ; terminate program int 0x21 |
| 005-007 | Three strings are declared out of which two are equal and one is different. |
| 044-045 | LDS and LES are used to load the pointers to the two strings in DS:SI and ES:DI. |
| 070 | Since there are 4 parameters to the subroutine “ret 8” is used. |

Inside the debugger we observe that REPE is shown as REP. This is because REP and REPE are represented with the same prefix byte. When used with STOS, LODS, and MOVS it functions as REP and when used with SCAS and CMPS it functions as REPE.

Exercises

- Write code to find the byte in AL in the whole megabyte of memory such that each memory location is compared to AL only once.

- Write a far procedure to reverse an array of 64k words such that the first element becomes the last and the last becomes the first and so on. For example if the first word contained 0102h, this value is swapped with the last word. The next word is swapped with the second last word and so on. The routine will be passed two parameters through the stack; the segment and offset of the first element of the array.

- Write a near procedure to copy a given area on the screen at the center of the screen without using a temporary array. The routine will be passed top, left, bottom, and right in that order through the stack. The parameters passed will always be within range the height will be odd and the width will be even so that it can be exactly centered.

- Write code to find two segments in the whole memory that are exactly the same. In other words find two distinct values which if loaded in ES and DS then for every value of SI [DS:SI]=[ES:SI].

- Write a function writechar that takes two parameters. The first parameter is the character to write and the second is the address of a memory area containing top, left, bottom, right, current row, current column, normal attribute, and cursor attribute in 8 consecutive bytes. These define a virtual window on the screen.

The function writes the passed character at (current row, current column) using the normal attribute. It then increments current column, If current column goes outside the window, it makes it zero and increments current row. If current row gets out of window, it scrolls the window one line up, and blanks out the new line in the window. In the end, it sets the attribute of the new (current row, current column) to cursor attribute.

- Write a function “strcpy” that takes the address of two parameters via stack, the one pushed first is source and the second is the destination. The function should copy the source on the destination including the null character assuming that sufficient space is reserved starting at destination.