Lesson No.27

Programmable Interval Timer

Another very important peripheral device is the Programmable Interval Timer (PIT), the chip numbered 8254. This chip has a precise input frequency of 1.19318 MHz. This frequency is fixed regardless of the processor clock. Inside the chip is a 16bit divisor which divides this input frequency and the output is connected to the IRQ 0 line of the PIC. The special number 0 if placed in the divisor means a divisor of 65536 and not 0. The standard divisor is 0 unless we change it. Therefore by default IRQ 0 is generated 1193180/65536=18.2 times per second. This is called the timer tick. There is an interval of about 55ms between two timer ticks. The system time is maintained with the timer interrupt. This is the highest priority interrupt and breaks whatever is executing. Time can be maintained with this interrupt as this frequency is very precise and is part of the IBM standard.

When writing a TSR we give control back to DOS so TSR activation, reactivation and action is solely interrupt based, whether this is a hardware interrupt or a software one. Control is never given back; it must be caught, just like we caught control by hooking the keyboard interrupt. Our next example will hook the timer interrupt and display a tick count on the screen.

|  | Example 9.7 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 | ; display a tick count on the top right of screen [org 0x0100] jmp start tickcount: dw 0 ; subroutine to print a number at top left of screen ; takes the number to be printed as its parameter printnum: push bp mov bp, sp push es push ax push bx push cx push dx push di mov ax, 0xb800 mov es, ax ; point es to video base mov ax, [bp+4] ; load number in ax mov bx, 10 ; use base 10 for division mov cx, 0 ; initialize count of digits nextdigit: mov dx, 0 ; zero upper half of dividend div bx ; divide by 10 add dl, 0x30 ; convert digit into ascii value push dx ; save ascii value on stack inc cx ; increment count of values cmp ax, 0 ; is the quotient zero jnz nextdigit ; if no divide it again mov di, 140 ; point di to 70th column nextpos: pop dx ; remove a digit from the stack mov dh, 0x07 ; use normal attribute mov [es:di], dx ; print char on screen add di, 2 ; move to next screen location loop nextpos ; repeat for all digits on stack pop di pop dx pop cx pop bx pop ax pop es pop bp ret 2 ; timer interrupt service routine timer: push ax inc word [cs:tickcount]; increment tick count push word [cs:tickcount] call printnum ; print tick count mov al, 0x20 out 0x20, al ; end of interrupt pop ax iret ; return from interrupt start: xor ax, ax mov es, ax ; point es to IVT base cli ; disable interrupts mov word [es:8*4], timer; store offset at n*4 mov [es:8*4+2], cs ; store segment at n*4+2 sti ; enable interrupts mov dx, start ; end of resident portion add dx, 15 ; round up to next para mov cl, 4 shr dx, cl ; number of paras mov ax, 0x3100 ; terminate and stay resident int 0x21 |

When we execute the program the counter starts on the screen. Whatever we do, take directory, open EDIT, the debugger etc. the counter remains running on the screen. No one is giving control to the program; the program is getting executed as a result of timer generating INT 8 after every 55ms.

Our next example will hook both the keyboard and timer interrupts. When the shift key is pressed the tick count starts incrementing and as soon as the shift key is released the tick count stops. Both interrupt handlers are communicating through a common variable. The keyboard interrupt sets this variable while the timer interrupts modifies its behavior according to this variable.

|  | Example 9.8 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009-049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 106 107 108 109 110 111 112 113 | ; display a tick count while the left shift key is down [org 0x0100] jmp start seconds: dw 0 timerflag: dw 0 oldkb: dd 0 ;;;;; COPY LINES 007-047 FROM EXAMPLE 9.7 (printnum) ;;;;; ; keyboard interrupt service routine kbisr: push ax in al, 0x60 ; read char from keyboard port cmp al, 0x2a ; has the left shift pressed jne nextcmp ; no, try next comparison cmp word [cs:timerflag], 1; is the flag already set je exit ; yes, leave the ISR mov word [cs:timerflag], 1; set flag to start printing jmp exit ; leave the ISR nextcmp: cmp al, 0xaa ; has the left shift released jne nomatch ; no, chain to old ISR mov word [cs:timerflag], 0; reset flag to stop printing jmp exit ; leave the interrupt routine nomatch: pop ax jmp far [cs:oldkb] ; call original ISR exit: mov al, 0x20 out 0x20, al ; send EOI to PIC pop ax iret ; return from interrupt ; timer interrupt service routine timer: push ax cmp word [cs:timerflag], 1 ; is the printing flag set jne skipall ; no, leave the ISR inc word [cs:seconds] ; increment tick count push word [cs:seconds] call printnum ; print tick count skipall: mov al, 0x20 out 0x20, al ; send EOI to PIC pop ax iret ; return from interrupt start: xor ax, ax mov es, ax ; point es to IVT base mov ax, [es:9*4] mov [oldkb], ax ; save offset of old routine mov ax, [es:9*4+2] mov [oldkb+2], ax ; save segment of old routine cli ; disable interrupts mov word [es:9*4], kbisr ; store offset at n*4 mov [es:9*4+2], cs ; store segment at n*4+2 mov word [es:8*4], timer ; store offset at n*4 mov [es:8*4+2], cs ; store segment at n*4+ sti ; enable interrupts mov dx, start ; end of resident portion add dx, 15 ; round up to next para mov cl, 4 shr dx, cl ; number of paras mov ax, 0x3100 ; terminate and stay resident int 0x21 |
| 006 | This flag is one when the timer interrupt should increment and zero when it should not. |
| 058-059 | As the keyboard controller repeatedly generates the press code if the release code does not come in a specified time, we have placed a check to not repeatedly set it to one. |
| 058 | Another way to access TSR data is using the CS override instead of initializing DS. It is common mistake not to initialize DS and also not put in CS override in a real time interrupt handler. |

When we execute the program and the shift key is presseed, the counter starts incrementing. When the key is released the counter stops. When it is pressed again the counter resumes counting. As this is made as a TSR any other program can be loaded and will work properly alongside the TSR.

Parallel Port

Computers can control external hardware through various external ports like the parallel port, the serial port, and the new additions USB and FireWire. Using this, computers can be used to control almost anything. For our examples we will use the parallel port. The parallel port has two views, the connector that the external world sees and the parallel port controller ports through which the processor communicates with the device connected to the parallel port.

The parallel port connector is a 25pin connector called DB-25. Different pins of this connector have different meanings. Some are meaningful only with the printer. This is a bidirectional port so there are some pins to take data from the processor to the parallel port and others to take data from the parallel port to the processor. Important pins for our use are the data pins from pin 2 to pin 9 that take data from the processor to the device. Pin 10, the ACK pin, is normally used by the printer to acknowledge the receipt of data and show the willingness to receive more data. Signalling this pin generates IRQ 7 if enabled in the PIC and in the parallel port controller. Pin 18-25 are ground and must be connected to the external circuit ground to provide the common reference point otherwise they won’t understand each other voltage levels. Like the datum point in a graph this is the datum point of an electrical circuit. The remaining pins are not of our concern in these examples.

This is the external view of the parallel port. The processor cannot see these pins. The processor uses the I/O ports of the parallel port controller. The first parallel port LPT1 has ports designated from 378 to 37A. The first port 378 is the data port. If we use the OUT instruction on this port, 1 bits result in a 5V signal on the corresponding pin and a 0 bits result in a 0V signal on the corresponding pin.

Port 37A is the control port. Our interest is with bit 4 of this port which enables the IRQ 7 triggering by the ACK pin. We have attached a circuit that connects 8 LEDs with the parallel port pins. The following examples sends the scancode of the key pressed to the parallel port so that it is visible on LEDs.

|  | Example 9.9 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 | ; show scancode on external LEDs connected through parallel port [org 0x0100] jmp start oldisr: dd 0 ; space for saving old ISR ; keyboard interrupt service routine kbisr: push ax push dx in al, 0x60 ; read char from keyboard port mov dx, 0x378 out dx, al ; write char to parallel port pop ax pop dx jmp far [cs:oldisr] ; call original ISR start: xor ax, ax mov es, ax ; point es to IVT base mov ax, [es:9*4] mov [oldisr], ax ; save offset of old routine mov ax, [es:9*4+2] mov [oldisr+2], ax ; save segment of old routine cli ; disable interrupts mov word [es:9*4], kbisr ; store offset at n*4 mov [es:9*4+2], cs ; store segment at n*4+2 sti ; enable interrupts mov dx, start ; end of resident portion add dx, 15 ; round up to next para mov cl, 4 shr dx, cl ; number of paras mov ax, 0x3100 ; terminate and stay resident int 0x21 |

The following example uses the same LED circuit and sends data such that LEDs switch on and off turn by turn so that it looks like light is moving back and forth.

|  | Example 9.10 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 | ; show lights moving back and forth on external LEDs [org 0x0100] jmp start signal: db 1 ; current state of lights direction: db 0 ; current direction of motion ; timer interrupt service routine timer: push ax push dx push ds push cs pop ds ; initialize ds to data segment cmp byte [direction], 1; are moving in right direction je moveright ; yes, go to shift right code shl byte [signal], 1 ; shift left state of lights jnc output ; no jump to change direction mov byte [direction], 1; change direction to right mov byte [signal], 0x80; turn on left most light jmp output ; proceed to send signal moveright: shr byte [signal], 1 ; shift right state of lights jnc output ; no jump to change direction mov byte [direction], 0; change direction to left mov byte [signal], 1 ; turn on right most light output: mov al, [signal] ; load lights state in al mov dx, 0x378 ; parallel port data port out dx, al ; send light state of port mov al, 0x20 out 0x20, al ; send EOI on PIC pop ds pop dx pop ax iret ; return from interrupt start: xor ax, ax mov es, ax ; point es to IVT base cli ; disable interrupts mov word [es:8*4], timer ; store offset at n*4 mov [es:8*4+2], cs ; store segment at n*4+2 sti ; enable interrupts mov dx, start ; end of resident portion add dx, 15 ; round up to next para mov cl, 4 shr dx, cl ; number of paras mov ax, 0x3100 ; terminate and stay resident int 0x21 |

We will now use the parallel port to control a slightly complicated circuit. This time we will also use the parallel port interrupt. We are using a 220 V bulb with AC input. AC current is 50Hz sine wave. We have made our circuit such that it triggers the parallel port interrupt whenever the since wave crosses zero. We have control of passing the AC current to the bulb. We control it such that in every cycle only a fixed percentage of time the current passes on to the bulb. Using this we can control the intensity or glow of the bulb.

Our first example will slowly turn on the bulb by increasing the power provided using the mechanism just described.

|  | Example 9.11 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 106 107 108 | ; slowly turn on a bulb by gradually increasing the power provided [org 0x0100] jmp start flag: db 0 ; next time turn on or turn off stop: db 0 ; flag to terminate the program divider: dw 11000 ; divider for minimum intensity oldtimer: dd 0 ; space for saving old isr ; timer interrupt service routine timer: push ax push dx cmp byte [cs:flag], 0 ; are we here to turn off je switchoff ; yes, go to turn off code switchon: mov al, 1 mov dx, 0x378 out dx, al ; no, turn the bulb on mov ax, 0x0100 out 0x40, al ; set timer divisor LSB to 0 mov al, ah out 0x40, al ; set timer divisor MSB to 1 mov byte [cs:flag], 0 ; flag next timer to switch off jmp exit ; leave the interrupt routine switchoff: xor ax, ax mov dx, 0x378 out dx, al ; turn the bulb off exit: mov al, 0x20 out 0x20, al ; send EOI to PIC pop dx pop ax iret ; return from interrupt ; parallel port interrupt service routine parallel: push ax mov al, 0x30 ; set timer to one shot mode out 0x43, al cmp word [cs:divider], 100; is the current divisor 100 je stopit ; yes, stop sub word [cs:divider], 10; decrease the divisor by 10 mov ax, [cs:divider] out 0x40, al ; load divisor LSB in timer mov al, ah out 0x40, al ; load divisor MSB in timer mov byte [cs:flag], 1 ; flag next timer to switch on mov al, 0x20 out 0x20, al ; send EOI to PIC pop ax iret ; return from interrupt stopit: mov byte [stop], 1 ; flag to terminate the program mov al, 0x20 out 0x20, al ; send EOI to PIC pop ax iret ; return from interrupt start: xor ax, ax mov es, ax ; point es to IVT base mov ax, [es:0x08*4] mov [oldtimer], ax ; save offset of old routine mov ax, [es:0x08*4+2] mov [oldtimer+2], ax ; save segment of old routine cli ; disable interrupts mov word [es:0x08*4], timer ; store offset at n*4 mov [es:0x08*4+2], cs ; store segment at n*4+2 mov word [es:0x0F*4], parallel ; store offset at n*4 mov [es:0x0F*4+2], cs ; store segment at n*4+2 sti ; enable interrupts mov dx, 0x37A in al, dx ; parallel port control register or al, 0x10 ; turn interrupt enable bit on out dx, al ; write back register in al, 0x21 ; read interrupt mask register and al, 0x7F ; enable IRQ7 for parallel port out 0x21, al ; write back register recheck: cmp byte [stop], 1 ; is the termination flag set jne recheck ; no, check again mov dx, 0x37A in al, dx ; parallel port control register and al, 0xEF ; turn interrupt enable bit off out dx, al ; write back register in al, 0x21 ; read interrupt mask register or al, 0x80 ; disable IRQ7 for parallel port out 0x21, al ; write back regsiter cli ; disable interrupts mov ax, [oldtimer] ; read old timer ISR offset mov [es:0x08*4], ax ; restore old timer ISR offset mov ax, [oldtimer+2] ; read old timer ISR segment mov [es:0x08*4+2], ax ; restore old timer ISR segment sti ; enable interrupts mov ax, 0x4c00 ; terminate program int 0x21 |

The next example is simply the opposite of the previous. It slowly turns the bulb off from maximum glow to no glow.

|  | Example 9.12 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010-037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 106 107 108 | ; slowly turn off a bulb by gradually decreasing the power provided [org 0x0100] jmp start flag: db 0 ; next time turn on or turn off stop: db 0 ; flag to terminate the program divider: dw 0 ; divider for maximum intensity oldtimer: dd 0 ; space for saving old isr ;;;;; COPY LINES 009-036 FROM EXAMPLE 9.11 (timer) ;;;;; ; parallel port interrupt service routine parallel: push ax mov al, 0x30 ; set timer to one shot mode out 0x43, al cmp word [cs:divider], 11000; current divisor is 11000 je stopit ; yes, stop add word [cs:divider], 10; increase the divisor by 10 mov ax, [cs:divider] out 0x40, al ; load divisor LSB in timer mov al, ah out 0x40, al ; load divisor MSB in timer mov byte [cs:flag], 1 ; flag next timer to switch on mov al, 0x20 out 0x20, al ; send EOI to PIC pop ax iret ; return from interrupt stopit: mov byte [stop], 1 ; flag to terminate the program mov al, 0x20 out 0x20, al ; send EOI to PIC pop ax iret ; return from interrupt start: xor ax, ax mov es, ax ; point es to IVT base mov ax, [es:0x08*4] mov [oldtimer], ax ; save offset of old routine mov ax, [es:0x08*4+2] mov [oldtimer+2], ax ; save segment of old routine cli ; disable interrupts mov word [es:0x08*4], timer ; store offset at n*4 mov [es:0x08*4+2], cs ; store segment at n*4+2 mov word [es:0x0F*4], parallel ; store offset at n*4 mov [es:0x0F*4+2], cs ; store segment at n*4+2 sti ; enable interrupts mov dx, 0x37A in al, dx ; parallel port control register or al, 0x10 ; turn interrupt enable bit on out dx, al ; write back register in al, 0x21 ; read interrupt mask register and al, 0x7F ; enable IRQ7 for parallel port out 0x21, al ; write back register recheck: cmp byte [stop], 1 ; is the termination flag set jne recheck ; no, check again mov dx, 0x37A in al, dx ; parallel port control register and al, 0xEF ; turn interrupt enable bit off out dx, al ; write back register in al, 0x21 ; read interrupt mask register or al, 0x80 ; disable IRQ7 for parallel port out 0x21, al ; write back regsiter cli ; disable interrupts mov ax, [oldtimer] ; read old timer ISR offset mov [es:0x08*4], ax ; restore old timer ISR offset mov ax, [oldtimer+2] ; read old timer ISR segment mov [es:0x08*4+2], ax ; restore old timer ISR segment sti ; enable interrupts mov ax, 0x4c00 ; terminate program int 0x21 |

This example is a mix of the previous two. Here we can increase the bulb intensity with F11 and decrease it with F12.

|  | Example 9.13 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009-036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 106 107 108 109 110 111 | ; control external bulb intensity with F11 and F12 [org 0x0100] jmp start flag: db 0 ; next time turn on or turn off divider: dw 100 ; initial timer divider oldkb: dd 0 ; space for saving old ISR ;;;;; COPY LINES 009-036 FROM EXAMPLE 9.11 (timer) ;;;;; ; keyboard interrupt service routine kbisr: push ax in al, 0x60 cmp al, 0x57 jne nextcmp cmp word [cs:divider], 11000 je exitkb add word [cs:divider], 100 jmp exitkb nextcmp: cmp al, 0x58 jne chain cmp word [cs:divider], 100 je exitkb sub word [cs:divider], 100 jmp exitkb exitkb: mov al, 0x20 out 0x20, al pop ax iret chain: pop ax jmp far [cs:oldkb] ; parallel port interrupt service routine parallel: push ax mov al, 0x30 ; set timer to one shot mode out 0x43, al mov ax, [cs:divider] out 0x40, al ; load divisor LSB in timer mov al, ah out 0x40, al ; load divisor MSB in timer mov byte [cs:flag], 1 ; flag next timer to switch on mov al, 0x20 out 0x20, al ; send EOI to PIC pop ax iret ; return from interrupt start: xor ax, ax mov es, ax ; point es to IVT base mov ax, [es:0x09*4] mov [oldkb], ax ; save offset of old routine mov ax, [es:0x09*4+2] mov [oldkb+2], ax ; save segment of old routine cli ; disable interrupts mov word [es:0x08*4], timer ; store offset at n*4 mov [es:0x08*4+2], cs ; store segment at n*4+2 mov word [es:0x09*4], kbisr ; store offset at n*4 mov [es:0x09*4+2], cs ; store segment at n*4+2 mov word [es:0x0F*4], parallel ; store offset at n*4 mov [es:0x0F*4+2], cs ; store segment at n*4+2 sti ; enable interrupts mov dx, 0x37A in al, dx ; parallel port control register or al, 0x10 ; turn interrupt enable bit on out dx, al ; write back register in al, 0x21 ; read interrupt mask register and al, 0x7F ; enable IRQ7 for parallel port out 0x21, al ; write back register mov dx, start ; end of resident portion add dx, 15 ; round up to next para mov cl, 4 shr dx, cl ; number of paras mov ax, 0x3100 ; terminate and stay resident int 0x21 |

Exercises

- Suggest a reason for the following. The statements are all true.

  - We should disable interrupts while hooking interrupt 8h. I.e. while placing its segment and offset in the interrupt vector table.

  - We need not do this for interrupt 80h.

  - We need not do this when hooking interrupt 8h from inside the interrupt handler of interrupt 80h.

  - We should disable interrupts while we are changing the stack (SS and SP).

  - EOI is not sent from an interrupt handler which does interrupt chaining.

  - If no EOI is sent from interrupt 9h and no chaining is done, interrupt 8h still comes if the interrupt flag is on.

  - After getting the size in bytes by putting a label at the end of a COM TSR, 0fh is added before dividing by 10h.

  - Interrupts are disabled but divide by zero interrupt still comes.

- If no hardware interrupts are coming, what are all possible reasons?

- Write a program to make an asterisks travel the border of the screen, from upper left to upper right to lower right to lower left and back to upper left indefinitely, making each movement after one second.

- [Musical Arrow] Write a TSR to make an arrow travel the border of the screen from top left to top right to bottom right to bottom left and back to top left at the speed of 36.4 locations per second. The arrow should not destroy the data beneath it and should be restored as soon as the arrow moves forward.

The arrow head should point in the direction of movement using the characters > V < and ^. The journey should be accompanied by a different tone from the pc speaker for each side of the screen. Do interrupt chaining so that running the TSR 10 times produces 10 arrows travelling at different locations.

HINT: At the start you will need to reprogram channel 0 for 36.4 interrupts per second, double the normal. You will have to reprogram channel 2 at every direction change, though you can enable the speaker once at the very start.

- In the above TSR hook the keyboard interrupt as well and check if 'q' is pressed. If not chain to the old interrupt, if yes restore everything and remove the TSR from memory. The effect should be that pressing 'q' removes one moving arrow. If you do interrupt chaining when pressing 'q' as well, it will remove all arrows at once.

- Write a TSR to rotate the screen (scroll up and copy the old top most line to the bottom) while F10 is pressed. The screen will keep rotating while F10 is pressed at 18.2 rows per second. As soon as F10 is released the rotation should stop and the original screen restored. A secondary buffer of only 160 bytes (one line of screen) can be used.

- Write a TSR that hooks software interrupt 0x80 and the timer interrupt. The software interrupt is called by other programs with the address of a far function in ES:DI and the number of timer ticks after which to call back that function in CX. The interrupt records this information and returns to the caller. The function will actually be called by the timer interrupt after the desired number of ticks. The maximum number of functions and their ticks can be fixed to 8.

- Write a TSR to clear the screen when CTRL key is pressed and restore it when it is released.

- Write a TSR to disable all writes to the hard disk when F10 is pressed and re-enable when pressed again like a toggle.

HINT: To write to the hard disk programs call the BIOS service INT 0x13 with AH=3.

- Write a keyboard interrupt handler that disables the timer interrupt (no timer interrupt should come) while Q is pressed. It should be re-enabled as soon as Q is released.

- Write a TSR to calculate the current typing speed of the user. Current typing speed is the number of characters typed by the user in the last five seconds. The speed should be represented by printing asterisks at the right border (80th column) of the screen starting from the upper right to the lower right corner (growing downwards). Draw n asterisks if the user typed n characters in the last five seconds. The count should be updated every second.

- Write a TSR to show a clock in the upper right corner of the screen in the format HH:MM:SS.DD where HH is hours in 24 hour format, MM is minutes, SS is seconds and DD is hundredth of second. The clock should beep twice for one second each time with half a second interval in between at the start of every minute at a frequency of your choice.

HINT: IBM PC uses a Real Time Clock (RTC) chip to keep track of time while switched off. It provides clock and calendar functions through its two I/O ports 70h and 71h. It is used as follows:

mov  al, <command>
              out  0x70, al        ; command byte written at first port
              jmp  D1              ; waste one instruction time
D1:           in   al, 0x71        ; result of command is in AL now

Following are few commands

00 Get current second

02 Get current minute

04 Get current hour

All numbers returned by RTC are in BCD. E.g. if it is 6:30 the second and third command will return 0x30 and 0x06 respectively in al.

# Footnotes

The parallel port is most commonly used with the printer. However some new printers have started using the USB port.

Older computer had more than one parallel port named LPT2 and having ports from 278-27A.