Debug Interrupts

Debugger using single step interrupt

The use of the trap flag has been deferred till now. The three flags not used for mathematical operations are the direction flag, the interrupt flag and the trap flag. The direction and interrupt flags have been previously discussed.

If the interrupt flag is set, the after every instruction a type 1 interrupt will be automatically generated. When the IVT and reserved interrupts were discussed this was named as the single step interrupt. This is like the divide by zero interrupt which was never explicitly invoked but it came itself. The single step interrupt behaves in the same manner.

The debugger is made using this interrupt. It allows one instruction to be executed and then return control to us. It has its display code and its code to wait for the key in the INT 1 handler. Therefore after every instruction the values of all registers are shown and the debugger waits for a key. Another interrupt used by the debugger is the break point interrupt INT 3. Apart from single stepping debugger has the breakpoint feature. INt 3 is used for this feature. INT 3 has a single byte opcode so it can replace any instruction. To put a breakpoint the instruction is replaced with INT 3 opcode and restored in the INT 3 handler. The INT 3 opcode is agained placed by a single step interrupt that is set up for this purpose after the replaced instruction has been executed.

There is no instruction to set or clear the trap flag like there are instructions for the interrupt and direction flags. We use twop special instructions PUSHF and POPF to push and pop the flag from the stack. We use PUSHF to place flags on the stack, change TF in this image on the stack and then reload into the flags register with POPF. The single step interrupt will come after the first instruction after POPF. The interrupt mechanism automatically clears IF and TF otherwise there would an infinite recursion of the single step interrupt. The TF is set in the flags on the stack so another interrupt will comes after one more instruction is executed after the return of the interrupt.

The following example is a very elementary debugger using the trap flag and the single step interrupt.

|  | Example 10.1 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009-026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 106 107 108 109 110 111 112 113 114 115 116 117 118 119 120 121 123 124 125 126 127 128 129 130 131 132 133 134 135 136 137 138 139 140 141 142 143 144 145 146 147 148 149 150 151 152 153 154 155 156 157 158 159 160 161 162 163 164 165 166 167 168 169 170 171 172 173 174 175 176 177 178 179 180 181 182 183 184 185 186 187 188 189 190 191 192 193 194 195 196 197 198 199 200 201 202 203 204 205 206 207 208 209 210 211 212 213 214 215 216 217 218 219 220 221 222 | ; single stepping using the trap flag and single step interrupt [org 0x0100] jmp start flag: db 0 ; flag whether a key pressed oldisr: dd 0 ; space for saving old ISR names: db 'FL =CS =IP =BP =AX =BX =CX =DX =SI =DI =DS =ES =' ;;;;; COPY LINES 008-025 FROM EXAMPLE 6.2 (clrscr) ;;;;; ; subroutine to print a number on screen ; takes the row no, column no, and number to be printed as parameters printnum: push bp mov bp, sp push es push ax push bx push cx push dx push di mov di, 80 ; load di with columns per row mov ax, [bp+8] ; load ax with row number mul di ; multiply with columns per row mov di, ax ; save result in di add di, [bp+6] ; add column number shl di, 1 ; turn into byte count add di, 8 ; to end of number location mov ax, 0xb800 mov es, ax ; point es to video base mov ax, [bp+4] ; load number in ax mov bx, 16 ; use base 16 for division mov cx, 0 ; initialize count of digits nextdigit: mov dx, 0 ; zero upper half of dividend div bx ; divide by 10 add dl, 0x30 ; convert digit into ascii value cmp dl, 0x39 ; is the digit an alphabet jbe skipalpha ; no, skip addition add dl, 7 ; yes, make in alphabet code skipalpha: mov dh, 0x07 ; attach normal attribute mov [es:di], dx ; print char on screen sub di, 2 ; to previous screen location loop nextdigit ; if no divide it again pop di pop dx pop cx pop bx pop ax pop es pop bp ret 6 ; subroutine to print a string ; takes row no, column no, address of string, and its length ; as parameters printstr: push bp mov bp, sp push es push ax push bx push cx push dx push si push di mov ax, 0xb800 mov es, ax ; point es to video base mov di, 80 ; load di with columns per row mov ax, [bp+8] ; load ax with row number mul di ; multiply with columns per row mov di, ax ; save result in di add di, [bp+6] ; add column number shl di, 1 ; turn into byte count mov si, [bp+6] ; string to be printed mov cx, [bp+4] ; length of string mov ah, 0x07 ; normal attribute is fixed nextchar: mov al, [si] ; load next char of string mov [es:di], ax ; show next char on screen add di, 2 ; move to next screen location add si, 1 ; move to next char loop nextchar ; repeat the operation cx times pop di pop si pop dx pop cx pop bx pop ax pop es pop bp ret 8 ; keyboard interrupt service routine kbisr: push ax in al, 0x60 ; read a char from keyboard port test al, 0x80 ; is it a press code jnz skipflag ; no, leave the interrupt add byte [cs:flag], al ; yes, set flag to proceed skipflag: mov al, 0x20 out 0x20, al pop ax iret ; single step interrupt service routine trapisr: push bp mov bp, sp ; to read cs, ip and flags push ax push bx push cx push dx push si push di push ds push es sti ; waiting for keyboard interrupt push cs pop ds ; initialize ds to data segment mov byte [flag], 0 ; set flag to wait for key call clrscr ; clear the screen mov si, 6 ; first register is at bp+6 mov cx, 12 ; total 12 registers to print mov ax, 0 ; start from row 0 mov bx, 5 ; print at column 5 l3: push ax ; row number push bx ; column number mov dx, [bp+si] push dx ; number to be printed call printnum ; print the number sub si, 2 ; point to next register inc ax ; next row number loop l3 ; repeat for the 12 registers mov ax, 0 ; start from row 0 mov bx, 0 ; start from column 0 mov cx, 12 ; total 12 register names mov si, 4 ; each name length is 4 chars mov dx, names ; offset of first name in dx l1: push ax ; row number push bx ; column number push dx ; offset of string push si ; length of string call printstr ; print the string add dx, 4 ; point to start of next string inc ax ; new row number loop l1 ; repeat for 12 register names keywait: cmp byte [flag], 0 ; has a key been pressed je keywait ; no, check again pop es pop ds pop di pop si pop dx pop cx pop bx pop ax pop bp iret start: xor ax, ax mov es, ax ; point es to IVT base mov ax, [es:9*4] mov [oldisr], ax ; save offset of old routine mov ax, [es:9*4+2] mov [oldisr+2], ax ; save segment of old routine mov word [es:1*4], trapisr ; store offset at n*4 mov [es:1*4+2], cs ; store segment at n*4+2 cli ; disable interrupts mov word [es:9*4], kbisr ; store offset at n*4 mov [es:9*4+2], cs ; store segment at n*4+2 sti ; enable interrupts pushf ; save flags on stack pop ax ; copy flags in ax or ax, 0x100 ; set bit corresponding to TF push ax ; save ax on stack popf ; reload into flags register ; the trap flag bit is on now, INT 1 will come after next instruction ; sample code to check the working of our elementary debugger mov ax, 0 mov bx, 0x10 mov cx, 0x20 mov dx, 0x40 l2: inc ax add bx, 2 dec cx sub dx, 2 jmp l2 |