Lesson No.30

Concepts of Multitasking

To experience the power of assembly language we introduce how to implement multitasking. We observed in the debugger that our thread of instructions was broken by the debugger; it got the control, used all registers, displayed an elaborate interface, waited for the key, and then restored processor state to what was immediately before interruption. Our program resumed as if nothing happened. The program execution was in the same logical flow.

If we have two different programs A and B. Program A is broken, its state saved, and returned to B instead of A. By looking at the instruction set, we can immediately say that nothing can stop us from doing that. IRET will return to whatever CS and IP it finds on the stack. Now B is interrupted somehow, its state saved, and we return back to A. A will have no way of knowing that it was interrupted as its entire environment has been restored. It never knew the debugger took control when it was debugged. It sill has no way of gaining this knowledge. If this work of breaking and restoring programs is done at high speed the user will feel that all the programs are running at the same time where actually they are being switched to and forth at high speed.

In essence multitasking is simple, even though we have to be extremely careful when implementing it. The environment of a program in the very simple case is all its registers and stack. We will deal with stack later. Now to get control from the program without the program knowing about it, we can use the IRQ 0 highest priority interrupt that is periodically coming to the processor.

Now we present a very basic example of multitasking. We have two subroutines written in assembly language. All the techiniques discussed here are applicable to code written in higher level languages as well. However the code to control this multitasking cannot be easily written in a higher level language so we write it in assembly language. The two subroutines rotate bars by changing characters at the two corners of the screen and have infinite loops. By hooking the timer interrupt and saving and restoring the registers of the tasks one by one, it appears that both tasks are running simultaneously.

|  | Example 11.1 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 | ; elementary multitasking of two threads [org 0x0100] jmp start ; ax,bx,ip,cs,flags storage area taskstates: dw 0, 0, 0, 0, 0 ; task0 regs dw 0, 0, 0, 0, 0 ; task1 regs dw 0, 0, 0, 0, 0 ; task2 regs current: db 0 ; index of current task chars: db '\¦/-' ; shapes to form a bar ; one task to be multitasked taskone: mov al, [chars+bx] ; read the next shape mov [es:0], al ; write at top left of screen inc bx ; increment to next shape and bx, 3 ; taking modulus by 4 jmp taskone ; infinite task ; second task to be multitasked tasktwo: mov al, [chars+bx] ; read the next shape mov [es:158], al ; write at top right of screen inc bx ; increment to next shape and bx, 3 ; taking modulus by 4 jmp tasktwo ; infinite task ; timer interrupt service routine timer: push ax push bx mov bl, [cs:current] ; read index of current task mov ax, 10 ; space used by one task mul bl ; multiply to get start of task mov bx, ax ; load start of task in bx pop ax ; read original value of bx mov [cs:taskstates+bx+2], ax ; space for current task pop ax ; read original value of ax mov [cs:taskstates+bx+0], ax ; space for current task pop ax ; read original value of ip mov [cs:taskstates+bx+4], ax ; space for current task pop ax ; read original value of cs mov [cs:taskstates+bx+6], ax ; space for current task pop ax ; read original value of flags mov [cs:taskstates+bx+8], ax ; space for current task inc byte [cs:current] ; update current task index cmp byte [cs:current], 3 ; is task index out of range jne skipreset ; no, proceed mov byte [cs:current], 0 ; yes, reset to task 0 skipreset: mov bl, [cs:current] ; read index of current task mov ax, 10 ; space used by one task mul bl ; multiply to get start of task mov bx, ax ; load start of task in bx mov al, 0x20 out 0x20, al ; send EOI to PIC push word [cs:taskstates+bx+8] ; flags of new task push word [cs:taskstates+bx+6] ; cs of new task push word [cs:taskstates+bx+4] ; ip of new task mov ax, [cs:taskstates+bx+0] ; ax of new task mov bx, [cs:taskstates+bx+2] ; bx of new task iret ; return to new task start: mov word [taskstates+10+4], taskone ; initialize ip mov [taskstates+10+6], cs ; initializae cs mov word [taskstates+10+8], 0x0200 ; initialize flags mov word [taskstates+20+4], tasktwo ; initialize ip mov [taskstates+20+6], cs ; initializae cs mov word [taskstates+20+8], 0x0200 ; initialize flags mov word [current], 0 ; set current task index xor ax, ax mov es, ax ; point es to IVT base cli mov word [es:8*4], timer mov [es:8*4+2], cs ; hook timer interrupt mov ax, 0xb800 mov es, ax ; point es to video base xor bx, bx ; initialize bx for tasks sti jmp $ ; infinite loop |

The space where all registers of a task are stsored is called the process control block or PCB. Actual PCB contains a few more things that are not relevant to us now. INT 08 that is saving and restoring the registers is called the scheduler and the whole event is called a context switch.

Elaborate Multitasking

In our next example we will save all 14 registers and the stack as well. 28 bytes are needed by these registers in the PCB. We add some more space to make the size 32, a power of 2 for easy calculations. One of these words is used to form a linked list of the PCBs so that strict ordering of active PCBs is not necessary. Also in this example we have given every thread its own stack. Now threads can have function calls, parameters and local variables etc. Another important change in this example is that the creation of threads is now dynamic. The thread registration code initializes the PCB, and adds it to the linked list so that the scheduler will give it a turn.

|  | Example 11.2 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014-057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 106 107 108 109 110 111 112 113 114 115 116 117 118 119 120 121 123 124 125 126 127 128 129 130 131 132 133 134 135 136 137 138 139 140 141 142 143 144 145 146 147 148 149 150 151 152 153 154 155 156 157 158 159 160 161 162 163 164 165 166 167 168 169 170 171 172 173 174 175 176 177 178 179 180 181 182 183 184 185 186 187 188 189 190 191 192 193 194 195 196 197 198 199 200 201 202 203 204 205 206 207 208 209 210 211 212 | ; multitasking and dynamic thread registration [org 0x0100] jmp start ; PCB layout: ; ax,bx,cx,dx,si,di,bp,sp,ip,cs,ds,ss,es,flags,next,dummy ; 0, 2, 4, 6, 8,10,12,14,16,18,20,22,24, 26 , 28 , 30 pcb: times 32*16 dw 0 ; space for 32 PCBs stack: times 32*256 dw 0 ; space for 32 512 byte stacks nextpcb: dw 1 ; index of next free pcb current: dw 0 ; index of current pcb lineno: dw 0 ; line number for next thread ;;;;; COPY LINES 028-071 FROM EXAMPLE 10.1 (printnum) ;;;;; ; mytask subroutine to be run as a thread ; takes line number as parameter mytask: push bp mov bp, sp sub sp, 2 ; thread local variable push ax push bx mov ax, [bp+4] ; load line number parameter mov bx, 70 ; use column number 70 mov word [bp-2], 0 ; initialize local variable printagain: push ax ; line number push bx ; column number push word [bp-2] ; number to be printed call printnum ; print the number inc word [bp-2] ; increment the local variable jmp printagain ; infinitely print pop bx pop ax mov sp, bp pop bp ret ; subroutine to register a new thread ; takes the segment, offset, of the thread routine and a parameter ; for the target thread subroutine initpcb: push bp mov bp, sp push ax push bx push cx push si mov bx, [nextpcb] ; read next available pcb index cmp bx, 32 ; are all PCBs used je exit ; yes, exit mov cl, 5 shl bx, cl ; multiply by 32 for pcb start mov ax, [bp+8] ; read segment parameter mov [pcb+bx+18], ax ; save in pcb space for cs mov ax, [bp+6] ; read offset parameter mov [pcb+bx+16], ax ; save in pcb space for ip mov [pcb+bx+22], ds ; set stack to our segment mov si, [nextpcb] ; read this pcb index mov cl, 9 shl si, cl ; multiply by 512 add si, 256*2+stack ; end of stack for this thread mov ax, [bp+4] ; read parameter for subroutine sub si, 2 ; decrement thread stack pointer mov [si], ax ; pushing param on thread stack sub si, 2 ; space for return address mov [pcb+bx+14], si ; save si in pcb space for sp mov word [pcb+bx+26], 0x0200 ; initialize thread flags mov ax, [pcb+28] ; read next of 0th thread in ax mov [pcb+bx+28], ax ; set as next of new thread mov ax, [nextpcb] ; read new thread index mov [pcb+28], ax ; set as next of 0th thread inc word [nextpcb] ; this pcb is now used exit: pop si pop cx pop bx pop ax pop bp ret 6 ; timer interrupt service routine timer: push ds push bx push cs pop ds ; initialize ds to data segment mov bx, [current] ; read index of current in bx shl bx, 1 shl bx, 1 shl bx, 1 shl bx, 1 shl bx, 1 ; multiply by 32 for pcb start mov [pcb+bx+0], ax ; save ax in current pcb mov [pcb+bx+4], cx ; save cx in current pcb mov [pcb+bx+6], dx ; save dx in current pcb mov [pcb+bx+8], si ; save si in current pcb mov [pcb+bx+10], di ; save di in current pcb mov [pcb+bx+12], bp ; save bp in current pcb mov [pcb+bx+24], es ; save es in current pcb pop ax ; read original bx from stack mov [pcb+bx+2], ax ; save bx in current pcb pop ax ; read original ds from stack mov [pcb+bx+20], ax ; save ds in current pcb pop ax ; read original ip from stack mov [pcb+bx+16], ax ; save ip in current pcb pop ax ; read original cs from stack mov [pcb+bx+18], ax ; save cs in current pcb pop ax ; read original flags from stack mov [pcb+bx+26], ax ; save cs in current pcb mov [pcb+bx+22], ss ; save ss in current pcb mov [pcb+bx+14], sp ; save sp in current pcb mov bx, [pcb+bx+28] ; read next pcb of this pcb mov [current], bx ; update current to new pcb mov cl, 5 shl bx, cl ; multiply by 32 for pcb start mov cx, [pcb+bx+4] ; read cx of new process mov dx, [pcb+bx+6] ; read dx of new process mov si, [pcb+bx+8] ; read si of new process mov di, [pcb+bx+10] ; read diof new process mov bp, [pcb+bx+12] ; read bp of new process mov es, [pcb+bx+24] ; read es of new process mov ss, [pcb+bx+22] ; read ss of new process mov sp, [pcb+bx+14] ; read sp of new process push word [pcb+bx+26] ; push flags of new process push word [pcb+bx+18] ; push cs of new process push word [pcb+bx+16] ; push ip of new process push word [pcb+bx+20] ; push ds of new process mov al, 0x20 out 0x20, al ; send EOI to PIC mov ax, [pcb+bx+0] ; read ax of new process mov bx, [pcb+bx+2] ; read bx of new process pop ds ; read ds of new process iret ; return to new process start: xor ax, ax mov es, ax ; point es to IVT base cli mov word [es:8*4], timer mov [es:8*4+2], cs ; hook timer interrupt sti nextkey: xor ah, ah ; service 0 – get keystroke int 0x16 ; bios keyboard services push cs ; use current code segment mov ax, mytask push ax ; use mytask as offset push word [lineno] ; thread parameter call initpcb ; register the thread inc word [lineno] ; update line number jmp nextkey ; wait for next keypress |

When the program is executed the threads display the numbers independently. However as keys are pressed and new threads are registered, there is an obvious slowdown in the speed of multitasking. To improve that, we can change the timer interrupt frequency. The following can be used to set to an approximately 1ms interval.

mov  ax, 1100
out  0x40, al
mov  al, ah
out  0x40, al

This makes the threads look faster. However the only real change is that the timer interrupt is now coming more frequently.