lESSON nO.33

BIOS Video Services

The Basic Input Output System (BIOS) provides services for video, keyboard, serial port, parallel port, time etc. The video services are exported via INT 10. We will discuss some very simple services. Video services are classified into two broad categories; graphics mode services and text mode services. In graphics mode a location in video memory corresponds to a dot on the screen. In text mode this relation is not straightforward. The video memory holds the ASCII of the character to be shown and the actual shape is read from a font definition stored elsewhere in memory. We first present a list of common video services used in text mode.

INT 10 - VIDEO - SET VIDEO MODE

AH = 00h

AL = desired video mode

Some common video modes include 40x25 text mode (mode 0), 80x25 text mode (mode 2), 80x50 text mode (mode 3), and 320x200 graphics mode (mode D).

INT 10 - VIDEO - SET TEXT-MODE CURSOR SHAPE

AH = 01h

CH = cursor start and options

CL = bottom scan line containing cursor (bits 0-4)

INT 10 - VIDEO - SET CURSOR POSITION

AH = 02h

BH = page number

0-3 in modes 2&3

0-7 in modes 0&1

0 in graphics modes

DH = row (00h is top)

DL = column (00h is left)

INT 10 - VIDEO - SCROLL UP WINDOW

AH = 06h

AL = number of lines by which to scroll up (00h = clear entire window)

BH = attribute used to write blank lines at bottom of window

CH, CL = row, column of window's upper left corner

DH, DL = row, column of window's lower right corner

INT 10 - VIDEO - SCROLL DOWN WINDOW

AH = 07h

AL = number of lines by which to scroll down (00h=clear entire window)

BH = attribute used to write blank lines at top of window

CH, CL = row, column of window's upper left corner

DH, DL = row, column of window's lower right corner

INT 10 - VIDEO - WRITE CHARACTER AND ATTRIBUTE AT CURSOR POSITION

AH = 09h

AL = character to display

BH = page number

BL = attribute (text mode) or color (graphics mode)

CX = number of times to write character

INT 10 - VIDEO - WRITE CHARACTER ONLY AT CURSOR POSITION

AH = 0Ah

AL = character to display

BH = page number

BL = attribute (text mode) or color (graphics mode)

CX = number of times to write character

INT 10 - VIDEO - WRITE STRING

AH = 13h

AL = write mode

bit 0: update cursor after writing

bit 1: string contains alternating characters and attributes

bits 2-7: reserved (0)

BH = page number

BL = attribute if string contains only characters

CX = number of characters in string

DH, DL = row, column at which to start writing

ES:BP -> string to write

## Chargen Services

In our first example we will read the font definition in memory and change it to include a set of all on pixels in the last line showing an effect of underline on all character including space. An 8x16 font is stored in 16 bytes. A sample character and the corresponding 16 values stored in the font information are shown for the character ‘A’. We start with two services from the chargen subset of video services that we are going to use.

INT 10 - VIDEO - GET FONT INFORMATION
AX = 1130h

BH = pointer specifier

Return:

ES:BP = specified pointer

CX = bytes/character of on-screen font

DL = highest character row on screen

INT 10 - TEXT-MODE CHARGEN

AX = 1110h

ES:BP -> user table

CX = count of patterns to store

DX = character offset into map 2 block

BL = block to load in map 2

BH = number of bytes per character pattern

We will use 6 as the pointer specifier which means the 8x16 font stored in ROM.

|  | Example 12.1 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 | ; put underlines on screen font [org 0x0100] jmp start font: times 256*16 db 0 ; space for font start: mov ax, 0x1130 ; service 11/30 – get font info mov bx, 0x0600 ; ROM 8x16 font int 0x10 ; bios video services mov si, bp ; point si to rom font data mov di, font ; point di to space for font mov cx, 256*16 ; font size push ds push es pop ds ; ds:si to rom font data pop es ; es:di to space for font cld ; auto increment mode rep movsb ; copy font push cs pop ds ; restore ds to data segment mov si, font-1 ; point si before first char mov cx, 0x100 ; total 256 characters change: add si, 16 ; one character has 16 bytes mov byte [si], 0xFF ; change last line to all ones loop change ; repeat for each character mov bp, font ; es:bp points to new font mov bx, 0x1000 ; bytes per char & block number mov cx, 0x100 ; number of characters to change xor dx, dx ; first character to change mov ax, 0x1110 ; service 11/10 – load user font int 0x10 ; bios video services mov ax, 0x4c00 ; terminate program int 0x21 |

Our second example is similar to the last example however in this case we are doing something funny on the screen. We are reversing the shapes of all the characters on the screen.

|  | Example 12.2 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 | ; reverse each character of screen font [org 0x0100] jmp start font: times 256*16 db 0 ; space for font start: mov ax, 0x1130 ; service 11/30 – get font info mov bx, 0x0600 ; ROM 8x16 font int 0x10 ; bios video services mov si, bp ; point si to rom font data mov di, font ; point di to space for font mov cx, 256*16 ; font size push ds push es pop ds ; ds:si to rom font data pop es ; es:di to space for font cld ; auto increment mode rep movsb ; copy font push cs pop ds ; restore ds to data segment mov si, font ; point si to start of font change: mov al, [si] ; read one byte mov cx, 8 inner: shl al, 1 ; shift left with MSB in carry rcr bl, 1 ; rotate right using carry loop inner ; repeat eight times mov [si], bl ; write back reversed byte inc si ; next byte of font cmp si, font+256*16 ; is whole font reversed jne change ; no, reverse next byte mov bp, font ; es:bp points to new font mov bx, 0x1000 ; bytes per char & block number mov cx, 0x100 ; number of characters to change xor dx, dx ; first character to change mov ax, 0x1110 ; service 11/10 – load user font int 0x10 ; bios video services mov ax, 0x4c00 ; terminate program int 0x21 |

## Graphics Mode Services

We will take an example of using graphics mode video services as well. We will draw a line across the screen using the following service.

INT 10 - VIDEO - WRITE GRAPHICS PIXEL

AH = 0Ch

BH = page number

AL = pixel color

CX = column

DX = row

|  | Example 12.3 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 | ; draw line in graphics mode [org 0x0100] mov ax, 0x000D ; set 320x200 graphics mode int 0x10 ; bios video services mov ax, 0x0C07 ; put pixel in white color xor bx, bx ; page number 0 mov cx, 200 ; x position 200 mov dx, 200 ; y position 200 l1: int 0x10 ; bios video services dec dx ; decrease y position loop l1 ; decrease x position and repeat mov ah, 0 ; service 0 – get keystroke int 0x16 ; bios keyboard services mov ax, 0x0003 ; 80x25 text mode int 0x10 ; bios video services mov ax, 0x4c00 ; terminate program int 0x21 |