Lesson no.35

Storage Access Using BIOS

We will be using BIOS disk services to directly see the data stored in the directory entries by DOS. For this purpose we will be using the BIOS disk services.

INT 13 - DISK - RESET DISK SYSTEM

AH = 00h

DL = drive

Return:

CF = error flag

AH = error code

INT 13 - DISK - READ SECTOR(S) INTO MEMORY

AH = 02h

AL = number of sectors to read (must be nonzero)

CH = low eight bits of cylinder number

CL = sector number 1-63 (bits 0-5)

high two bits of cylinder (bits 6-7, hard disk only)

DH = head number

DL = drive number (bit 7 set for hard disk)

ES:BX -> data buffer

Return:

CF = error flag

AH = error code

AL = number of sectors transferred

INT 13 - DISK - WRITE DISK SECTOR(S)

AH = 03h

AL = number of sectors to write (must be nonzero)

CH = low eight bits of cylinder number

CL = sector number 1-63 (bits 0-5)

high two bits of cylinder (bits 6-7, hard disk only)

DH = head number

DL = drive number (bit 7 set for hard disk)

ES:BX -> data buffer

Return:

CF = error flag

AH = error code

AL = number of sectors transferred

INT 13 - DISK - GET DRIVE PARAMETERS

AH = 08h

DL = drive (bit 7 set for hard disk)

Return:

CF = error flag

AH = error code

CH = low eight bits of maximum cylinder number

CL = maximum sector number (bits 5-0)

high two bits of maximum cylinder number (bits 7-6)

DH = maximum head number

DL = number of drives

ES:DI -> drive parameter table (floppies only)

|  | Example 13.1 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 | ; floppy directory using bios services [org 0x0100] jmp start sector: times 512 db 0 ; space for directory sector entryname: times 11 db 0 ; space for a file name db 10, 13, '$' ; new line and terminating $ start: mov ah, 0 ; service 0 – reset disk system mov dl, 0 ; drive A: int 0x13 ; bios disk services jc error ; if error, terminate program mov ah, 2 ; service 2 – read sectors mov al, 1 ; count of sectors mov ch, 0 ; cyliner mov cl, 2 ; sector mov dh, 1 ; head mov dl, 0 ; drive A: mov bx, sector ; buffer to read sector int 0x13 ; bios disk services jc error ; if error, terminate program mov bx, 0 ; start from first entry nextentry: mov di, entryname ; point di to space for filename mov si, sector ; point si to sector add si, bx ; move ahead to desired entry mov cx, 11 ; one filename is 11 bytes long cld ; auto increment mode rep movsb ; copy filename mov ah, 9 ; service 9 – output string mov dx, entryname ; filename to be printed int 0x21 ; dos services add bx, 32 ; point to next dir entry cmp bx, 512 ; is last entry in this sector jne nextentry ; no, print next entry error: mov ax, 0x4c00 ; terminate program int 0x21 |

With the given services and the bits allocated for heads, tracks, and sectors only 8GB disks can be accessed. This limitation can be overcome by using INT 13 extensions that take a linear 64bit sector number and handle all the head, track, sector conversion themselves. The important services in this category are listed below.

INT 13 - INT 13 Extensions - EXTENDED READ

AH = 42h

DL = drive number

DS:SI -> disk address packet

Return:

CF = error flag

AH = error code

disk address packet's block count field set to number of blocks

successfully transferred

INT 13 - INT 13 Extensions - EXTENDED WRITE

AH = 43h

AL = write flags

DL = drive number

DS:SI -> disk address packet

Return:

CF = error flag

AH = error code

disk address packet's block count field set to number of blocks

successfully transferred

The format of the disk address packet used above is as follows.

Offset	Size	Description

00h	BYTE	size of packet = 10h

01h	BYTE	reserved (0)

02h	WORD	number of blocks to transfer

04h	DWORD	-> transfer buffer

08h	QWORD	starting absolute block number

Hard disks have a different formation from floppy disks in that there is a partition table at the start that allows several logical disks to be maintained within a single physical disk. The physical sector 0 holds the master boot record and a partition table towards the end. The first 446 bytes contain MBR, then there are 4 16 byte partition entries and then there is a 2 byte signature. A partition table entry has the following format.

Byte 0 – 0x80 for active 0x00 for inactive

Byte 1-3 – Starting CHS

Byte 4 – Partition Type

Byte 5-7 – Ending CHS

Byte 8-B – Starting LBA

Byte C-F – Size of Partition

Some important partition types are listed below.

00 Unused Entry

01 FAT12

05 Extended Partition

06 FAT16

0b FAT32

0c FAT32 LBA

0e FAT16 LBA

0f Extended LBA

07 NTFS

Extended partition type signals that the specified area is treated as a complete hard disk with its own partition table and partitions. Therefore extended partitions allow a recursion in partitioning and consequently an infinite number of partitions are possible. The following program reads the partition tables (primary and extended) using recursion and displays in an indented form all partitions present on the first hard disk in the system.

|  | Example 13.2 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009-026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 106 107 108 109 110 111 112 113 114 115 116 117 118 119 120 121 123 124 125 126 127 128 129 130 131 132 133 134 135 136 137 138 139 140 141 142 143 144 145 146 147 148 149 150 151 152 153 154 155 156 157 158 159 160 161 162 163 164 165 166 167 168 169 170 171 172 173 174 175 176 177 178 179 180 181 182 183 184 185 186 187 188 189 190 191 192 193 194 195 196 197 198 199 200 201 202 203 204 205 206 207 208 209 210 211 212 213 214 215 216 217 218 219 | ; a program to display the partition table [org 0x0100] jmp start dap: db 0x10, 0 ; disk address packet dw 1 dd 0, 0, 0 msg: times 17 db ' ' db 10, 13, '$' fat12: db 'FAT12...$' fat16: db 'FAT16...$' fat32: db 'FAT32...$' ntfs: db 'NTFS....$' extended: db 'EXTEND..$' unknown: db 'UNKNOWN.$' partypes: dw 0x1, fat12 ; table of known partition types dw 0x5, extended dw 0x6, fat16 dw 0xe, fat16 dw 0xb, fat32 dw 0xc, fat32 dw 0x7, ntfs dw 0xf, extended dw 0x0, unknown ; subroutine to print a number in a string as hex ; takes address of string and a 16bit number as parameter printnum: push bp mov bp, sp push ax push bx push cx push dx push di mov di, [bp+6] ; string to store the number add di, 3 mov ax, [bp+4] ; load number in ax mov bx, 16 ; use base 16 for division mov cx, 4 nextdigit: mov dx, 0 div bx ; divide by 16 add dl, 0x30 ; convert into ascii value cmp dl, 0x39 jbe skipalpha add dl, 7 skipalpha: mov [di], dl ; update char in string dec di loop nextdigit pop di pop dx pop cx pop bx pop ax pop bp ret 4 ; subroutine to print the start and end of a partition ; takes the segment and offset of the partition table entry printpart: push bp mov bp, sp push es push ax push di les di, [bp+4] ; point es:di to dap mov ax, msg push ax push word [es:di+0xA] call printnum ; print first half of start add ax, 4 push ax push word [es:di+0x8] call printnum ; print second half of start add ax, 5 push ax push word [es:di+0xE] call printnum ; print first half of end add ax, 4 push ax push word [es:di+0xC] call printnum ; print second half of end mov dx, msg mov ah, 9 int 0x21 ; print the whole on the screen pop di pop ax pop es pop bp ret 4 ; recursive subroutine to read the partition table ; take indentation level and 32bit absolute block number as parameters readpart: push bp mov bp, sp sub sp, 512 ; local space to read sector push ax push bx push cx push dx push si mov ax, bp sub ax, 512 mov word [dap+4], ax ; init dest offset in dap mov [dap+6], ds ; init dest segment in dap mov ax, [bp+4] mov [dap+0x8], ax ; init sector no in dap mov ax, [bp+6] mov [dap+0xA], ax ; init second half of sector no mov ah, 0x42 ; read sector in LBA mode mov dl, 0x80 ; first hard disk mov si, dap ; address of dap int 0x13 ; int 13 jc failed ; if failed, leave mov si, -66 ; start of partition info nextpart: mov ax, [bp+4] ; read relative sector number add [bp+si+0x8], ax ; make it absolute mov ax, [bp+6] ; read second half adc [bp+si+0xA], ax ; make seconf half absolute cmp byte [bp+si+4], 0 ; is partition unused je exit mov bx, partypes ; point to partition types mov di, 0 nextmatch: mov ax, [bx+di] cmp [bp+si+4], al ; is this partition known je found ; yes, so print its name add di, 4 ; no, try next entry in table cmp di, 32 ; are all entries compared jne nextmatch ; no, try another found: mov cx, [bp+8] ; load indentation level jcxz noindent ; skip if no indentation needed indent: mov dl, ' ' mov ah, 2 ; display char service int 0x21 ; dos services loop indent ; print required no of spaces noindent: add di, 2 mov dx, [bx+di] ; point to partition type name mov ah, 9 ; print string service int 0x21 ; dos services push ss mov ax, bp add ax, si push ax ; pass partition entry address call printpart ; print start and end from it cmp byte [bp+si+4], 5 ; is it an extended partition je recurse ; yes, make a recursive call cmp byte [bp+si+4], 0xf ; is it an extended partition jne exit ; yes, make a recursive call recurse: mov ax, [bp+8] add ax, 2 ; increase indentation level push ax push word [bp+si+0xA] ; push partition type address push word [bp+si+0x8] call readpart ; recursive call exit: add si, 16 ; point to next partition entry cmp si, -2 ; gone past last entry jne nextpart ; no, read this entry failed: pop si pop dx pop bx pop cx pop ax mov sp, bp pop bp ret 6 start: xor ax, ax push ax ; start from zero indentation push ax ; main partition table at 0 push ax call readpart ; read and print it mov ax, 0x4c00 ; terminate program int 0x21 |