Lesson no.36

Storage Access using DOS

BIOS provides raw access to the storage medium while DOS gives a more logical view and more cooked services. Everything is a file. A directory is a specially organized file that is interpreted by the operating system itself. A list of important DOS services for file manipulation is given below.

INT 21 - CREATE OR TRUNCATE FILE

AH = 3Ch

CX = file attributes

DS:DX -> ASCIZ filename

Return:

CF = error flag

AX = file handle or error code

INT 21 - OPEN EXISTING FILE

AH = 3Dh

AL = access and sharing modes

DS:DX -> ASCIZ filename

CL = attribute mask of files to look for (server call only)

Return:

CF = error flag

AX = file handle or error code

INT 21 - CLOSE FILE

AH = 3Eh

BX = file handle

Return:

CF = error flag

AX = error code

INT 21 - READ FROM FILE

AH = 3Fh

BX = file handle

CX = number of bytes to read

DS:DX -> buffer for data

Return:

CF = error flag

AX = number of bytes actually read or error code

INT 21 - WRITE TO FILE

AH = 40h

BX = file handle

CX = number of bytes to write

DS:DX -> data to write

Return:

CF = error flag

AX = number of bytes actually written or error code

INT 21 - DELETE FILE

AH = 41h

DS:DX -> ASCIZ filename (no wildcards, but see notes)

Return:

CF = error flag

AX = error code

INT 21 - SET CURRENT FILE POSITION

AH = 42h

AL = origin of move

BX = file handle

CX:DX = offset from origin of new file position

Return:

CF = error flag

DX:AX = new file position in bytes from start of file

AX = error code in case of error

INT 21 - GET FILE ATTRIBUTES

AX = 4300h

DS:DX -> ASCIZ filename

Return:

CF = error flag

CX = file attributes

AX = error code

INT 21 - SET FILE ATTRIBUTES

AX = 4301h

CX = new file attributes

DS:DX -> ASCIZ filename

Return:

CF = error flag

AX = error code

We will use some of these services to find that two files are same in contents or different. We will read the file names from the command prompt. The command string is passed to the program in the program segment prefix located at offset 0 in the current segment. The area from 0-7F contains information for DOS, while the command tail length is stored at 80. From 81 to FF, the actual command tail is stored terminated by a CR (Carriage Retrun).

|  | Example 13.3 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 106 107 108 109 110 111 112 113 114 115 116 117 | ; file comparison using dos services [org 0x0100] jmp start filename1: times 128 db 0 ; space for first filename filename2: times 128 db 0 ; space for second filename handle1: dw 0 ; handle for first file handle2: dw 0 ; handle for second file buffer1: times 4096 db 0 ; buffer for first file buffer2: times 4096 db 0 ; buffer for second file format: db 'Usage error: diff <filename1> <filename2>$' openfailed: db 'First file could not be opened$' openfailed2: db 'Second file could not be opened$' readfailed: db 'First file could not be read$' readfailed2: db 'Second file could not be read$' different: db 'Files are different$' same: db 'Files are same$' start: mov ch, 0 mov cl, [0x80] ; command tail length in cx dec cx ; leave the first space mov di, 0x82 ; start of command tail in di mov al, 0x20 ; space for parameter separation cld ; auto increment mode repne scasb ; search space je param2 ; if found, proceed mov dx, format ; else, select error message jmp error ; proceed to error printing param2: push cx ; save original cx mov si, 0x82 ; set si to start of param mov cx, di ; set di to end of param sub cx, 0x82 ; find param size in cx dec cx ; excluding the space mov di, filename1 ; set di to space for filename 1 rep movsb ; copy filename there mov byte [di], 0 ; terminate filename with 0 pop cx ; restore original cx inc si ; go to start of next filename mov di, filename2 ; set di to space for filename 2 rep movsb ; copy filename there mov byte [di], 0 ; terminate filename with 0 mov ah, 0x3d ; service 3d – open file mov al, 0 ; readonly mode mov dx, filename1 ; address of filename int 0x21 ; dos services jnc open2 ; if no error, proceed mov dx, openfailed ; else, select error message jmp error ; proceed to error printing open2: mov [handle1], ax ; save handle for first file mov ah, 0x3d ; service 3d – open file mov al, 0 ; readonly mode mov dx, filename2 ; address of filename int 0x21 ; dos services jnc store2 ; if no error, proceed mov dx, openfailed2 ; else, select error message jmp error ; proceed to error printing store2: mov [handle2], ax ; save handle for second file readloop: mov ah, 0x3f ; service 3f – read file mov bx, [handle1] ; handle for file to read mov cx, 4096 ; number of bytes to read mov dx, buffer1 ; buffer to read in int 0x21 ; dos services jnc read2 ; if no error, proceed mov dx, readfailed ; else, select error message jmp error ; proceed to error printing read2: push ax ; save number of bytes read mov ah, 0x3f ; service 3f – read file mov bx, [handle2] ; handle for file to read mov cx, 4096 ; number of bytes to read mov dx, buffer2 ; buffer to read in int 0x21 ; dos services jnc check ; if no error, proceed mov dx, readfailed2 ; else, select error message jmp error ; proceed to error printing check: pop cx ; number of bytes read of file 1 cmp ax, cx ; are number of byte same je check2 ; yes, proceed to compare them mov dx, different ; no, files are different jmp error ; proceed to message printing check2: test ax, ax ; are zero bytes read jnz compare ; no, compare them mov dx, same ; yes, files are same jmp error ; proceed to message printing compare: mov si, buffer1 ; point si to file 1 buffer mov di, buffer2 ; point di to file 2 buffer repe cmpsb ; compare the two buffers je check3 ; if equal, proceed mov dx, different ; else, files are different jmp error ; proceed to message printing check3: cmp ax, 4096 ; were 4096 bytes read je readloop ; yes, try to read more mov dx, same ; no, files are same error: mov ah, 9 ; service 9 – output message int 0x21 ; dos services mov ah, 0x3e ; service 3e – close file mov bx, [handle1] ; handle of file to close int 0x21 ; dos services mov ah, 0x3e ; service 3e – close file mov bx, [handle2] ; handle of file to close int 0x21 ; dos services mov ax, 0x4c00 ; terminate program int 0x21 |

Another interesting service that DOS provides regarding files is executing them. An important point to understand here is that whenever a program is executed in DOS all available memory is allocated to it. No memory is available to execute any new programs. Therefore memory must be freed using explicit calls to DOS for this purpose before a program is executed. Important services in this regard are listed below.

INT 21 - ALLOCATE MEMORY

AH = 48h

BX = number of paragraphs to allocate

Return:

CF = error flag

AX = segment of allocated block or error code in case of error

BX = size of largest available block in case of error

INT 21 - FREE MEMORY

AH = 49h

ES = segment of block to free

Return:

CF = error flag

AX = error code

INT 21 - RESIZE MEMORY BLOCK

AH = 4Ah

BX = new size in paragraphs

ES = segment of block to resize

Return:

CF = error flag

AX = error code

BX = maximum paragraphs available for specified memory block

INT 21 - LOAD AND/OR EXECUTE PROGRAM

AH = 4Bh

AL = type of load (0 = load and execute)

DS:DX -> ASCIZ program name (must include extension)

ES:BX -> parameter block

Return:

CF = error flag

AX = error code

The format of parameter block is as follows.

Offset	Size	Description

00h	WORD	segment of environment to copy for child process

(copy caller's environment if 0000h)

02h	DWORD	pointer to command tail to be copied into child's PSP

06h	DWORD	pointer to first FCB to be copied into child's PSP

0Ah	DWORD	pointer to second FCB to be copied into child's PSP

0Eh	DWORD	(AL=01h) will hold subprogram's initial SS:SP on return

12h	DWORD	(AL=01h) will hold entry point (CS:IP) on return

As an example we will use the multitasking kernel client from the multitasking chapter and modify it such that after running all three threads it executes a new instance of the command prompt instead of indefinitely hanging around.

|  | Example 13.4 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019-062 063-104 104-127 128-146 147-192 193 194 195 196 197 198 199 200 201 202 203 204 205 206 207 208 209 210 211 212 213 214 215 216 217 218 219 220 221 222 223 224 225 226 227 228 229 230 231 232 233 234 | ; another multitasking TSR caller [org 0x0100] jmp start ; parameter block layout: ; cs,ip,ds,es,param ; 0, 2, 4, 6, 8 paramblock: times 5 dw 0 ; space for parameters lineno: dw 0 ; line number for next thread chars: db '\¦/-' ; chracters for rotating bar message: db 'moving hello' ; moving string message2: db ' ' ; to erase previous string messagelen: dw 12 ; length of above strings tail: db ' ',13 command: db 'COMMAND.COM', 0 execblock: times 11 dw 0 ;;;;; COPY LINES 028-071 FROM EXAMPLE 10.1 (printnum) ;;;;; ;;;;; COPY LINES 073-114 FROM EXAMPLE 10.1 (printstr) ;;;;; ;;;;; COPY LINES 103-126 FROM EXAMPLE 11.5 (mytask) ;;;;; ;;;;; COPY LINES 128-146 FROM EXAMPLE 11.5 (mytask2) ;;;;; ;;;;; COPY LINES 148-193 FROM EXAMPLE 11.5 (mytask3) ;;;;; start: mov [paramblock+0], cs ; code segment parameter mov word [paramblock+2], mytask ; offset parameter mov [paramblock+4], ds ; data segment parameter mov [paramblock+6], es ; extra segment parameter mov word [paramblock+8], 0 ; parameter for thread mov si, paramblock ; address of param block in si int 0x80 ; multitasking kernel interrupt mov [paramblock+0], cs ; code segment parameter mov word [paramblock+2], mytask2 ; offset parameter mov [paramblock+4], ds ; data segment parameter mov [paramblock+6], es ; extra segment parameter mov word [paramblock+8], 0 ; parameter for thread mov si, paramblock ; address of param block in si int 0x80 ; multitasking kernel interrupt mov [paramblock+0], cs ; code segment parameter mov word [paramblock+2], mytask3 ; offset parameter mov [paramblock+4], ds ; data segment parameter mov [paramblock+6], es ; extra segment parameter mov word [paramblock+8], 0 ; parameter for thread mov si, paramblock ; address of param block in si int 0x80 ; multitasking kernel interrupt mov ah, 0x4a ; service 4a – resize memory mov bx, end ; end of memory retained add bx, 15 ; rounding up mov cl, 4 shr bx, cl ; converting into paras int 0x21 ; dos services mov ah, 0x4b ; service 4b - exec mov al, 0 ; load and execute mov dx, command ; command to be executed mov bx, execblock ; address of execblock mov word [bx+2], tail ; offset of command tail mov [bx+4], ds ; segment of command tail int 0x21 ; dos services jmp $ ; loop infinitely if returned end: |