Lesson no.37

Device Drivers

Device drivers are operating system extensions that become part of the operating system and extend its services to new devices. Device drivers in DOS are very simple. They just have their services exposed through the file system interface.

Device driver file starts with a header containing a link to the next driver in the first four bytes followed by a device attribute word. The most important bit in the device attribute word is bit 15 which dictates if it is a character device or a block device. If the bit is zero the device is a character device and otherwise a block device. Next word in the header is the offset of a strategy routine, and then is the offset of the interrupt routine and then in one byte, the number of units supported is stored. This information is padded with seven zeroes.

Strategy routine is called whenever the device is needed and it is passed a request header. Request header stores the unit requested, the command code, space for return value and buffer pointers etc. Important command codes include 0 to initialize, 1 to check media, 2 to build a BIOS parameter block, 4 and 8 for read and write respectively. For every command the first 13 bytes of request header are same.

RH+0	BYTE		Length of request header

RH+1	BYTE		Unit requested

RH+2	BYTE		Command code

RH+3	BYTE		Driver’s return code

RH+5	9 BYTES	Reserved

The request header details for different commands is listed below.

0 – Driver Initialization

Passed to driver

RH+18	DWORD	Pointer to character after equal sign on CONFIG.SYS line that loaded driver (read-only)

RH+22	BYTE	Drive number for first unit of this block driver (0=A...)

Return from driver

RH+13	BYTE	Number of units (block devices only)

RH+14	DWORD 	Address of first free memory above driver (break address)

RH+18	DWORD	BPB pointer array (block devices only)

1 – Media Check

RH+13	BYTE	Media descriptor byte

Return

RH+14	BYTE	Media change code
			-1 if disk changed
			0 if dont know whether disk changed
			1 if disk not changed

RH+15	DWORD	pointer to previous volume label if device attrib bit 11=1 (open/close/removable media supported)

2 – Build BPB

RH+13	BYTE	Media descriptor byte

RH+14	DWORD 	buffer address (one sector)

Return

RH+18	DWORD	pointer to new BPB

if bit 13 (ibm format) is set buffer is first sector of fat, otherwise scrach space

4 – Read / 8 – Write / 9 – Write with verify

RH+13	BYTE 	Media descriptor byte

RH+14	DWORD 	transfer address

RH+18	WORD	byte or sector count

RH+20	WORD	starting sector number (for block devices)

Return

RH+18	WORD	actual byte or sectors transferred

RH+22	DWORD	pointer to volume label if error 0Fh is returned

The BIOS parameter block discussed above is a structure that provides parameters about the storage medium. It is stored in the first sector or the boot sector of the device. Its contents are listed below.

00-01	bytes per sector

02	sectors per allocation unit

03-04	Number of reserved sectors ( 0 based)

05	number of file allocation tables

06-07	max number of root directory entries

08-09	total number of sectors in medium

0A	media descriptor byte

0B-0C	number of sectors occupied by a single FAT

0D-0E	sectors per track (3.0 or later)

0F-10	number of heads (3.0 or later)

11-12	number of hidden sectors (3.0 or later)

13-14	high-order word of number of hidden sectors (4.0)

15-18	IF bytes 8-9 are zero, total number of sectors in medium

19-1E	Reserved should be zero

We will be building an example device driver that takes some RAM and expresses it as a secondary storage device to the operating system. Therefore a new drive is added and that can be browsed to, filed copied to and from just like ordinary drives expect that this drive is very fast as it is located in the RAM. This program cannot be directly executed since it is not a user program. This must be loaded by adding the line “device=filename.sys” in the “config.sys” file in the root directory.

|  | Example 13.5 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 106 107 108 109 110 111 112 113 114 115 116 117 118 119 120 121 122 123 | ; ram disk dos block device driver header: dd -1 ; no next driver dw 0x2000 ; driver attributes: block device dw strategy ; offset of strategy routine dw interrupt ; offset of interrupt routine db 1 ; no of units supported times 7 db 0 ; reserved request: dd 0 ; space for request header ramdisk: times 11 db 0 ; initial part of boot sector bpb: dw 512 ; bytes per sector db 1 ; sectors per cluster dw 1 ; reserved sectors db 1 ; fat copies dw 48 ; root dir entries dw 105 ; total sectors db 0xf8 ; media desc byte: fixed disk dw 1 ; sectors per fat times 482 db 0 ; remaining part of boot sector db 0xfe, 0xff, 0xff ; special bytes at start of FAT times 509 db 0 ; remaining FAT entries unused times 103*512 db 0 ; 103 sectors for data bpbptr: dw bpb ; array of bpb pointers dispatch: dw init ; command 0: init dw mediacheck ; command 1: media check dw getbpb ; command 2: get bpb dw unknown ; command 3: not handled dw input ; command 4: input dw unknown ; command 5: not handled dw unknown ; command 6: not handled dw unknown ; command 7: not handled dw output ; command 8: output dw output ; command 9: output with verify ; device driver strategy routine strategy: mov [cs:request], bx ; save request header offset mov [cs:request+2], es ; save request header segment retf ; device driver interrupt routine interrupt: push ax push bx push cx push dx push si push di push ds push es push cs pop ds les di, [request] mov word [es:di+3], 0x0100 mov bl, [es:di+2] mov bh, 0 cmp bx, 9 ja skip shl bx, 1 call [dispatch+bx] skip: pop es pop ds pop di pop si pop dx pop cx pop bx pop ax retf mediacheck: mov byte [es:di+14], 1 ret getbpb: mov word [es:di+18], bpb mov [es:di+20], ds ret input: mov ax, 512 mul word [es:di+18] mov cx, ax mov ax, 512 mul word [es:di+20] mov si, ax add si, ramdisk les di, [es:di+14] cld rep movsb ret output: mov ax, 512 mul word [es:di+18] mov cx, ax lds si, [es:di+14] mov ax, 512 mul word [es:di+20] mov di, ax add di, ramdisk push cs pop es cld rep movsb unknown: ret init: mov ah, 9 mov dx, message int 0x21 mov byte [es:di+13], 1 mov word [es:di+14], init mov [es:di+16], ds mov word [es:di+18], bpbptr mov [es:di+20], ds ret message: db 13, 10, 'RAM Disk Driver loaded',13,10,'$' |