Lesson no.38 (Serial port programming)

Introduction

Serial port is a way of communication among two devices just like the parallel port. The basic difference is that whole bytes are sent from one place to another in case of parallel port while the bits are sent one by one on the serial port in a specially formatted fashion. The serial port connection is a 9pin DB-9 connector with pins assigned as shown below.

We have made a wire that connects signal ground of the two connectors, the TD of one to the RD of the other and the RD of one to the TD of the other. This three wire connection is sufficient for full duplex serial communication. The data on the serial port is sent in a standard format called RS232 communication. The data starts with a 1 bit called the start bit, then five to eight data bits, an optional parity bit, and one to two 0 bits called stop bits. The number of data bits, parity bits, and the number of stop bits have to be configured at both ends. Also the duration of a bit must be precisely known at both ends called the baud rate of the communication.

The BIOS INT 14 provides serial port services. We will use a mix of BIOS services and direct port access for our example. A major limitation in using BIOS is that it does not allows interrupt driven data transfer, i.e. we are interrupted whenever a byte is ready to be read or a byte can be transferred since the previous transmission has completed. To achieve this we have to resort to direct port access. Important BIOS services regarding the serial port are discussed below.

INT 14 - SERIAL - INITIALIZE PORT

AH = 00h

AL = port parameters

DX = port number (00h-03h)

Return:

AH = line status

AL = modem status

Every bit of line status conveys different information. From most significant to least significant, the meanings are timeout, transmitter shift register empty, transmitter holding register empty, break detect, receiver ready, overrun, parity error, and framing error. Modem status is not used in direct serial communication. The port parameters in AL consist of the baud rate, parity scheme, number of stop bits, and number of data bits. The description of various bits is as under.

INT 14 - SERIAL - WRITE CHARACTER TO PORT

AH = 01h

AL = character to write

DX = port number (00h-03h)

Return:

AH bit 7 = error flag

AH bits 6-0 = port status

INT 14 - SERIAL - READ CHARACTER FROM PORT

AH = 02h

DX = port number (00h-03h)

Return:

AH = line status

AL = received character if AH bit 7 clear

INT 14 - SERIAL - GET PORT STATUS

AH = 03h

DX = port number (00h-03h)

Return:

AH = line status

AL = modem status

Serial port is also accessible via I/O ports. COM1 is accessible via ports 3F8-3FF while COM2 is accessible via 2F8-2FF. The first register at 3F8 (or 2F8 for the other port) is the transmitter holding register if written to and the receiver buffer register if read from. Other registers of our interest include 3F9 whose bit 0 must be set to enable received data available interrupt and bit 1 must be set to enable transmitter holding register empty interrupt. Bit 0 of 3FA is set if an interrupt is pending and its bits 1-3 identify the cause of the interrupt. The three bit causes are as follows.

110	(16550, 82510) timeout interrupt pending

101	(82510) timer interrupt

100	(82510) transmit machine

011	receiver line status interrupt. priority=highest

010	received data available register interrupt. priority=second

001	transmitter holding register empty interrupt. priority=third

000	modem status interrupt. priority=fourth

The register at 3FB is line control register while the one at 3FD is line status register. The line status register has the same bits as returned in line status by the get port status BIOS interrupt however the most significant bit is reserved in this case instead of signaling a timeout. The register at 3FC is the modem control register. Bit 3 of this register must be set to enable interrupt generation by the serial port.

Serial Communication

We give an example where two computers are connected using a serial cable made just as described above. The program is to be run on both computers. After that whatever is typed on one computer appears on the screen of the other.

|  | Example 14.1 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 | ; a program using serial port to transfer data back and forth [org 0x0100] jmp start screenpos: dw 0 ; where to display next character ; subroutine to clear the screen clrscr: push es push ax push cx push di mov ax, 0xb800 mov es, ax ; point es to video base xor di, di ; point di to top left column mov ax, 0x0720 ; space char in normal attribute mov cx, 2000 ; number of screen locations cld ; auto increment mode rep stosw ; clear the whole screen pop di pop cx pop ax pop es ret serial: push ax push bx push dx push es mov dx, 0x3FA ; interrupt identification register in al, dx ; read register and al, 0x0F ; leave lowerniblle only cmp al, 4 ; is receiver data available jne skipall ; no, leave interrupt handler mov dx, 0x3F8 ; data register in al, dx ; read character mov dx, 0xB800 mov es, dx ; point es to video memory mov bx, [cs:screenpos] ; get current screen position mov [es:bx], al ; write character on screen add word [cs:screenpos], 2 ; update screen position cmp word [cs:screenpos], 4000 ; is the screen full jne skipall ; no, leave interrupt handler call clrscr ; clear the screen mov word [cs:screenpos], 0 ; reset screen position skipall: mov al, 0x20 out 0x20, al ; end of interrupt pop es pop dx pop bx pop ax iret start: call clrscr ; clear the screen mov ah, 0 ; initialize port service mov al, 0xE3 ; line settings = 9600, 8, N, 1 xor dx, dx ; port = COM1 int 0x14 ; BIOS serial port services xor ax, ax mov es, ax ; point es to IVT base mov word [es:0x0C*4], serial mov [es:0x0C*4+2], cs ; hook serial port interrupt mov dx, 0x3FC ; modem control register in al, dx ; read register or al, 8 ; enable bit 3 (OUT2) out dx, al ; write back to register mov dx, 0x3F9 ; interrupt enable register in al, dx ; read register or al, 1 ; receiver data interrupt enable out dx, al ; write back to register in al, 0x21 ; read interrupt mask register and al, 0xEF ; enable IRQ 4 out 0x21, al ; write back to register main: mov ah, 0 ; read key service int 0x16 ; BIOS keybaord services push ax ; save key for later use retest: mov ah, 3 ; get line status xor dx, dx ; port = COM1 int 0x14 ; BIOS keyboard services and ah, 32 ; trasmitter holding register empty jz retest ; no, test again pop ax ; load saved key mov dx, 0x3F8 ; data port out dx, al ; send on serial port jmp main |

# Text boxes

1 – Carrier Detect (CD)

2 – Received Data (RD)

3 – Transmitted Data (TD)

4 – Data Terminal Ready (DTR)

5 – Signal Ground

6 – Data Set Ready (DSR)

7 – Request to Send (RTS)

8 – Clear to Send (CTS)

9 – Ring Indicator (RI)

7

6

5

4

3

2

1

0

baud rate

000-110

001-150

010-300

011-600

100-1200

101-2400

110-4800

111-9600

parity

00-N

10-N

01-O

11-E

data bits

00-5

01-6

10-7

11-8

stop bits

0-1

1-2