Lesson no. 39-43

Introduction

Till now we have been discussing the 8088 architecture which was a 16bit processor. Newer processors of the Intel series provide 32bit architecture. Till now we were in real mode of a newer processor which is basically a compatibility mode making the newer processor just a faster version of the original 8088. Switching processor in the newer 32bit mode is a very easy task. Just turn on the least significant bit of a new register called CR0 (Control Register 0) and the processor switches into 32bit mode called protected mode. However manipulations in the protected mode are very different from those in the read mode.

All registers in 386 have been extended to 32bits. The new names are EAX, EBX, ECX, EDX, ESI, EDI, ESP, EBP, EIP, and EFLAGS. The original names refer to the lower 16bits of these registers. A 32bit address register can access upto 4GB of memory so memory access has increased a lot.

As regards segment registers the scheme is not so simple. First of all we call them segment selectors instead of segment registers and they are still 16bits wide. We are also given two other segment selectors FS and GS for no specific purpose just like ES.

The working of segment registers as being multiplied by 10 and added into the offset for obtaining the physical address is totally changed. Now the selector is just an index into an array of segment descriptors where each descriptor describes the base, limit, and attributes of a segment. Role of selector is to select on descriptor from the table of descriptors and the role of descriptor is to define the actual base address. This decouples the selection and actual definition which is needed in certain protection mechanisms introduced into this processor. For example an operating system can define the possible descriptors for a program and the program is bound to select one of them and nothing else. This sentence also hints that the processor has some sense of programs that can or cannot do certain things like change this table of descriptors. This is called the privilege level of the program and varies for 0 (highest privilege) to 3 (lowest privilege). The format of a selector is shown below.

The table index (TI) is set to 0 to access the global table of descriptors called the GDT (Global Descriptor Table). It is set to 1 to access another table, the local descriptor table (LDT) that we will not be using. RPL is the requested privilege level that ranges from 0-3 and informs what privilege level the program wants when using this descriptor. The 13bit index is the actual index into the GDT to select the appropriate descriptor. 13 bits mean that a maximum of 8192 descriptors are possible in the GDT.

The GDT itself is an array of descriptors where each descriptor is an 8byte entry. The base and limit of GDT is stored in a 48bit register called the GDTR. This register is loaded with a special instruction LGDT and is given a memory address from where the 48bits are fetched. The first entry of the GDT must always be zero. It is called the null descriptor. After that any number of entries upto a maximum of 8191 can follow. The format of a code and data descriptor is shown below.

The 32bit base in both descriptors is scattered into different places because of compatibility reasons. The limit is stored in 20 bits but the G bit defines that the limit is in terms of bytes of 4K pages therefore a maximum of 4GB size is possible. The P bit must be set to signal that this segment is present in memory. DPL is the descriptor privilege level again related to the protection levels in 386. D bit defines that this segment is to execute code is 16bit mode or 32bit mode. C is conforming bit that we will not be using. R signals that the segment is readable. A bit is automatically set whenever the segment is accessed. The combination of S (system) and X (executable) tell that the descriptors is a code or a data descriptor. B (big) bit tells that if this data segment is used as stack SP is used or ESP is used.

Our first example is a very rudimentary one that just goes into protected mode and prints an A on the screen by directly accessing 000B8000.

|  | Example 15.1 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 | [org 0x0100] jmp start gdt: dd 0x00000000, 0x00000000 ; null descriptor dd 0x0000FFFF, 0x00CF9A00 ; 32bit code ; \--/\--/ \/¦¦¦¦\/ ; ¦ ¦ ¦ ¦¦¦¦+--- Base (16..23)=0 fill later ; ¦ ¦ ¦ ¦¦¦+--- X=1 C=0 R=1 A=0 ; ¦ ¦ ¦ ¦¦+--- P=1 DPL=00 S=1 ; ¦ ¦ ¦ ¦+--- Limit (16..19) = F ; ¦ ¦ ¦ +--- G=1 D=1 r=0 AVL=0 ; ¦ ¦ +--- Base (24..31) = 0 ; ¦ +--- Limit (0..15) = FFFF ; +--- Base (0..15)=0 fill later dd 0x0000FFFF, 0x00CF9200 ; data ; \--/\--/ \/¦¦¦¦\/ ; ¦ ¦ ¦ ¦¦¦¦+--- Base (16..23) = 0 ; ¦ ¦ ¦ ¦¦¦+--- X=0 E=0 W=1 A=0 ; ¦ ¦ ¦ ¦¦+--- P=1 DPL=00 S=1 ; ¦ ¦ ¦ ¦+--- Limit (16..19) = F ; ¦ ¦ ¦ +--- G=1 B=1 r=0 AVL=0 ; ¦ ¦ +--- Base (24..31) = 0 ; ¦ +--- Limit (0..15) = FFFF ; +--- Base (0..15) = 0 gdtreg: dw 0x17 ; 16bit limit dd 0 ; 32bit base (filled later) stack: times 256 dd 0 ; for use in p-mode stacktop: start: mov ax, 0x2401 int 0x15 ; enable A20 xor eax, eax mov ax, cs shl eax, 4 mov [gdt+0x08+2], ax shr eax, 16 mov [gdt+0x08+4], al ; fill base of code desc xor edx, edx mov dx, cs shl edx, 4 add edx, stacktop ; edx = stack top for p-mode xor eax, eax mov ax, cs shl eax, 4 add eax, gdt mov [gdtreg+2], eax ; fill phy base of gdt lgdt [gdtreg] ; load gdtr mov eax, cr0 or eax, 1 cli ; MUST disable interrupts mov cr0, eax ; P-MODE ON jmp 0x08:pstart ; load cs ;;;;; 32bit protected mode ;;;;; [bits 32] ; ask assembler to generate 32bit code pstart: mov eax, 0x10 mov ds, ax mov es, ax ; load other seg regs mov fs, ax ; flat memory model mov gs, ax mov ss, ax mov esp, edx mov byte [0x000b8000], 'A' ; direct poke at video jmp $ ; hang around |

Gate A20 is a workaround for a bug that is not detailed here. The BIOS call will simply enable it to open the whole memory for us. Another important thing is that the far jump we used loaded 8 into CS but CS is now a selector so it means Index=1, TI=0, and RPL=0 and therefore the actual descriptor loaded is the one at index 1 in the GDT.

32bit Programming

Our next example is to give a falvour of 32bit programming. We have written the printstr function for read and for protected mode. The availability of larger registers and flexible addressing rules allows writing a much comprehensive version of the code. Also offsets to parameters and default widths change.

|  | Example 15.2 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 106 107 108 109 110 111 112 113 114 115 116 117 118 119 120 121 123 124 125 126 127 128 129 130 131 132 133 134 135 136 137 138 139 140 141 142 143 144 145 146 147 148 149 150 133 134 135 136 137 138 139 140 141 142 143 144 145 146 | [org 0x0100] jmp start gdt: dd 0x00000000, 0x00000000 ; null descriptor dd 0x0000FFFF, 0x00CF9A00 ; 32bit code dd 0x0000FFFF, 0x00CF9200 ; data gdtreg: dw 0x17 ; 16bit limit dd 0 ; 32bit base rstring: db 'In Real Mode...', 0 pstring: db 'In Protected Mode...', 0 stack: times 256 dd 0 ; 1K stack stacktop: printstr: push bp ; real mode print string mov bp, sp push ax push cx push si push di push es mov di,[bp+4] ;load string address mov cx,0xffff ;load maximum possible size in cx xor al,al ;clear al reg repne scasb ;repeat scan mov ax,0xffff ; sub ax,cx ;calculate length dec ax ;off by one, as it includes zero mov cx,ax ;move length to counter mov ax, 0xb800 mov es, ax ; point es to video base mov ax,80 ;its a word move, clears ah mul byte [bp+8] ;its a byte mul to calc y offset add ax,[bp+10] ;add x offset shl ax,1 ;mul by 2 to get word offset mov di,ax ;load pointer mov si, [bp+4] ; string to be printed mov ah, [bp+6] ; load attribute cld ; set auto increment mode nextchar: lodsb ;load next char and inc si by 1 stosw ;store ax and inc di by 2 loop nextchar pop es pop di pop si pop cx pop ax pop bp ret 8 start: push byte 0 ; 386 can directly push immediates push byte 10 push byte 7 push word rstring call printstr mov ax, 0x2401 int 0x15 ; enable a20 xor eax, eax mov ax, cs shl eax, 4 mov [gdt+0x08+2], ax shr eax, 16 mov [gdt+0x08+4], al ; set base of code desc xor edx, edx mov dx, cs shl edx, 4 add edx, stacktop ; stacktop to be used in p-mode xor ebx, ebx mov bx, cs shl ebx, 4 add ebx, pstring ; pstring to be used in p-mode xor eax, eax mov ax, cs shl eax, 4 add eax, gdt mov [gdtreg+2], eax ; set base of gdt lgdt [gdtreg] ; load gdtr mov eax, cr0 or eax, 1 cli ; disable interrupts mov cr0, eax ; enable protected mode jmp 0x08:pstart ; load cs ;;;;; 32bit protected mode ;;;;; [bits 32] pprintstr: push ebp ; p-mode print string routine mov ebp, esp push eax push ecx push esi push edi mov edi, [ebp+8] ;load string address mov ecx, 0xffffffff ;load maximum possible size in cx xor al, al ;clear al reg repne scasb ;repeat scan mov eax, 0xffffffff ; sub eax, ecx ;calculate length dec eax ;off by one, as it includes zero mov ecx, eax ;move length to counter mov eax, 80 ;its a word move, clears ah mul byte [ebp+16] ;its a byte mul to calc y offset add eax, [ebp+20] ;add x offset shl eax, 1 ;mul by 2 to get word offset add eax, 0xb8000 mov edi, eax ;load pointer mov esi, [ebp+8] ; string to be printed mov ah, [ebp+12] ; load attribute cld ; set auto increment mode pnextchar: lodsb ;load next char and inc si by 1 stosw ;store ax and inc di by 2 loop pnextchar pop edi pop esi pop ecx pop eax pop ebp ret 16 ; 4 args now mean 16 bytes pstart: mov ax, 0x10 ; load all seg regs to 0x10 mov ds, ax ; flat memory model mov es, ax mov fs, ax mov gs, ax mov ss, ax mov esp, edx ; load saved esp on stack push byte 0 push byte 11 push byte 7 push ebx call pprintstr ; call p-mode print string routine mov eax, 0x000b8000 mov ebx, '/-\¦' nextsymbol: mov [eax], bl mov ecx, 0x00FFFFFF loop $ ror ebx, 8 jmp nextsymbol |

VESA Linear Frame Buffer

As an example of accessing a really large area of memory for which protected mode is a necessity, we will be accessing the video memory in high resolution and high color graphics mode where the necessary video memory is alone above a megabyte. We will be using the VESA VBE 2.0 for a standard for these high resolution modes.

VESA is the Video Electronics Standards Association and VBE is the set of Video BIOS Extensions proposed by them. The VESA VBE 2.0 standard includes a linear frame buffer mode that we will be using. This mode allows direct access to the whole video memory. Some important VESA services are listed below.

INT 10 – VESA – Get  SuperVGA Infromation

AX = 4F00h

ES:DI -> buffer for SuperVGA information

Return:

AL = 4Fh if function supported

AH = status

INT 10 – VESA – Get SuperVGA Mode Information

AX = 4F01h

CX = SuperVGA video mode

ES:DI -> 256-byte buffer for mode information

Return:

AL = 4Fh if function supported

AH = status

ES:DI filled if no error

INT 10 – VESA – Set VESA Video Mode

AX = 4F02h

BX = new video mode

Return:

AL = 4Fh if function supported

AH = status

One of the VESA defined modes is 8117 which is a 1024x768 mode with 16bit color and a linear frame buffer. The 16 color bits for every pixel are organized in 5:6:5 format with 5 bits for red, 6 for green, and 5 for blue. This makes 32 shades of red and blue and 64 shades of green and 64K total possible colors. The 32bit linear frame buffer base address is available at offset 28 in the mode information buffer. Our example will produces shades of green on the screen and clear them and again print them in an infinite loop with delays inbetween.

|  | Example 15.3 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 | [org 0x0100] jmp start modeblock: times 256 db 0 gdt: dd 0x00000000, 0x00000000 ; null descriptor dd 0x0000FFFF, 0x00CF9A00 ; 32bit code dd 0x0000FFFF, 0x00CF9200 ; data gdtreg: dw 0x17 ; 16bit limit dd 0 ; 32bit base stack: times 256 dd 0 ; 1K stack stacktop: start: mov ax, 0x4f01 ; get vesa mode information mov cx, 0x8117 ; 1024*768*64K linear frame buffer mov di, modeblock int 0x10 mov esi, [modeblock+0x28] ; save frame buffer base mov ax, 0x4f02 ; set vesa mode mov bx, 0x8117 int 0x10 mov ax, 0x2401 int 0x15 ; enable a20 xor eax, eax mov ax, cs shl eax, 4 mov [gdt+0x08+2], ax shr eax, 16 mov [gdt+0x08+4], al ; set base of code desc xor edx, edx mov dx, cs shl edx, 4 add edx, stacktop ; stacktop to be used in p-mode xor eax, eax mov ax, cs shl eax, 4 add eax, gdt mov [gdtreg+2], eax ; set base of gdt lgdt [gdtreg] ; load gdtr mov eax, cr0 or eax, 1 cli ; disable interrupts mov cr0, eax ; enable protected mode jmp 0x08:pstart ; load cs ;;;;; 32bit protected mode ;;;;; [bits 32] pstart: mov ax, 0x10 ; load all seg regs to 0x10 mov ds, ax ; flat memory model mov es, ax mov fs, ax mov gs, ax mov ss, ax mov esp, edx ; load saved esp on stack l1: xor eax, eax mov edi, esi mov ecx, 1024*768*2/4 ; divide by 4 as dwords cld rep stosd mov eax, 0x07FF07FF mov ecx, 32 ; no of bands mov edi, esi l2: push ecx mov ecx, 768*16 ; band width = 32 lines cld rep stosd mov ecx, 0x000FFFFF ; small wait loop $ pop ecx sub eax, 0x00410041 loop l2 mov ecx, 0x0FFFFFFF ; long wait loop $ jmp l1 |

Interrupt Handling

Handling interrupts in protected mode is also different. Instead of the IVT at physical address 0 there is the IDT (interrupt descriptor table) located at physical address stored in IDTR, a special purpose register. The IDTR is also a 48bit register similar in structure to the GDTR and loaded with another special instruction LGDT. The format of the interrupt descriptor is as shown below.

The P and DPL have the same meaning as in data and code descriptors. The S bit tells that this is a system descriptor while the 1110 following it tells that it is a 386 interrupt gate. Our example hooks the keyboard and timer interrupts and displays certain things on the screen to show that they are working.

|  | Example 15.4 |
| --- | --- |
| 001 002 003 004 005 006 007 008 009 010 011 012 013 014 015 016 017 018 019 020 021 022 023 024 025 026 027 028 029 030 031 032 033 034 035 036 037 038 039 040 041 042 043 044 045 046 047 048 049 050 051 052 053 054 055 056 057 058 059 060 061 062 063 064 065 066 067 068 069 070 071 072 073 074 075 076 077 078 079 080 081 082 083 084 085 086 087 088 089 090 091 092 093 094 095 096 097 098 099 100 101 102 103 104 105 106 107 108 109 110 111 112 113 114 | [org 0x0100] jmp start gdt: dd 0x00000000, 0x00000000 ; null descriptor dd 0x0000FFFF, 0x00CF9A00 ; 32bit code dd 0x0000FFFF, 0x00CF9200 ; data gdtreg: dw 0x17 ; 16bit limit dd 0 ; 32bit base idt: times 8 dw unhandled, 0x0008, 0x8e00, 0x0000 dw timer, 0x0008, 0x8e00, 0x0000 \---/ \----/ ¦¦\/ \----/ ¦ ¦ ¦¦ ¦ +----- offset bits 16..32 ¦ ¦ ¦¦ +----- reserved ¦ ¦ ¦+------ Type=E 386 Interrupt Gate ¦ ¦ +--- P=1 DPL=00 S=0 ¦ +------- selector +-------- offset bits 0..15 dw keyboard, 0x0008, 0x8e00, 0x0000 times 246 dw unhandled, 0x0008, 0x8e00, 0x0000 idtreg: dw 0x07FF dd 0 stack: times 256 dd 0 ; 1K stack stacktop: start: mov ax, 0x2401 int 0x15 ; enable a20 xor eax, eax mov ax, cs shl eax, 4 mov [gdt+0x08+2], ax shr eax, 16 mov [gdt+0x08+4], al ; set base of code desc xor edx, edx mov dx, cs shl edx, 4 add edx, stacktop ; stacktop to be used in p-mode xor eax, eax mov ax, cs shl eax, 4 add eax, gdt mov [gdtreg+2], eax ; set base of gdt lgdt [gdtreg] ; load gdtr xor eax, eax mov ax, cs shl eax, 4 add eax, idt mov [idtreg+2], eax ; set base of idt cli ; disable interrupts lidt [idtreg] ; load idtr mov eax, cr0 or eax, 1 mov cr0, eax ; enable protected mode jmp 0x08:pstart ; load cs ;;;;; 32bit protected mode ;;;;; [bits 32] unhandled: iret timer: push eax inc byte [0x000b8000] mov al, 0x20 out 0x20, al pop eax iret keyboard: push eax in al, 0x60 mov ah, al and al, 0x0F shr ah, 4 add ax, 0x3030 cmp al, 0x39 jbe skip1 add al, 7 skip1: cmp ah, 0x39 jbe skip2 add ah, 7 skip2: mov [0x000b809C], ah mov [0x000b809E], al skipkb: mov al, 0x20 out 0x20, al pop eax iret pstart: mov ax, 0x10 ; load all seg regs to 0x10 mov ds, ax ; flat memory model mov es, ax mov fs, ax mov gs, ax mov ss, ax mov esp, edx ; load saved esp on stack mov al, 0xFC out 0x21, al ; no unexpected int comes sti ; interrupts are okay now jmp $ |

Exercises

- Write very brief and to-the-point answers.

  - Why loading idtr with a value appropriate for real mode is necessary while gdtr is not?

  - What should we do in protected mode so that when we turn protection off, we are in unreal mode?

  - If the line jmp code:next is replaced with call code:somefun, the prefetch queue is still emptied. What problem will occur when somefun will return?

  - How much is ESP decremented when an interrupt arrives. This depends on weather we are in 16-bit mode or 32-bit. Does it depend on any other thing as well? If yes, what?

  - Give two instructions that change the TR register.

- Name the following descriptors like code descriptor, data descriptor, interrupt gate etc.

gdt: 	dd 0x00000000, 0x00000000
dd 0x00000000, 0x00000000
dd 0x80000fA0, 0x0000820b
dd 0x0000ffff, 0x00409a00
dd 0x80000000, 0x0001d20b

- Using the above GDT, which of the following values, when moved into DS will cause an exception and why.

0x00
0x08
0x10
0x18
0x28
0x23

- Using the above GDT, if DS contains 0x20, which of the following offsets will cause an exception on read access?

0x0ffff
0x10000
0x10001

- The following function is written in 32-bit code for a 16-bit stack. Against every instruction, write the prefixes generated before that instruction. Prefixes can be address size, operand size, repeat, or segment override. Then rewrite the code such that no prefixes are generated considering that this is assembled and executed in 32-bit mode. Don’t care for retaining register values. The function copies specified number of DWORDs between two segments.

[bits 32]
memcpy:       mov  bp, sp             
              lds  esi, [bp+4]        ; source address
              les  edi, [bp+10]       ; destination address
              mov  cx, [bp+16]        ; count of DWORDs to move
              shl  cx, 1              ; make into count of WORDs
L1:           mov  dx, [si]
              mov  [es:di], dx
              dec  cx
              jnz  L1
              ret

- Rewrite the following scheduler so that it schedules processes stored in readyQ, where enque and deque functions are redefined and readyQ contains TSS selectors of processes to be multitasked. Remember you can’t use a register as a segment in a jump (eg jmp ax:0) but you can jump to an indirect address (eg jmp far [eax]) where eax points to a six-byte address. Declare any variables you need.

mov al, 0x20
scheduler:    jmp USERONESEL:0
              out  0x20, al
              mov  byte [USERONEDESC+5], 0x89
              jmp  USERTWOSEL:0
              out  0x20, al
              mov  byte [USERTWODESC+5], 0x89
              jmp  scheduler

- Protected mode has specialized mechanism for multitasking using task state segments but the method used in real mode i.e. saving all registers in a PCB, selecting the next PCB and loading all registers from there is still applicable. Multitask two tasks in protected mode multitasking without TSS. Assume that all processes are at level zero so no protection issues arise. Be careful to save the complete state of the process.

- Write the following descriptors.

  - 32 bit, conforming, execute-only code segment at level 2, with base at 6MB and a size of 4MB.

  - 16 bit, non-conforming, readable code segment at level 0, with base at 1MB and a size of 10 bytes.

  - Read only data segment at level 3, with base at 0 and size of 1MB.

  - Interrupt Gate with selector 180h and offset 11223344h.

- Write physical addresses for the following accesses where CS points to the first descriptor above, DS to the second, ES to the third, EBX contains 00010000h, and ESI contains 00020000h

  - [bx+si]

  - [ebx+esi-2ffffh]

  - [es:ebx-10h]

- Which of the following will cause exceptions and why. The registers have the same values as the last question.

  - mov eax, [cs:10000h]

  - mov [es:esi:100h], ebx

  - mov ax, [es:ebx]

- Give short answers.

  - How can a GPF (General protection fault) occur while running the following code

push es
pop  es

  - How can a GPF occur during the following instruction? Give any two reasons.

jmp  10h:100h

  - What will happen if we call interrupt 80h after loading out IDT and before switching to protected mode?

  - What will happen if we call interrupt 80h after switching into protected mode but before making a far jump?

- Write the following descriptors. Assume values for attributes not specifically mentioned.

  - Write able 32-bit data segment with 1 GB base and 1 GB limit and a privilege level of 2.

  - Readable 16-bit code descriptor with 1 MB base and 1 MB limit and a privilege level of 1.

  - Interrupt gate given that the handler is at 48h:12345678h and a privilege level of 0.

- Describe the following descriptors. Give their type and the value of all their fields.

dd 01234567h, 789abcdeh
dd 30405060h, 70809010h
dd 00aabb00h, 00ffee00h

- Make an EXE file, switch into protected mode, rotate an asterisk on the border of the screen, and return to real mode when the border is traversed.