## Slide 1: Number Systems and Data Representation.

## Slide 2: Number System
A number system is defined as a system of writing for expressing numbers. It is the mathematical notation for representing numbers of a given set by using digits or other symbols in a consistent manner.

## Slide 3: Positional Number
A number is represented by a string of a digits where each digit position has an associated weight.
The weight is based on the radix of the number System.

## Slide 4: Non-Positional Number
Non-positional number system is used for personal accounting method. In non-weighted number system, there is a huge symbol to represent any number. In non-positional number system, each symbol represents the same value regardless of its position. e.g. Roman style as I, II, III, IV etc.

## Slide 5: Common Number Systems
System | Base | Symbols | Used by humans? | Used in computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No

## Slide 6: Quantities/Counting (1 of 3)
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7
p. 33

## Slide 7: Quantities/Counting (2 of 3)
Decimal | Binary | Octal | Hexa- decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 8: Quantities/Counting (3 of 3)
Decimal | Binary | Octal | Hexa- decimal
16 | 10000 | 20 | 10
17 | 10001 | 21 | 11
18 | 10010 | 22 | 12
19 | 10011 | 23 | 13
20 | 10100 | 24 | 14
21 | 10101 | 25 | 15
22 | 10110 | 26 | 16
23 | 10111 | 27 | 17

## Slide 9: Conversion Among Bases
The possibilities:
Hexadecimal
Decimal
Octal
Binary

## Slide 10: Example
2510 = 110012 = 318 = 1916
Base

## Slide 11: Decimal to Decimal
Hexadecimal
Decimal
Octal
Binary
Next slide…

## Slide 12: Weight
12510 | => | 5 | x | 100 | = | 5
 |  | 2 | x | 101 | = | 20
1 |  |  | x | 102 | = 100 | 
 |  |  |  |  | 125 | 
Base

## Slide 13: Binary to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 14: Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 15: Example
20
21
22
23
24
25
= | 1
= | 2
= | 0
= | 8
= | 0
= | 32
 | 4310
Bit “0” |  |  | 
1010112 | => | 1 | x
 |  | 1 | x
 |  | 0 | x
 |  | 1 | x
 |  | 0 | x
 |  | 1 | x

## Slide 16: Octal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 17: Octal to Decimal
Technique
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 18: Example
7248 | => | 4 | x
 |  | 2 | x
 |  | 7 | x
80
81
82
= 4
= 16
= 448
46810

## Slide 19: Hexadecimal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 20: Hexadecimal to Decimal
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 21: Example
ABC16 | => | C | x | 160 | = | 12 | x | 1 | = | 12
 |  | B | x | 161 | = | 11 | x | 16 | = | 176
 |  | A | x | 162 | = | 10 | x | 256 | = | 2560
274810

## Slide 22: Decimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 23: Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1
  Etc.

## Slide 24: Example
12510 = ?2
2 125
2 62 1
2 31 0
2 15 1
2 7 1
2 3 1
2 1 1
0 1
12510 = 11111012

## Slide 25: Octal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 26: Octal to Binary
Technique
– Convert each octal digit to a 3-bit equivalent binary representation

## Slide 27: Example
7058 = ?2
7 0 5
111 000 101
7058 = 1110001012

## Slide 28: Hexadecimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 29: Hexadecimal to Binary
Technique
– Convert each hexadecimal digit to a 4-bit equivalent binary representation

## Slide 30: Example
10AF16 = ?2
1
0
A
F
0001 0000 1010 1111
10AF16 = 00010000101011112

## Slide 31: Decimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 32: Decimal to Octal
Technique
  Divide by 8
  Keep track of the remainder

## Slide 33: Example
123410 = ?8
8 1234
8 154 2
8 19 2
8 2 3
0 2
123410 = 23228

## Slide 34: Decimal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 35: Decimal to Hexadecimal
Technique
  Divide by 16
  Keep track of the remainder

## Slide 36: Example
123410 = ?16
123410 = 4D216
 | 16 | 1234 |  |  | 
 | 16 | 77 | 2 |  | 
 | 16 | 4 | 13 | = | D
 |  | 0 | 4 |  | 

## Slide 37: Binary to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 38: Binary to Octal
Technique
  Group bits in threes, starting on right
  Convert to octal digits

## Slide 39: Example
10110101112 | = | ?8 |  |  | 
 |  | 1 | 011 | 010 | 111
 |  | 1 | 3 | 2 | 7
10110101112 = 13278

## Slide 40: Binary to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 41: Binary to Hexadecimal
Technique
  Group bits in fours, starting on right
  Convert to hexadecimal digits

## Slide 42: Example
10101110112 = ?16
10 1011 1011
2
B
B
10101110112 = 2BB16

## Slide 43: Octal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 44: Octal to Hexadecimal
Technique
– Use binary as an intermediary

## Slide 45: Example
10768 = ?16
1
0
7
6
001 000 111 110
2
3
E
10768 = 23E16

## Slide 46: Hexadecimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 47: Hexadecimal to Octal
Technique
– Use binary as an intermediary

## Slide 48: Example
1F0C16 = ?8
1
F
0
C
0001 1111 0000 1100
1 7 4
1
4
1F0C16 = 174148

## Slide 49: Exercise – Convert ...
Don’t use a calculator!
Decimal | Binary | Octal | Hexa- decimal
33 |  |  | 
 | 1110101 |  | 
 |  | 703 | 
 |  |  | 1AF
Skip answer
Answer

## Slide 50: Exercise – Convert …
Decimal | Binary | Octal | Hexa- decimal
33 | 100001 | 41 | 21
117 | 1110101 | 165 | 75
451 | 111000011 | 703 | 1C3
431 | 110101111 | 657 | 1AF
Answer

## Slide 51: Binary Addition
Two 1-bit values
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 10
“two”

## Slide 52: Binary Addition
Two n-bit values
  Add individual bits
  Propagate carries
– E.g.,
101110
21
+ 11001 + 25
46
1
10101
1

## Slide 53: Multiplication
Binary, two 1-bit values
A | B | A B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 54: Multiplication
Binary, two n-bit values
– As with decimal values
– E.g.,
1110
x 1011
1110
1110
0000
1110
10011010

## Slide 55: Binary Subtraction
https://www.youtube.com/watch?v=PQ7cU31968c

## Slide 56
Thank you