## Slide 1: SEVEN LAYER MODEL(OSI MODEL)

## Slide 2: INTRODUCTION
4
International standard organization (ISO) established a committee in 1977 to develop an architecture for systems communication.
Open System Interconnection (OSI) reference model is the result of this effort.
This model allows any two different systems to communicate
Regardless of their underlying architecture.

## Slide 3: CONT..
5
The OSI model describes how data flows from one computer, through a network to another computer.
The OSI model is not a protocol; it is a model for understanding and designing a network architecture that is flexible and robust.
The OSI model consists of seven separate but related layers, each of which defines a part of the process of moving information across a network.

## Slide 4: OSI Model's 7 Layers
6
APPLICATION
PRESENTATION
SESSION
TRANSPORT
NETWORK
DATA LINK
PHYSICAL
APPLICATION
PRESENTATION
SESSION
TRANSPORT
NETWORK
DATA LINK
PHYSICAL
MIDDLE LAYER
HIGHER LAYER
Application to Application
Application to Application
Application to Application
Process to Process
LOWER LAYER
Hop to Hop
Switch
Hop to Hop
Physical Medium
Hub and Repeater
Router
Source to Destination
Source to Destination

## Slide 5: HOST AND MEDIA LAYER
7

## Slide 6: PHYSICAL LAYER
One of the major function of the physical layer is to move data in the form of electromagnetic signals across a transmission medium.
Its responsible for movements of individual bits from one hop (Node) to next.
Both data and the signals can be either analog or digital.
Transmission media work by conducting energy along a physical path which can be wired or wireless
Concerned:
Physical characteristics of interface and medium (Transmission medium)
Representation of bits (stream of bits (0s or 1s) with no interpretation and encoded into signals)
Data rate (duration of a bit, which is how long it last)
Synchronization of bits (sender and receivers clock must be synchronized)
Line configuration (Point-to-Point, Point-to-Multipoint)
Physical topology
Transmission mode (Simplex, half duplex, full duplex)
8
110 | 10101000000010111
110 | 10101000000010111
From data link layer To data link layer
Physical layer
Physical layer
Transmission medium

## Slide 7: DATA LINK LAYER (HOST TO HOST)
Data link layer is responsible for moving frames from one hop (Node) to the next.
Concerned:
Framing (stream of bits into manageable data units)
Physical addressing (MAC Address)
Flow Control (mechanism for overwhelming the receiver)
Error Control (trailer, retransmission)
Access Control (defining master device in the same link)
Data
H2
T2
From network layer
Data
H2
T2
To network layer
To physical layer
From physical layer
Data link layer
Data link layer

## Slide 8: NETWORK LAYER (SOURCE TO DESTINATION)
Data
H3
Packet
From transport layer
Data
H3
Packet
To transport layer
To data link layer From data link layer
The network layer is responsible for the delivery of individual packets from the source host to the destination host.
Concerned:
  Logical addressing (IP Address)
  Routing (Source to destination transmission between networks)
Network layer
Network layer

## Slide 9: TRANSPORT LAYER (PROCESS TO PROCESS)
The transport layer is responsible for the delivery of a message from one process to another
Concerned:
Service-point addressing (Port address)
Segmentation and reassembly (Sequence number)
Connection control (Connectionless or connection oriented)
Flow control (end to end)
Error Control (Process to Process)
11
Segments
From session layer
To network layer
Transport layer
H4 | Data |  | H4 | Data
H4 | Data
Segments
H4 | Data
From session layer
From network layer
Transport layer
H4 | Data
H4 | Data

## Slide 10: SESSION LAYER (DIALOG INITIATION)
The session layer is responsible for dialog control and synchronization
Concerned:
Dialog Control (Half Duplex/Full duplex)
Synchronization (Synchronization points, process inline within same page)
Data
H5
From Presentation layer
To transport layer
Data
Data
Syn
Syn
Syn
Data
H5
To Presentation layer
From transport layer
Data
Data
Syn
Syn
Syn
Session layer
Session layer

## Slide 11: PRESENTATION LAYER (DEPENDENCY)
The presentation layer is responsible for translation, compression and encryption
Concerned:
Translation (interoperability between different encoding system)
Encryption (Privacy schemes)
Compression (data compression)
Data
H6
From application layer
To session layer
Data
H6
To application layer
From session layer
presentation layer
presentation layer

## Slide 12
The application layer is responsible for providing services to the user.
Concerned:
Network virtual terminal (Software)
File transfer, access and management
Mail services
Data
H7
USER
(Human or Program)
To presentation layer
Data
H7
Application layer
Application layer
Message
Message
X.500
FTAM
X.400
X.500
FTAM
X.400
From presentation layer
USER
(Human or Program)
Application Layer

## Slide 13: THE END