## Slide 1: Feedback
Instructor: Engr. Hira Akash

## Slide 2: Feedback
Positive and Negative feedback
Principle of feedback amplifier
Stabilization of gain by negative feedback
Bandwidth improvement with negative feedback
Reduction of nonlinear distortion

## Slide 3: Feedback
In the feedback process a part of output is sampled and fed back to the input. The fed back signal can be in phase with or out of phase with the original input signal.
Definition of feedback:
Feedback is defined as the process in which a part of output signal (voltage or current) is returned back to the input.
The amplifier that operates on the principle of feedback is known as feedback amplifier.

## Slide 4
Positive feedback
Negative feedback.
If the original input signal and the feedback signal are in phase, the feedback is called as positive feedback.
However if these two signals are out of phase then the feedback is called as negative feedback.

## Slide 5: Characteristics of basic amplifiers
Important characteristics of an amplifier are its :
Voltage gain.
Input impedance.
Output impedance.
Band width.

## Slide 6: Need for feed back
The parameters of a basic amplifier are required to changed as per the need.
These changes can be brought out efficiently by introducing feed back in the amplifier.

## Slide 7: negative feed back
When the feed back signal decreases the net input signal i.e., the feedback signal is 180 out of phase with respect to input signal, it is called negative or Degenerative feed back.

## Slide 8: positive feed back
When the feed back signal increases the net input signal i.e., the feedback signal is in phase with the input signal, it is called Positive or Regenerative feed back.

## Slide 9: Advantages of Negative Feed back
Improves stability in gain.
Reduces distortion.
Reduces the noise level at the output

## Slide 10: Disadvantages of negative feed back
Decreases the gain.
Decreases the distortion.
Decreases the noise.
Due to these features: it is used in amplifiers

## Slide 11: Disadvantages of positive feed back
Increases the distortion.
Increases the noise.
Poor stability.
Due to these features:
  it is seldom used in amplifiers.
  it is used in oscillators.

## Slide 12: Comparison of positive and negative feed bac

## Slide 13: Principle of feed back.

## Slide 14
Feed back amplifier is one in which a part of the output of an amplifier is fed back to the input.
It consists of
basic amplifier with a gain A.
feed back network.
sampling network.
mixing network

## Slide 15: Stabilization of gain by negative feedback
The effect of negative (or degenerative) feedback is to “reduce” the gain. For example, if someone criticises you or gives you negative feedback about something, you feel unhappy about yourself and therefore lack energy, you feel less positive.
Because negative feedback produces stable circuit responses, improves stability and increases the operating bandwidth of a given system, the majority of all control and feedback systems is degenerative reducing the effects of the gain.
An example of a negative feedback system is an electronic amplifier based on an operational amplifier as shown.

## Slide 16: CONT

## Slide 17: CONT
Negative feedback control of the amplifier is achieved by applying a small part of the output voltage signal at Vout back to the inverting ( – ) input terminal via the feedback resistor, Rf.
If the input voltage Vin is positive, the op-amp amplifies this positive signal, but because its connected to the inverting input of the amplifier, and the output becomes more negative. Some of this output voltage is returned back to the input by the feedback network of Rf.

## Slide 18: Bandwidth improvement with negative feedback
Feedback reduces the overall gain of a system with the degree of reduction being related to the systems open-loop gain. Negative feedback also has effects of reducing distortion, noise, sensitivity to external changes as well as improving system bandwidth and input and output impedances.
The op amp gain bandwidth product is constant for voltage-feedback amplifiers. However it is not applicable for current feedback amplifiers because relationship between gain and bandwidth is not linear. Therefore decreasing the gain by a factor of ten will increase the bandwidth by the same factor.

## Slide 19: reduction of nonlinear distortion by negative feedback
Negative feedback applied to an amplifier linearizes the transfer characteristic of the amplifier and reduces the distortion of the input signal that is generated by the nonlinearity. The gain of the amplifier at an operating point is also reduced accordingly.