## Slide 1: Soil and Environment EC/Env-203
BS SEMESTER 6
SESSION 2017-21
Course Tutor: Dr Moneeza Abbas

## Slide 2: Impact of Agrochemicals on soil

## Slide 3
INTODUCTION
Agrochemicals are the generic name given to chemicals (fertilizers, pesticides, insecticides, etc.) use in agricultural to facilitate plant growth and protection. In short, they are agricultural chemicals.
Although initially used to improve crop production, overuse of chemicals has now started affecting the environment. Apart from the obvious effects on crops and the food chain, agrochemicals have a wide area of application. Due to these many uses, they seep into the surrounding land and water bodies, therefore having a widespread effect.
.

## Slide 4: Cont.
Regarding their impact on crops, excessive use of such chemicals generates a significant amount of residues. These residues cause nutrient imbalance and quality reduction of agricultural produce. The residues lead to long-term ill effects on the health of organisms that consume them. For example, pesticide residues in food have been linked to being one of the causes of asthma in humans.

## Slide 5: Cont..
In many developing nations, current agricultural methods follow unsustainable practices which have resulted in a huge amount of toxic effluents being emitted directly or indirectly into the soil, air, and water .
Currently, various agrochemicals (i.e., herbicides, fungicides, insecticides, nematicides, molluscicides, rodenticides, chemical fertilizers are being used non-judiciously which have adversely affected beneficial soil (micro) biota.

## Slide 6: Cont..
Impacts of Herbicides on Soil Biota
Herbicides show a reduction in the total microbial population within 7 to 30 days after application depending on the type of herbicidal molecules and adversely affect the microbial biodiversity indirectly by altering the physiology or biosynthetic mechanisms.
The detrimental effects of applied chemical herbicides on soil microbial diversity depend on the degradability, adsorption and desorption, bioavailability, bioactivity, persistence, concentration, and toxicity of agrochemicals along with soil factors such as texture, vegetation, tillage system, and organic matter.
The soil type can also play a critical role in the herbicidal effect. The effect can be more severe in coarse-textured soils

## Slide 7: Cont..
Fungicides and Soil Microbial Environment
Several studies have reported the harmful effects on soil microbial growth, survival, and activity . Fungicide has an inhibitory effect on several soil microbial populations, but the impact is non-significant
Several biochemical processes in soil are closely linked with enzymatic activities which are adversely affected by residues and toxic elements left after application of fungicides

## Slide 8: Insecticides and Soil Microbial Environment
The applied insecticides affect the growth, survival, and working capacity of symbiotic rhizobial association with roots of legume plants resulting in dwindled atmospheric N-fixation. The antagonistic interaction between the applied insecticides and symbiotic N-fixers differ with the specific chemical group of insecticide and the specific N-fixer group.

## Slide 9: Conclusions
The mandate for agriculture development is to feed and provide adequate nutrition and surplus to the mounting human population without compromising on ecology and environment of the biosphere. Pesticides and their use are considered as magic bullets in developing nations. Pesticides cause serious hazards to soil environment and human health because a lot of pesticides and their derivatives remain in the soil system for a considerable period. Most pesticides negatively affect the biological functionaries of microbes, their diversity, composition, and biochemical processes. Pesticides cause imbalance of soil fertility which directly affects crop yield.

## Slide 10
Thank you