## Slide 1: Techniques for Data Capturing

## Slide 2: Digitizing
The technique of converting the traditional paper map or other hard copy graphics into computer compatible digital data is termed digitizing.

## Slide 3: Classification of Digitizing Techniques
Tablet or Manual Digitizing
Maps are encoded and entered by hand
On-screen or Heads Up Digitizing

## Slide 4: Manual Digitization
Digitization process is similar to drawing maps manually . Here the pencil / staddler is replaced by the cursor.
Cursor is used to traced feature visible on source map.
This process involves mechanical device as cursor thus it is called semi automated digitization.
Scanning is known as fully automated system

## Slide 5: On Screen Digitization
Computer Digitization
Scanning

## Slide 6: Scanner
A scanner is a piece of hardware for converting an analogue source document into digital raster format.
 A digital scanner illuminates a to-be-scanned document and measures with a sensor the intensity of the reflected light.
The result of the scanning process is an image as a matrix of pixels, each of which holds a reflectance value.(Gray Scale – 256 gray tones from 0 to 256 for black and white image and red, green blue for color image.

## Slide 7: Types of Scanners
Electromechanical or Drum Scanner.
Flat Bed / CCD / Roll Feed Type Scanner.

## Slide 8: Electromechanical or Drum Scanner
Document to be scanned is attached to a revolving drum and passes under the fixed sensor array at a constant speed. This array is in close proximity to the document and both are enclosed in a container together with a light source.

## Slide 9: Electromechanical or Drum Scanner
A type of scanner used to capture the highest resolution from an image. Photographs and transparencies are taped, clamped or fitted into a clear cylinder (drum
A scanner head containing a light source and photo detector reads the reflectivity of the target graphics.

## Slide 10: Electromechanical or Drum Scanner
A light source that focuses on one pixel is beamed onto the drum and moves down the drum a line at a time.

## Slide 11: Flatbed / CCD / Roll feed Type Scanner
A scanner that provides a flat, glass surface to hold pages of paper, books and other objects for scanning. The usual configuration is that a light source and sensor traverse the document automatically in a series of parallel lines measuring the reflected light by Charged Couple Device (CCD) and thereby resolving the document into matrix of pixels.

## Slide 12: Modes of Scanning
Color
Monochromatic

## Slide 13: Monochromatic Scanning
During monochromatic scanning only the grey level is registered for every pixel. Usually grey scale values range from 0 black to 256 white

## Slide 14: Color Scanning
A color scanner scans each document three times, every time using a filter for one of the three basic colors components (RGB) and recording all three of them simultaneously.
Each of the three scales allows 256 different values.
The final color recognition occurs by interpreting the intensities of the three component colors simultaneously.